## Slide 1: Building great networked media devices for Play To apps
Edwin Heredia & Zane Salim
Program Managers
Microsoft Corporation
HW-177T

## Slide 2: Agenda
Play To experiences from Metro style apps
How Play To works in Windows 8
Certifying your Play To device
You’ll leave with an understanding of
How to make your devices work with Play To

## Slide 3: Play To makes it easy for customers to enjoy media from the web and apps on devices

## Slide 4: Play To from the web and Metro style apps
demo

## Slide 5: Play To from Metro style apps
Setup-free and easy to discover
Built into HTML5 media tags in IE10
Working music, video, and photo apps
Simple to support in Metro style apps

## Slide 6
How Play To works
in Windows 8

## Slide 7: Play To user experience
Play To Controller
Play To Receiver

## Slide 8: Connection Protocols
Connection Protocols
Ethernet, Wi-Fi, Wi-Fi Direct, IP, TCP, UDP
Discovery & Description
UPnP Device Architecture v1.0
Control Protocols
UPnP AV MediaRenderer v1
HTTP Streaming
HTTP 1.1, DLNA extensions
Media Formats
DLNA MF Guidelines
DLNA Guidelines

## Slide 9: Play To receiver architecture
Wired/Wireless/Wi-Fi Direct
TCP/IP, UDP/IP & HTTP
Media
Steaming
Client
Decoders
Connection
Manager
AV Transport
Rendering Control
UPnP AV Media Renderer V1

## Slide 10: Play To Session
2. User selects content
3. User invokes Play To
4. Controller sends the content URI (Play)
1. List of supported formats/profiles
5. HTTP Request
7. Pause, Stop, Seek
6. Content stream
TV plays content progressively

## Slide 11: Enabling Play To in apps
<body>
<video id=“videoplayer” src=“http://www.contoso.com/clip.mp4” controls autoplay />
<script type=“text/javascript”>
// Step 1: Obtain PlayToManager object for the application’s current view
var ptm = Windows.Media.PlayTo.PlayToManager.getForCurrentView();
// Step 2: Register for the sourcerequested event so a media source can be specified
ptm.addEventListener(“sourcerequested”, function(e) {
// Step 3: Specify the mediaElement to stream.
// The user chooses a target device in the UI.
var request = e.sourceRequest;
var deferral = request.getDeferral();
request.setSource(document.getElementById(“videoplayer”).msPlayToSource);
deferral.complete();
});
</script>
</body>

## Slide 12
Certifying your Play To device

## Slide 13: Quality Media Experiences
Usability and Performance
Consistent and reliable experience
Optimized for common formats
High-quality media rendering
Delivers complete experiences
Windows only shows certified Play To devices in the Devices charm
Windows Device Certification
Protocol Compliance Requirements (DLNA)
Product Quality and User Experience Requirements
+
=

## Slide 14: Usability, performance, and quality
A certified Play To receiver
  Is always available and very responsive
  Has low latency when a user plays audio, video or pictures
  Selects the content variant that offers the best quality
  Supports natively H.264 video with AAC-LC audio in MP4 containers

## Slide 15: Consistent, reliable, and complete
A certified Play To receiver
  Complies with standardized protocols (DLNA)
  Implements good error handling
  Supports rich user libraries
  Implements all the transport controls
  Saves energy (stand-by mode) but also Wake-on-LAN
  Supports Play To over Wi-Fi Direct

## Slide 16: Certifying your Play To device
Creates a consistent and reliable experience for customers
Ensures that your device works well with Metro style apps
Enables you to create a Metro style device app that is automatically installed with the device

## Slide 17: Developer Preview receivers and apps
Receivers
  Western Digital TV Live Hub
  Windows 7 certified Onkyo AV Receivers
  Windows 7 and Windows 8 PCs running Windows Media Player
Metro style apps
  Internet Explorer
  Conference app
  Notespace

## Slide 18
Recap

## Slide 19: Play To in Windows 8
Makes it easy for customers to enjoy media from the web and apps on your devices
Delivers a setup-free, and easy to discover experience
Works with HTML5 websites using IE10 and Metro style apps

## Slide 20: Call to action
Partner with us to deliver compelling Play To device experiences with Windows 8
Design and build devices that work well with media from the web and Metro style apps
Get your Play To devices certified for Windows 8

## Slide 21: Related sessions
[HW-745T] Reimagining the experience for connecting with devices
[PLAT-775T] Your Metro style app, video and audio, Part 1
[HW-329T] Understanding Wi-Fi Direct in Windows 8
[APP-788T] Integrating stunning media experiences in XAML
[APP-408T] Integrating with the Windows device experience
[HW-275T] Building and delivering a great Metro style app for your device
[HW-286T] Simplifying wireless and network device discovery and pairing
[HW-260T] Windows Certification: improvements to the logo program

## Slide 22: Further reading and documentation
Whitepapers:
  Design Guidelines for Play To Receivers
  Play To & Media Sharing for Metro Style Apps
Developer Center:
  Streaming media to devices using PlayTo
  Quickstart: Using PlayTo in applications
  Windows.Media.PlayTo namespace
  Windows Application Contracts
  Windows Dev Center home

## Slide 23
Feedback and questions http://forums.dev.windows.com
Session feedback http://bldw.in/SessionFeedback
thank you

## Slide 24
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.