## Slide 1: Designing systems and developing drivers for NFC
Max Morris
Principal Program Manager
Priya Dandawate
Program Manager
Microsoft Corporation
HW-269T

## Slide 2: Agenda
Proximity user model & scenarios
Programming model
Proximity stack & driver development
Design considerations
You’ll leave with examples of how to
Create a system that integrates your proximity solution

## Slide 3: A proximity solution integrated into Windows helps deliver a new class of experiences to users

## Slide 4: Open a website, share a website
demo

## Slide 5: Launch an app, DJ with a friend
demo

## Slide 6: It’s about connecting people together, not just connecting devices

## Slide 7: What users think about proximity….
video

## Slide 8
video

## Slide 9: Tapping devices together is a digital handshake

## Slide 10: Cute kissing, or hi-fiving?
video

## Slide 11
video

## Slide 12: Proximity user model
Tap and go is a gesture…
… that’s a natural interaction
… between people
… in close proximity to each other
… through devices they are holding
… to do something together.

## Slide 13
Programming model

## Slide 14: Tap and go experiences
Send & receive simple messages
Connect an app with the same app on another device
Leverage the Share contract to send files
Setting up a device

## Slide 15: Tap and go experiences have a common pattern
Windows provides a simple programming construct for this pattern so apps can focus on the experience

## Slide 16: Tap and go as a programming construct
Tap and go is about anticipating user intent & triggering actions
The common tap and go pattern
  User sets the context
  User taps to another device
  User’s expected action is triggered
Tap and go is not about talking machine language to a radio

## Slide 17
Proximity stack
& driver development

## Slide 18: Windows and a proximity solution work together to deliver simplicity & predictability

## Slide 19: NFC is the leading proximity technology
NFC provides a compatibility baseline to enable the tap and go scenarios

## Slide 20: Windows proximity architecture
Proximity API
Proximity Service
App
Proximity
Pairing Experience
Installed
App
List
Firewall
Service
App
App
Proximity Sharing Experience
Networking drivers
Proximity driver
Proximity device
Networking devices
App

## Slide 21: Device driver model
  GUID_DEVINTERFACE_NFP
New device interface class with nine new IOCTLs defined
Models the tap and go gesture at the device level
The driver implements a state machine for handling pub/sub

## Slide 22: Device driver model
Developers classify messages into namespaces for routing
Each publication and subscription is a unique open handle
  So, messages in the driver are a collection of reads and writes
  The driver pends the collection until a match is made during a tap
Upon being triggered by tap and go, the driver
  Sends active publications, notifying publishers of transmission
  Receives messages & maps to subscriptions, notifying subscribers

## Slide 23: How Windows 8 uses the proximity driver
Windows is active with an installed & enabled driver
  Subscriptions for arrival & departure of another device
  Subscriptions to pair devices over a wireless transport
  Subscriptions & publications for peer-to-peer sessions
  Subscriptions for URIs and MIME content
Sleep or lock screen
  Service sends the IOCTL to disable each publication & subscription
  On resume, service sends the IOCTL to enable

## Slide 24: How proximity drivers use NFC
Drivers implement NFC Forum protocols for interop
Windows messages are packaged in NDEF format
  NDEF = NFC Data Exchange Format
PC-to-PC scenarios use SNEP for multi-message exchange
  SNEP = Simple NDEF Exchange Protocol, runs over LLCP
  LLCP = Logical Link Control Protocol, runs over NFC peer-to-peer
Tag reading & writing scenarios just use NDEF directly

## Slide 25: Subscribing to a message
Polling
App
Proximity device
Proximity
API
Subscribe
Open Handle,
IOCTL_NFP_GET_NEXT_SUBSCRIBED_MESSAGE,
Pends the IOCTL
Begin
Pending
Proximity driver

## Slide 26: Publishing a message
App
Proximity
API
Proximity device
Polling
Publish
Open Handle,
IOCTL_NFP_SET_PAYLOAD,
IOCTL_NFP_GET_NEXT_TRANSMITTED_MESSAGE,
Pends the IOCTL
Begin
Pending
Proximity driver

## Slide 27: Exchanging the message
Polling
App
Proximity device
Proximity
API
App
Proximity
API
Proximity device
Polling
Pending
Proximity driver
Pending
Proximity driver
Tap occurs
SNEP over LLCP
Peer-to-peer NFC
Send message via SNEP

## Slide 28: Receiving the message
Receive message
App
Proximity device
Proximity
API
Message received
Fill pended buffer,
Complete IOCTL_NFP_GET_NEXT_SUBSCRIBED_MESSAGE,
Pend a new IOCTL
Pass message to driver
Pending
Proximity driver
Polling

## Slide 29: Stopping the subscription
App
Proximity device
Proximity
API
Stop subscribing
Cancel IO,
Close the handle
End
Pending
Proximity driver
Polling

## Slide 30: Receiving message send confirmation
App
Proximity
API
Proximity device
Pending
Proximity driver
Message sent
Message sent
Complete IOCTL_NFP_GET_NEXT_TRANSMITTED_MESSAGE,
Pend a new IOCTL
Pass confirmation to driver

## Slide 31: Stopping the publication
App
Proximity
API
Proximity device
Polling
Stop publishing
Cancel IO,
Close the handle
End
Pending
Proximity driver

## Slide 32: How Windows sets up a peer-to-peer session
Peer-to-peer sessions are kick-started using NFC
During the tap
  Windows exchanges peer & connectivity info
  Windows also negotiates a session key
After the tap
  If the app isn’t installed, Windows invites the user to get the app
  If the app isn’t in the foreground, Windows invites the user to switch
  Windows initiates all matching transports & chooses the best socket

## Slide 33
Design considerations

## Slide 34: Device driver engineering considerations
  The UMDF driver model works fine for performance
  Don’t poll in the driver for new messages, poll in the hardware
  Report presence when the peer radio is within field
  Don’t need to flush state on enable/disable
  Minimize battery impact by managing power & radio

## Slide 35: User experience considerations
  Place antenna in upper-right-hand on back of tablet
  Follow touch mark guidelines to help users know where to tap
  Use an antenna >= 3x5cm to support effective range
  A ferrite shield behind the antenna can minimize interference
  Be careful other antennas or a metal back don’t interfere

## Slide 36: System considerations
  Use a simple peripheral bus to minimize power drain
  If you must use USB, support selective suspend to save power
  Stop polling on the hardware when no active pubs or subs

## Slide 37: Certification & test collateral are designed to help you enable the tap and go scenarios

## Slide 38
Recap

## Slide 39: A proximity solution integrated into Windows helps deliver a new class of experiences to users

## Slide 40: With the proximity platform
You can enable a new class of apps using tap and go
You can integrate a proximity solution into your system
You can test your solution and system to certify they work well

## Slide 41: Related sessions
[APP-408T] Integrating with the Windows device experience
[HW-329T] Understanding Wi-Fi Direct in Windows 8
[APP-206T] Bring apps to life with Metro style animations in HTML5
[APP-405T] Share: your app powers the Windows 8 share experience
[PLAT-270T] Connecting and sharing with near field communication
[HW-328T] Using the Windows Driver Framework to build better drivers

## Slide 42: Further reading and documentation
Proximity Devices
Windows Hardware Dev Center
Windows Dev Center
Questions?
  Please visit the forums on the Windows Dev Center at http://forums.dev.windows.com
  For best response, please include the Build Session #269 in the title of your post

## Slide 43
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.