## Slide 1: Designing the building blocks for a Windows Server 8 cloud
Yigal.Edery@microsoft.com
Ross.Ortega@microsoft.com
SAC-430T

## Slide 2: Windows Server 8 is Cloud Optimized
Enable Multi Tenant Clouds
Network Virtualization. Dynamic VM Placement. Secure Isolation. …
High Scale & Low Cost Datacenters
Leverage Hardware. High Availability. SMB2. Low Cost Storage. …
Manageable & Extensible
WMIv2. PowerShell. Extensible Switch. …

## Slide 3: Agenda
Considerations in designing different types of clouds
Networking Topologies
Storage Architectures
Committed Service Levels
Putting it all together: Representative configurations

## Slide 4
SR-IOV
LBFO
RSS
iSCSI
Clusters
QoS
SAS
Spaces
10GbE
DCB
Network Virtualization
VMQ
Building an optimized cloud requires difficult decisions and tradeoffs among an
alphabet soup of technologies
???

## Slide 5
There is no “one size fits” all cloud
Different needs require different cloud architectures

## Slide 6
Use Windows Server 8 features and best practices to design servers and systems optimized for differing cloud requirements

## Slide 7: Requirements Influence Choices
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 8: Workloads Considerations
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 9: Which workloads will run in my cloud?
Cloud aware apps or legacy / stateful apps?
Are workloads trusted?
Compute-bound or Storage-bound?
Workloads size? And how many per server?

## Slide 10: Networking Considerations
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 11: Network Topology
Isolation of hoster and tenant traffic?
Leverage existing infrastructure?
Traffic Management?
[437] A Deep Dive Into Hyper-V Networking
LEARN
MORE

## Slide 12: InfiniBand vs. 10GbE vs. 1GbE
Converged Fabrics (fewer NICs):
  10 Gb Ethernet
    Great performance
    RDMA optional (for SMB2.2 file access)
    Offers Quality of Service (DCB) & Flexible bandwidth allocation
    New offloads
    …But physical switch ports more expensive
  InfiniBand (32 Gb and 56 Gb)
    Very high performance, low latency
    RDMA included (for SMB2.2 file access)
    …But Network management different than Ethernet
1 Gb Ethernet
  Adequate performance for many workloads
InfiniBand
1 GbE
10 GbE

## Slide 13
How many NICs should be in the server?

## Slide 14: Physical Isolation (4 NICs)
Multiple physical NICs
ACLs for guests
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server

## Slide 15: Management and Guest Isolation (2 NICs)
10 GbE NIC for parent partition
ACLs for guests
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server
10 GbE

## Slide 16: Convergence (1 NIC)
ACLs for all switch ports
QoS for Management OS traffic
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server
QoS
10 GbE
[439] QoS and Converged Fabric in the Data Center
LEARN
MORE

## Slide 17: NICs, Scalability and Performance
Windows Server 8 supports many NIC features including
  Data Center Bridging (DCB)
  Receive Segment Coalescing (RSC)
  Receive Side Scaling (RSS)
  Remote Direct Memory Access (RDMA)
  Single Root I/O Virtualization (SR-IOV)
  Virtual Machine Queue (VMQ)
  IPsec offload (IPsecTO)
[433] Network Acceleration and Other NIC Technologies
LEARN
MORE

## Slide 18: Using Network Offloads for Increased Scale
Scalability Offloads take advantage of all CPU cores
  Receive Side Scaling for native path
  Virtual Machine Queue for Hyper-V Switch path
Server
CPU0
CPU1
CPU2
CPU3
CPU7
CPU6
CPU5
CPU4
RSS
VMQ
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server
RSS
VMQ
*RSS and VMQ cannot both
be enabled on the same NIC

## Slide 19: Selecting NIC Offloads *
Flexibility and Scalability
Raw Performance
RDMA
SR-IOV**
Hyper-V Extensible Switch
Hyper-V Network Virtualization
NIC Teaming
RSS**
VMQ
IPsecTO
Performance offloads bypass Windows functionality
*Per NIC constraints
** Work together
*** Offloads require driver and possibly BIOS support

## Slide 20: Storage Considerations
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 21: Host Bus Adapters vs. NICs
HBA bypasses networking stack
Lowers CPU utilization
Filesystem
Port Driver (Storport)
LSO
Networking Stack
RSS
LSO
NDIS miniport
FC/iSCSI /SAS HBA
HBA miniport

## Slide 22: Storage Architectures
When?
Very low cost
Disk-bound VMs
Compute & Storage Scale Together
Compute & Storage Scale Independently
Hyper-V Server
SAS
Hyper-V Server(s)
Compute/Storage
Compute/Storage
SAS / iSCSI / FC
Hyper-V Server(s)
Compute
Storage
File Servers
10 GbE / RDMA
Optional Controller
Hyper-V Server(s)
SAN
Controller
When?
Grow capacity on two axis
Compute-bound VMs
Storage offloading
[446] Designing Systems for CA
[451] Building CA Systems with Hyper-V
LEARN
MORE

## Slide 23: Service Levels
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 24: Service Level Agreements
What performance guarantees will be offered to workloads?
How important is performance isolation?
What are the resiliency promises?

## Slide 25: Resiliency Approach
Cluster (optional)
Cluster
VMs not designed for failures, H/A at server level,
Failover clustering as another layer of protection,
High End Servers, double power and network infrastructure
VMs designed for failures, or downtime acceptable
Lower End Industry Standard Server, single infrastructure
Failover Clustering
Hosters
Private Clouds / Legacy Apps
Application failover
Switch
Switch
Hyper-V /
Parent
VMs
VMs
VMs
Hyper-V /
Parent
VMs
VMs
VMs
Switch
Switch
Hyper-V /
Parent
VMs
VMs
VMs
Hyper-V /
Parent
VMs
VMs
VMs
Switch
Switch

## Slide 26: Requirements Influence Choices
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Service Levels

## Slide 27: Requirements Influence Choices
Scalability
Reliability
Security
Performance
High Availability
Cost

## Slide 28: Representative Configurations
Optimized for different cloud types
Validated at Microsoft’s Engineering Excellence Center (EEC)
Guidance & Script Samples
Windows Server 8 Systems

## Slide 29: “Traditional” Enterprise Configuration w/ FC Storage
Physically isolated networks
HBA for storage access
Windows Server 2008 R2 guidance
SAN
FC
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Server
Storage
HBA
1 GbE
1 GbE
1 GbE
1 GbE

## Slide 30: Enable Support for Demanding Workloads…
10GbE for VM traffic
SR-IOV enables better scale, reduces latency
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Server
Storage
SAN
FC
HBA
1 GbE
1 GbE
1 GbE
10 GbE
SR-IOV
VMQ

## Slide 31: How About 10GbE for Storage Access?
Move to 10GbE fabric
Fast storage access, Ethernet based
SAN
iSCSI
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Server
Storage
1 GbE
1 GbE
1 GbE
1 GbE
10 GbE
RSS

## Slide 32: So you have 10GbE? Converge!
Converge onto 10GbE
Switches must support DCB
QoS policies and DCB traffic classes ensure bandwidth allocations
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server
10 GbE
RSS
DCB
QoS
SAN
iSCSI

## Slide 33: You’ve Converged? Use File Servers!
File Servers in front of storage
RDMA for high speed, low-latency, reduced CPU overhead
Less fibre-channel fabric
Better VM mobility
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
ACLs
Server
10 GbE
RSS
DCB
QoS
Storage
Windows File Server
RDMA
RDMA
SMB2

## Slide 34: High Availability AND Performance with 3 NICs!
RDMA or NIC Teaming?
SR-IOV or NIC Teaming?
Storage
Windows File Server
SMB2
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster / Storage
Manage
Server
NIC Teaming
SR-IOV
10 GbE
10 GbE
10 GbE
10 GbE
RSS
DCB

## Slide 35: Sample Documented Configuration
No network legacy concerns (green field)
Hyper-V clustered
Converged 10GbE with DCB for QoS
File Server clustered with scale-out
SAN
10GBE Switch + DCB support
Windows
File Server
Cluster
Storage
Manage
NIC Teaming
10 GbE
10 GbE
HBA
DCB
RSS
DCB
RSS
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
NIC Teaming
NIC Teaming
10 GbE
10 GbE
1 GbE
1 GbE
VM n
DCB
RSS
DCB
RSS
1GBE Switch
Internet
QoS
QoS

## Slide 36: Windows Server 8 is Cloud Optimized

## Slide 37: Optimize your Servers and Systems for the cloud Help your customers build better customized clouds!

## Slide 38: Related sessions
[SAC-429T] Using Windows Server 8 for building private and public IaaS clouds
[SAC-433T] Network acceleration and other NIC technologies for the data center
[SAC-437T] A deep dive into Hyper-V networking
[SAC-439T] Enabling multi-tenancy and converged fabric for the cloud using QoS
[SAC-442T] Building secure, scalable multi-tenant clouds using Hyper-V Network Virtualization – In this room!
[SAC-444T] Designing systems for continuous availability - multi-node with remote file storage
[SAC-446T] Designing systems for continuous availability and scalability
[SAC-451T] Building continuously available systems with Hyper-V

## Slide 39
Feedback and questions http://forums.dev.windows.com
Session feedback http://bldw.in/SessionFeedback
thank you

## Slide 40
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.