## Slide 1: Building Secure, Scalable Multi-Tenant Clouds using Hyper-V Network Virtualization
Murari Sridharan Yu-Shun Wang
Principal Development Lead Program Manager
Windows Core Networking
Microsoft Corporation
SAC-442T

## Slide 2: Windows Server 8 is Cloud Optimized
Enable Multi Tenant Clouds
Network Virtualization. Dynamic VM Placement. Secure Isolation. …
High Scale & Low Cost Datacenters
Leverage Hardware. High Availability. SMB2. Low Cost Storage. …
Manageable & Extensible
WMIv2. PowerShell. Extensible Switch. …

## Slide 3: Agenda
Build multi-tenant clouds efficiently at scale
  with Hyper-V Network Virtualization
Ecosystem requirements
Partner opportunities
You’ll leave with examples of how to
Make your datacenter dynamic and efficient
Build network virtualization capabilities in your hardware
Extend network virtualization capabilities of Windows Server 8

## Slide 4: Conventional datacenter is overprovisioned

## Slide 5: Resource Fragmentation
Spanning Tree Protocol eliminates paths
Good links that you paid for can’t be used
VLANs needed to divide up servers to limit packet storms and control plane traffic

## Slide 6: Resource Fragmentation
Size restrictions due to broadcast traffic overhead
Lots of small Layer-2 networks limited by concurrent VLAN tags
VLAN tags
ToR
Aggregation
Switch
VMs

## Slide 7: Static Workload Assignment
Server location on the LAN determines its network address
Migrating workloads requires network reconfiguration
Inefficient and error prone

## Slide 8: Dynamic Reconfiguration is Error Prone
VLAN tags
ToR
Aggregation
Switches
VMs
ToR

## Slide 9: Conventional datacenter is overprovisioned
Multi-tenancy makes it worse

## Slide 10: Multi-Tenancy on Shared Infrastructure
  Tenant Networks
  N Tenants
Contoso
NW
Traders
Woodgrove Bank
Contoso
N.W. Traders
Woodgrove Bank
Move
  Multi-tenant Datacenter

## Slide 11: Any Service, Any Server, Any Cloud

## Slide 12: Bring your network to the cloud
demo
Onboarding Contoso to the Cloud

## Slide 13: Demo: Hybrid Cloud
157.0.1.111
157.0.1.111
157.0.1.112
…
157.0.2.220
157.0.2.221
157.0.2.222
…
Hoster Datacenter
WEB | 10.0.1.3
SQL | 10.0.1.4
Contoso
10.0.1.3
WEB
10.0.1.4
SQL
Contoso
CloudNet Hosting Solutions
Customer Addresses
Provider Addresses

## Slide 14: Hybrid Cloud
Enterprises
  Seamless migration to the cloud
  Preserve host settings, IP addresses and policy
Cloud Administrator
  Easy to on-board tenants
  Flexible VM placement requiring no network reconfiguration
  Manage large number of tenant networks

## Slide 15: Hyper-V Network Virtualization
Server virtualization
  Run multiple virtual servers on a physical server
  Each VM has illusion it is running as a physical server
Hyper-V Network Virtualization
  Run multiple virtual networks on a physical network
  Each virtual network has illusion it is running as a dedicated fabric
Physical
server
Blue VM
Red VM
Blue network
Red network
Virtualization
Physical
network

## Slide 16: Hyper-V Network Virtualization
Location independent addressing by virtualizing the IP address
Create virtual Layer-2/Layer-3 topologies over any physical network that supports bi-directional IP connectivity
Physical network for example can be hierarchical 3-tier network, full bi-section bandwidth Clos network or a large Layer-2
Virtual networks can span over multiple physical subnets and across multiple sites

## Slide 17
Network Virtualization
  Generic Routing Encapsulation (GRE)
  IP Address Rewrite

## Slide 18: Generic Routing Encapsulation
1 Provider Address per HOST (shared by all VMs on the host)
Embed Tenant Network ID in the GRE header Key field
10.1.1.11
10.1.1.11
10.1.1.12
10.1.1.12
192.168.2.22
192.168.5.55
192.168.2.22192.168.5.55
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
1:N
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
GRE Key=20
GRE Key=30
MAC
MAC
192.168.2.22192.168.5.55

## Slide 19: Impact of GRE on Performance
Host Performance
  Any encapsulation will break stateless offloads in the host server (LSO, Checksum, RSC, RSS, VMQ)
  Engaging with IHVs to make stateless offloads GRE aware
Network Performance
  Multiple PAs can be associated with a physical server (M:N mapping of CA:PA) providing additional entropy
  Lowers burden of virtualization on the network infrastructure
  Deeper multi-tenancy integration requires changes to network devices/appliances, irrespective of the tunneling mechanism

## Slide 20: Address Rewrite
Each VM IP (CA) is mapped to a unique Provider Address (PA)
Regular TCP/IP packets on the wire
10.1.1.11
10.1.1.11
10.1.1.12
10.1.1.12
192.168.2.22
192.168.2.23
192.168.5.55
192.168.5.56
10.1.1.1110.1.1.12
192.168.2.22192.168.5.55
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
10.1.1.1110.1.1.12
192.168.2.23192.168.5.56

## Slide 21: Address Virtualization Summary
IP Rewrite
Performance and Compatibility
No need to upgrade existing NICs, existing switches, and existing network appliances
Immediately and incrementally deployable today without sacrificing performance
GRE Encapsulation
Deeper Multi-Tenancy Integration
Standards based – RFCs 2784 & 2890
As few as one IP address per host lowering burden on the switches
Full MAC headers and explicit Tenant Network ID marking supports for traffic analysis, metering and control
Hyper-V Network Virtualization leverages both

## Slide 22: Join the GRE ecosystem Informational RFC on Network Virtualization using GRE co-authored by Arista, Broadcom, Dell, Emulex, HP, Intel & Microsoft

## Slide 23: Call to Action
  NIC vendors
  Implement GRE compatible hardware offloads
  Switch vendors
  Use Tenant Network ID for ECMP, QoS, ACLs
  Appliance vendors
  Build GRE multi-tenant-aware products
  Network management software
  Build multi-tenancy aware control plane

## Slide 24
Software-Based Isolation

## Slide 25: Hyper-V Enforced Isolation
Hyper-V Extensible Switch
Green
VM 1
Red
VM 2
Server
Hyper-V Network Virtualization
Isolation based on
Tenant Network ID
Red
VM 1

## Slide 26: Flexible VM placement with Hyper-V enforced isolation
demo

## Slide 27: Demo: Hyper-V Enforced Isolation
157.0.1.112
157.0.1.111
157.0.1.111
157.0.1.112
…
157.0.2.220
157.0.2.221
157.0.2.222
…
Provider Addresses
WEB | 10.0.1.3
SQL | 10.0.1.4
Contoso
WEB | 10.0.1.3
SQL | 10.0.1.4
N.W Trader
10.0.1.3
WEB
10.0.1.4
SQL
Contoso
Hoster
10.0.1.3
WEB
10.0.1.4
SQL
N.W. Traders
Hoster Cloud

## Slide 28
Deployment & Management

## Slide 29: Incremental Deployment
Hoster Infrastructure
AD, DHCP, DNS, VMM, …
Database Cluster
Storage / SAN
VPN appliances, load balancers, proxies, …
CorpNet / Enterprise Infra: AD, DNS, DHCP, …
Windows Server 8 Hyper-V
Network Virtualization
Internet
Tenants
Cross
Premise

## Slide 30: Call to Action
Build cross-premise GRE gateway to connect public and private clouds
Build high-speed GRE gateway appliance to non-virtualized hardware devices
Incorporate gateway functionality into Top of Rack switches, storage appliances, load balancers, routers etc. or build a stand-alone appliance.

## Slide 31: Management Primitives
Remote management using WMI/PS
APIs to keep policy up-to-date to reflect VM migration
Logs for auditing

## Slide 32: Hyper-V Network Virtualization
Flexible VM Placement
    Decouples physical infrastructure from tenant’s virtual network
Administer VMs and the network separately
  Allow VM placement to occur independently of network topology
Scalable Layer-3 solution
  Immediately deployable on existing hardware & network gear
  Supports hierarchical and flat network topologies

## Slide 33: Call to Action
Join the GRE ecosystem
Build management software and a multi-tenancy aware control plane
Build multi-tenancy aware monitoring, diagnostic tools for Hyper-V Network Virtualization

## Slide 34: Related sessions
[SAC-437] A Deep Dive into Hyper-V Networking
[SAC-559] Extending the Hyper-V Switch
[SAC-433] Acceleration & Other NIC Technologies for the Datacenter
[SAC-439] QoS and Converged Fabric in the Datacenter
[SAC-433] Network Acceleration and other NIC Technologies for the Datacenter
[SAC-565] Windows Networking with PowerShell

## Slide 35: Further reading and documentation
Informational RFC draft on Network Virtualization using Generic Routing Encapsulation
  http://tools.ietf.org/html/draft-sridharan-virtualization-nvgre-00
Contact info –
  ws8cloudnetfb@microsoft.com

## Slide 36
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.