## Slide 1: Designing systems for continuous availability and scalability
SAC-446T
Surendra Verma
Development Manager
Microsoft Corporation
Mallikarjun Chadalapaka
Senior Program Manager
Microsoft Corporation
Jim Pinkerton
Architect
Microsoft Corporation

## Slide 2: Agenda
An Understanding of the Continuously Available Platform hardware and software features
Windows 8 Enables Partners To Deliver Differentiated, Continuously Available, Scalable, Cost-Effective Storage Solutions
Pointers to other talks for more detail
Define the “Continuously Available Platform”
Network Fault Tolerance and Scaling
  NIC Teaming
  File Access Related Scalability
NTFS enhancements for availability
Cost-effective business critical storage solutions
  Storage Spaces
OEMs
System Integrators
Network IHVs
Storage ISVs
Storage IHVs
Server Application Developers
WHO WILL BENEFIT FROM THIS TALK
TOPICS
WHAT YOU’LL LEAVE WITH

## Slide 3: Starting with the Basics
Goal: Enable industry standard servers to be continuously available
Secondary Goal: improve industry standard servers for better scale and failover time for continuously available services
Transparent failover is the ability to survive planned moves or unplanned failures – without errors visible to the user, without losing data, and while performing well at scale
Continuously available software and hardware platforms are designed to support transparent failover without data loss

## Slide 4: What is a Continuously Available Platform?
Single Node
Single Node
Preferred Deployment:
Clustered with at least 2 nodes for fault tolerance
RDMA NICs for Cluster Interconnect
Single Node
HBA
HBA
NIC
NIC
NIC
Preferred Deployment:
Multiple NICs for fault tolerance and scale
RDMA NICs for cluster interconnect and File Server deployments
HBA
Preferred Deployment:
Multiple HBAs for fault tolerance and scale
Choice of External Storage Array or External JBOD
Scale-Out

## Slide 5: Continuously Available Platforms
Capability | Single Node | Multi-Node
Redundant storage, storage serviceable with system running |  | 
Multiple network connections with transparent failover | * | *
Multiple storage connections with transparent failover | * | *
Shared data storage accessible from all nodes |  | 
Transparent failover between nodes without data loss |  | 
Redundant hardware components, serviceable with system running | * | *
*for price points that allow it

## Slide 6: Windows Server 8 E-to-E Storage Features, with File Server
Network Device Capabilities
RDMA
RSC
GRE
DCB
InfiniBand
Dynamic VMQ
IPsec Task Offload support from VMs
Hyper-V
Remote File Server VHDs
Online Storage Migration
Guest Clustering for Fibre Channel with Synthetic FC
Integrated with ODX, Trim, cluster client failover
DR – Hyper-V Replica
New VHD format (VHDX)
Networking
NIC Teaming
Better SLA enforcement (DCB, QOS)
Network Virtualization
Hyper-V Extensible Switch
SRIOV to guest
BranchCachev2
Platform Storage
File System (NTFS)
  64 TB Volumes
  Online Repair
  ODX, Trim
  Deduplication
  Integrity on SATA
Storage Mgmt.
  Native VHD mnt GUI
  Unified Storage Man. API, SMI-S
Virtualized Storage (Storage Spaces)
  Thin Provisioning,
  Resiliency, scale
  Pools
For External Storage Arrays
Optional Logo Req. for Thin Provisioning (Trim/Unmap) & Offloaded Data Transfer (ODX)
For Shared JBOD Storage Devices
Logo program for Storage Spaces-compatible hardware
Validation program for Clustered RAID Controllers
Data Mgmt.
Continuous and manual classification
Central access and audit control
Automatic RMS protection
Access Denied Remediation
Remote Storage Access
  Network & Server transparent failover
Active-Active
SMB2 Direct /RDMA
SMB2 Multichannel
VSS for SMB2 File Share
Heterogeneous Access
    NFSv3, NFSv4.1, iSCSI
    Branch - Directory Leases
  Branch - Folder Redirection “always offline” w/ sync
  Support for ODX , Trim, BranchCachev2
  FS Admin Console
Local I/O
Remote I/O
Local I/O Access
File Server & Networking Stack
Clustering
Cluster Aware Updates
Fast failover
Distributed NetNames
Intelligent VM placement & priority
Bitlocker support
Cluster Shared Volumes v2
Single namespace
Windows Caching integration
Transparent repair
Spaces Integration
Node 2
Node N
Scalable Cluster Management
Multi-Machine Management
PowerShell based management
Standards based management
Easy Deployment
Scalable Cluster Interconnect
Ethernet (RDMA opt.)
InfiniBand (RDMA)
Hyper-V
VSwitch
VM
VM
VM
Mgmt OS
NIC
NIC
External Storage Arrays
Shared JBOD
Node 1
NIC
NIC
HBA
HBA
Internet &
Data Center
Platform Storage
Clustering
File Server & NetworkingStack
VMBus
Data Management
VM
Local I/O
Node 1
Node 2
Node N
Too much for one talk!

## Slide 7: What We’ve Covered So Far …
Business and Partnering Opportunities: “Windows Server 8” Continuous Availability 
Designing Systems for Continuous Availability and Scalability
Session 446
Designing Systems for Continuous Availability – Multi-node with Remote File Storage
Session 444
Building Continuously Available File Server NAS Appliances
Session 449
Platform Storage Evolved 
Session 474
Designing Systems for Continuous Availability – Multi-node with Block Storage
Session 450
Building Continuously Available Systems with Hyper-V
Session 451
Session 443

## Slide 8: Windows Server 8 Continuously Available Platform: New Device Capabilities
Node 2
Node N
Network Devices for Converged Networks
New Network Fabric Support
  InfiniBand (IB) support, with inbox program
New Network Device Capabilities
  Multiple forms of new offloads, virtualization
Used for cluster interconnect & for File Server
Storage Devices
New virtualized storage: Spaces
New external storage choice: Shared JBOD
New type of HBA: Clustered RAID Controller
New capabilities for External Storage Arrays:
  Offloaded data transfer, Trim, TP Notifications
External Storage Arrays
Shared JBOD
Node 1
HBA
HBA
Platform Storage
Clustering
Data Management
Hyper-V
VSwitch
VM
VM
VM
Mgmt OS
VMBus
VM
Scale-Out
[433,437] “Windows Server 8” Networking
LEARN
MORE

## Slide 9: “Windows Server 8” Continuously Available Platform with File Server
Node 2
Node N
Node 2
Node N
Network Devices for Converged Networks
New Network Fabric Support
  InfiniBand (IB) support, with inbox program
New Network Device Capabilities
  Multiple forms of new offloads, virtualization
Used for cluster interconnect & for File Server
Hyper-V
VSwitch
VM
VM
VM
Mgmt OS
External Storage Arrays
Shared JBOD
Node 1
HBA
HBA
Platform Storage
Clustering
NIC
NIC
NIC
NIC
File Server & NetworkingStack
VMBus
Data Management
VM
Node 1
Scale-Out
Scale-Out
[433,437] “Windows Server 8” Networking
LEARN
MORE
Storage Devices
New virtualized storage: Spaces
New external storage choice: Shared JBOD
New type of HBA: Clustered RAID Controller
New capabilities for External Storage Arrays:
  Offloaded data transfer, Trim, TP Notifications

## Slide 10
Network Fault Tolerance and Scale
  NIC Teaming (LBFO)
  File Access Related Scalability
    SMB 2.2 Multichannel
    SMB 2.2 RDMA

## Slide 11: Network Interface Card (NIC) Teaming
Hyper-V Extensible Switch
NIC 1
NIC 2
NIC 3
Network switch
LBFO Provider
Protocol edge
Virtual miniport 1
Frame distribution/aggregation
Failure detection
Control protocol implementation
IM Mux
Port 1
Port 2
Port 3
LBFO Configuration DLL
LBFO Admin GUI
Kernel mode
User mode
WMI
IOCTL
Built into Windows Server 8
Transparent Failover
  Link-by-link failure detection (w/ switch support) causes transparent failover
Throughput
  Active-active or active-passive load balancing
  A single TCP connection will go on a single NIC
[433] Acceleration & Other NIC Technologies for the Data Center
LEARN
MORE

## Slide 12: SMB 2.2 Multichannel
Multiple 10GbE or InfiniBand
Multiple 1GbE NICs
SMB 2.2 Server
SMB 2.2 Client
Switch
1GbE
SMB 2.2 Server
SMB 2.2 Client
NIC
1GbE
NIC
1GbE
Switch
1GbE
NIC
1GbE
NIC
1GbE
Switch
10GbE/IB
NIC
10GbE/IB
NIC
10GbE/IB
Switch
10GbE/IB
NIC
10GbE/IB
NIC
10GbE/IB
Sample Configurations
Multiple TCP streams for one SMB 2.2 session
  Single NIC – with RSS enables more CPUs to process traffic
  Multiple NICs, with NIC Teaming – SMB 2.2 can use a single IP address per team
  Multiple NICs, Without NIC Teaming – each NIC must have a unique IP addresses (Required for RDMA NICs)
Failover
  SMB 2.2 Multichannel implements end-to-end failure detection
  Fully leverages NIC teaming failover but does not require it
Throughput
  Bandwidth aggregation with multiple NICs
  Multiple CPUs to process network interrupts with single RSS-capable NIC or multiple NICs
Automatic Configuration
  SMB 2.2 detects and uses multiple network paths

## Slide 13: SMB 2.2 Multichannel Performance
Preliminary data shows linear bandwidth scaling for up to 4 interfaces
    1 – 1150 MB/sec
    2 – 2330 MB/sec
    3 – 3320 MB/sec
    4 – 4300 MB/sec
Receive Side Scaling support in the NIC is critical
BW at small I/Os is bottlenecked on CPU
Chart: SMB 2.2 Client Interface Scaling - Throughput
| 512 | 1024 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
1 x 10GbE | 156.8149 | 226.1836 | 687.6917 | 875.673 | 1124.8726 | 1138.7496 | 1128.3732 | 1163.7644 | 1164.9838 | 1170.0508 | 1154.3338
2 x 10GbE | 162.0595 | 322.3353 | 1224.7526 | 2116.9096 | 2334.7591 | 2337.8289 | 2307.9321 | 2305.1336 | 2324.7594 | 2313.7383 | 2332.6083
3 x 10GbE | 161.8836 | 321.1907 | 1238.7885 | 2410.8725 | 3131.6209 | 3329.5767 | 3326.9938 | 3190.6087 | 3147.5608 | 3139.8305 | 3123.3739
4 x 10GbE | 161.5843 | 315.5044 | 1232.7342 | 2397.5162 | 3211.4626 | 3978.5875 | 4234.7012 | 4307.2203 | 4303.5958 | 4265.05 | 4231.0107
Data is all the way to persistent storage
//BUILD whitepaper provides full details
  http://go.microsoft.com/fwlink/p/?LinkId=227841

## Slide 14: Scaling Network Traffic
New Network offloads that improve scalability
  Receive Side Coalescing (RSC), IPsec Task Offload support from VMs
New network features for Virt. w/ Continuous Availability
  GRE, Dynamic VMQ
What is left to solve?
  CPU Utilization and throughput concerns
    Large I/Os – CPU utilization at high data rates (throughput is great)
    Small I/Os – CPU utilization and network throughput at high data rates
Solution: Remote Direct Memory Access (RDMA)
[437] A Deep Dive into Hyper-V Networking
LEARN
MORE

## Slide 15: SMB2 Direct (SMB2 over RDMA)
SMB 2.2 Client
SMB 2.2 Server
SMB 2.2 Server
SMB 2.2 Client
User
Kernel
Application
Disk
R-NIC
Network w/ RDMA support
NTFS SCSI
Network w/ RDMA support
R-NIC
Used by File Server and Clustered Shared Volumes (CSV version 2) for storage communication within a cluster
Advantages
  Scalable, fast and efficient storage access
  Minimal CPU utilization for I/O processing
    High throughput with low latency
Required hardware
  RDMA-capable network interface (R-NIC)
Can leverage SMB2 Multichannel for load balancing and failover
RDMA is “Remote Direct Memory Access” – a secure way to enable a DMA engine to transfer buffers between two machines across the network

## Slide 16: SMB 2.2 Direct Performance
Client: ~20% of 4 cores, or 80% of one core
Server: ~12% of 12 cores, or 140% of one core
3100 MBytes/sec
Bandwidth
CPU
Bandwidth
CPU
  Windows Server 8 supports all standards based RDMA networks
  Ethernet based protocols
    iWARP – RDMA on top of TCP/IP
      IETF standard over TCP/IP – http://www.ietf.org
      Only routable RDMA protocol
    ROCE (RDMA Over Converged Ethernet) - InfiniBand protocols on Ethernet
      IBTA standard – http://infinibandta.org
      Requires switches to support Data Center Bridging (DCB)
  InfiniBand based protocols
    InfiniBand protocols on an InfiniBand network (32 gbits/sec, 56 gbits/sec…)
InfiniBand Preliminary 512 KB I/O Results:
[433] Acceleration & Other NIC Technologies for the Data Center
LEARN
MORE

## Slide 17
NTFS enhancements for availability
  Improved NTFS integrity with industry standard storage
  Maximized file system availability

## Slide 18: Improved NTFS Integrity Usage of flush v/s force-unit-access
NTFS will flush disk cache to ensure ordered writes
Reduces possibility of corruption on power loss
Allows the disk to cache data for as long as safely possible
Delivers better reliability on industry standard SATA storage

## Slide 19: Maximized File System Availability NTFS – Online scan and repair
Prioritized volume availability for service uptime
  Online repair
  Online scan & corruption logging
Minimal downtime
  Scheduled repair
  Downtime proportional only to # logged corruptions
  Failover Clustering & CSV integration
Better manageability
  File system health via Action Center, PowerShell, Server Manager
Confidently deploy 64TB NTFS volumes with Windows 8

## Slide 20: Maximized File System Availability Online scan & repair: execution flow
Detect Corruption
NTFS detects a perceived anomaly in file system metadata
Online Verification
NTFS will validate whether issue is transient or genuine – volume remains online
If not transient, NTFS will attempt to rapidly self-heal – volume remains online
Online Self-Healing
Identify & Log
If not self-healed, NTFS will identify and log corrective actions
Precise & Rapid Correction
At the next maintenance window, volume can be taken offline and logged corruptions are corrected in seconds
For virtualized deployments on CSV, VM I/O is transparently paused for rapid correction and subsequently automatically resumed.
Administrator will be notified
Volume continues to remain online.

## Slide 21: Maximized File System Availability An illustrative example
Chart: 
| 100 Million Files | 200 Million Files | 300 Million Files
Windows Server 2008 R2 | 109 | 292 | 376
"Windows Server 8" | 0.13 | 0.13 | 0.13
Volume downtime to handle one corruption
Minutes
In this benchmark, “Windows Server 8”
execution time <8 seconds

## Slide 22: The New CHKDSK - Enabling Continuous Availability
demo

## Slide 23
Cost-effective Business Critical Storage – Storage Spaces

## Slide 24: Windows 8 is the most cost-effective platform for continuously available and highly scalable data access

## Slide 25: Cost-Effective Business Critical Storage Storage Spaces
Powerful new platform abstractions
  Storage Pools – Units of Aggregation, Administration & Isolation
  Storage Spaces (virtual disks): Resiliency, Provisioning & Performance
Target design point
  Industry standard interconnects: SATA or (Shared) SAS
  Industry standard storage: JBODs
Storage Spaces enable partners to deliver a new category of highly capable storage solutions to all Windows customer segments at dramatically lower price-points & maximized operational simplicity

## Slide 26: Storage Spaces Physical Deployment Topologies
OR
Direct-Attached
Shared – Availability & Scale
SATA or SAS
Shared SAS

## Slide 27: Storage Spaces - Ease Of Provisioning
demo

## Slide 28: Storage Spaces Capabilities
Optimized storage utilization
Resiliency & application-driven error correction
High-availability & scale-out with Failover Clustering & Cluster Shared Volumes
Operational simplicity
  Delegated administration & isolation for multi-tenant deployments
Workload optimized performance via heterogeneous media support

## Slide 29: Storage Spaces Optimized & flexible utilization
On-demand provisioning with trim support
  For use by NTFS, Hyper-V, and other applications e.g. SQL
Elastic capacity expansion
  Simply add more physical drives
VM
Storage Space
Hyper-V
NTFS
Filters
Contoso Hosting Company
Company A Pool
Company B Pool
20TB
Pool
20TB
Pool
40 TB physical storage
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
Thinly-provisioned Spaces contained within Pools
Industry standard physical storage

## Slide 30: Storage Spaces Resiliency & error correction
Redundant storage
  Mirrored Spaces and Parity Spaces with integrated journaling
Rapid Recovery – per pool hot spare support
Application driven intelligent error correction
Hot Spare
Industry standard physical storage
Mirrored
Space
Parity
Space
Mirrored
Space
Mirrored
Space
Parity
Space
Mirrored
Space
Mirrored
Space
Parity
Space
Resilient Spaces contained within a Pool

## Slide 31: Storage Spaces - Resiliency
demo

## Slide 32: Intelligent Error Correction – Mark Handle
// Change the handle info to read from a copy
MARK_HANDLE_INFO HandleInfo;
ZeroMemory( &HandleInfo, sizeof(MARK_HANDLE_INFO) );
HandleInfo.HandleInfo = MARK_HANDLE_READ_COPY;
HandleInfo.CopyNumber = 1; /* or 0, 1, ... */
Success = DeviceIoControl(NonCachedFileHandle, FSCTL_MARK_HANDLE, &HandleInfo,
sizeof(MARK_HANDLE_INFO), NULL, 0, NULL);
// Normal read file call
Success = ReadFile( NonCachedFileHandle, Buffer, BytesToRead, &BytesRead, Overlapped);

## Slide 33: Intelligent Error Correction – Perform Repair
// Repair call
union {
REPAIR_COPIES_INPUT RepairInput;
UCHAR RepairInputBuffer[FIELD_OFFSET(REPAIR_COPIES_INPUT, RepairCopies) + sizeof(ULONG) * 2];
};
REPAIR_COPIES_OUTPUT RepairOutput;
ZeroMemory( &RepairInput, sizeof(RepairInputBuffer) );
RepairInput.Flags = 0;
RepairInput.FileOffset = 0x1000;
RepairInput.Length = 0x4000;
RepairInput.SourceCopy = 1;
RepairInput.NumberOfRepairCopies = 2;
RepairInput.RepairCopies[0] = 0;
RepairInput.RepairCopies[1] = 2;
Success = DeviceIoControl(FileHandle, FSCTL_REPAIR_COPIES, &RepairInput,
sizeof(RepairInputBuffer), &RepairOutput,
sizeof(REPAIR_COPIES_OUTPUT), NULL);

## Slide 34: Storage Spaces Operational simplicity
Managed via Windows Storage Management API
Flexible & granular administrative control with self-service agility & tenant isolation
Contoso Hosting Company
Company A Pool
Company B Pool
Workload Admin
Space
Space
Hoster Admin
Space
Space
Workload Admin
Tenant Admin
Tenant Admin
Granular Access Control
Multi-tenant deployment

## Slide 35: Storage Spaces Effectively utilize hardware investment
Supports deployment requirements
  Utilize both SSD and HDD media types
  Control placement at Space granularity
Silver
Home Directories
Bronze
Archive
Gold
Finance
Thinly-provisioned Spaces contained within a Pool
Industry standard physical storage
Space
Space
Space
Backup
Archive
Space
Solid-state drives
15K RPM HDDs
Near-line HDDs
Home Dir
Finance
Finance

## Slide 36: Clustered Storage Spaces Scalable & continuously available workload deployments
4x Blades
Storage
Deployable elements
Physical View
Logical View
…
…
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
.\Finance
.\CRM
.\File-Shares
Enterprise Workload
Enterprise Workload
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
64TB
Space
VMs
.\db
.\VHDs
.\Home
Unified Cluster Shared Volume namespace
Clustered Pools & Spaces
Continuously available file server

## Slide 37: Summary
  Partners opportunity to build new options for reliable storage
  ODM, SI, & OEM opportunity to deliver new cost-effective solutions
  Application developer opportunity to optimize and manage storage
  IHV opportunity to deliver against new storage capabilities – follow certification requirements. For additional information contact:
    sfsquestions@microsoft.com for storage platform questions
    AskWinCAHW@microsoft.com for Validation Program for Clustered RAID Controllers
  Design systems for continuous availability and scalability
  Lowest Cost Systems, use clustering with redundant hardware optional except for shared storage with data redundancy
  Scalable Systems, use clustering, multiple NICs, multiple storage controllers, and redundant storage for improved SLA and better scalability

## Slide 38: For more information
RELATED SESSIONS
SAC-443T – Business and partnering opportunities: Windows Server 8 continuous availability
SAC-474T – Platform storage evolved
SAC-446T – Designing systems for continuous availability and scalability
SAC-450T – Designing systems for continuous availability - multi-node with block storage – multi-node with block storage
SAC-444T – Designing systems for continuous availability - multi-node with remote file storage - multi-node with remote file storage
SAC-451T – Building continuously available systems with Hyper-V
SAC-449T – Building continuously available file server NAS appliances
LEARN
MORE
Continuously Available Platform Talks
Related Windows Server 8 Talks
LEARN
MORE
SAC-430T – Designing the building blocks for a Windows Server 8 cloud
SAC-433T – Network acceleration and other NIC technologies for the data center
SAC-437T – A deep dive into Hyper-V networking
SAC-439T – Enabling multi-tenancy and converged fabric for the cloud using QoS

## Slide 39
Feedback and Questions: http://forums.dev.windows.com
Session Feedback: http://bldw.in/SessionFeedback
thank you

## Slide 40
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.