## Slide 2: Bringing Kinect Into Your Windows Store Apps
Kevin Kennedy
Senior Development Lead, Kinect Team, Microsoft
2-532

## Slide 3: K4W News @ //build
Kinect for Windows v2 coming this summer
Create & publish Kinect apps to the Windows Store
Kinect Unity plugin for both desktop & store apps

## Slide 4: Agenda
Kinect Development Overview
  Desktop and Windows Store
Kinect Data Sources
  Color, Depth, Infrared, Body, BodyIndex
Other tools
  Frame synchronization, coordinate mapping, processing body data
Notes: At start of presentation:
Survey Audience:
Who went to The earlier "" talk by Chris White?
Who had used Kinect V1?

## Slide 5: Kinect Overview

## Slide 6: The data sources
Audio, Speech,
Interactions
Depth
Infrared
Body
Body Masks
Color
Notes: Called “Streams” in V1
When talking about lean - present body as thumbstick. Tie in to design principles
Interactions and speech too

## Slide 7: Demo: Data Sources
Notes: Show detail of depth
Removal of other light sources from IR
Hand states

## Slide 8: High-level architecture
Kinect Drivers
Kinect Runtime
.Net
API
.Net
Apps
Native API
Native Apps
WinRT API
Windows Store Apps
C#, VB, JS, C++/CX
Multiple Kinect enabled applications can run simultaneously
Physical Kinect Sensor
Notes: One instance of the service per session
All the same – not lower-higher level
Talk to USB3, Windows 8, GPU requirement

## Slide 9: Design Principles
Minimize per-frame allocations
Low latency – high throughput
Expose low level data and high level interpretations
Notes: Talk to why these are important.
System is moving a lot of data constantly
Apps should “get-in, do it, and get out”
Deliver range of stuff from low to high level.
Working towards exposing higher level interpretations of lower level data – if you just want one specific goal
Hand state
Lean
Expressions,
Etc.

## Slide 10: Creating a new store app using Kinect
In “New Project” create a new Windows Store app
Enable Microphone and Webcam capabilities
Add a reference to WindowsPreview.Kinect
Use the WindowsPreview.Kinect namespace in your code
Notes: Everything is currently “WindowsPreview.Kinect” That, of course, will change before final RTM.

## Slide 11: Accessing Kinect Data Sources

## Slide 12: The KinectSensor class
Represents a single physical sensor
Always valid
  If sensor is unplugged, app will not receive any frames.
  App will start receiving frames when plugged back in
  KinectSensor.IsAvailable tells you if the sensor is actually there
this.sensor = KinectSensor.GetDefault(); this.sensor.Open(); // Make the world a better place with Kinect this.sensor.Close();
Sensor
Source
Reader
Frame
Frame Ref
sensor = kinect.KinectSensor.getDefault(); sensor.open(); // Make the world a better place with Kinect sensor.close();
C#
JavaScript
Notes: Improvement over V1 where app had to do more work to manage sensors coming and going
Talk to usage pattern

## Slide 13: Sources
Expose metadata about the source and give access to readers
Sensors expose one source per data type
Use the source
Sensor
Source
Reader
Frame
Frame Ref
Notes: Metadata – count of bodies, width and height of bitmap sources
We’ll talk about readers in the next slide

## Slide 14: Readers
Give access to frames
  Events
  Polling
Multiple readers may be created on a single source
  Allows better componentization
Readers can be paused
Sensor
Source
Reader
Frame
Frame Ref
Notes: “Allow multiple pieces of your application independent access to the frames”
Pausable – explain benefits

## Slide 15: Readers
C#
InfraredFrameReader reader =
sensor.InfraredFrameSource.OpenReader();
reader.FrameArrived +=
InfraredReaderFrameArrived;
...
// see in the dark
...
reader.Dispose();
JavaScript
reader = sensor.infraredFrameSource.openReader();
reader.onframearrived = function (args) { ... };
...
// see in the dark
...
reader.close();

## Slide 16: Frame references
Sent in frame event args and give access to the actual frame via AcquireFrame
By the time the app calls AcquireFrame, the frame might already have expired
FrameReference.RelativeTime allow you to temporally correlate frames
Sensor
Source
Reader
Frame
Frame Ref
Notes: Why will a frame expire
  A newer frame has already taken its place
  AcquireFrame returns null
  Caller always needs to check
Goes back to optimizing for
Timestamp replaces V1 frame index
Compare hand location across two bodies to know how fast hand is moving. Coordinating skeleton over IR overlay

## Slide 17: Frame references
C#
using (InfraredFrame frame =
args.FrameReference.AcquireFrame())
{
if (frame != null)
{
// Get what you need from the frame
}
}
JavaScript
var frame = args.frameReference.acquireFrame();
if(frame != null) {
// Get what you need from the frame
frame.close();
}
Notes: If the frame is null, that frame has expired. Your app will quickly catch up to a valid frame.

## Slide 18: Frames
Gives access to the frame data
  Make a local copy or access the underlying buffer directly
Contains metadata for the frame
  e.g. Color: format, width, height, etc.
Pro tip: Minimize how long you hold onto the frame
  Not Disposing frames will cause you to not receive more frames
Sensor
Source
Reader
Frame
Frame Ref

## Slide 19: Demo: Display an infrared frame in a Windows Store App
Notes: Create a Windows Store App, display color frames. Practice the hell out of this.

## Slide 20: Data source details

## Slide 21: InfraredFrameSource
512 x 424 array of pixels
30 fps
2 bytes per pixel
  16-bit IR intensity value
Ambient light removed
From the same physical sensor as depth
Notes: Not heat – different frequency
People have used this for: night vision, computer vision applications that need consistent illumination like face recognition, retro reflective materials also show up very well

## Slide 22: DepthFrameSource
512 x 424 array of depth pixels
30 fps
Range: 0.5 - 4.5 meters
Each depth pixel is a 16-bit distance in millimeters from the sensor’s focal plane

## Slide 23: ColorFrameSource
1920 x 1080 array of color pixels
Different image sensor than depth
30 fps
  Will maintain brightness and quality by dropping to 15 fps in low-light
Notes: Different sensor means different pixel dimensions and aspect ratio. Also has wider field of view so there will be color pixels that don’t map to depth pixels.

## Slide 24: BodyIndexFrameSource
512 x 424 array of body indexes
  -1: No body at this pixel
  0 to 5: Index of the corresponding body, as tracked by the body source
30 fps
Resolution is same as depth
Notes: Could detect a body moved by comparing one frame to the next
Can be used directly for some background removal

## Slide 25: BodyFrameSource
Frame data is a collection of Body objects each with 25 joints
  Each joint has position in 3D space and an orientation
Up to six simultaneous bodies
30fps
Hand State on 2 bodies
Lean
Notes: Call out thumb and fingertip, hips, skeleton leaning

## Slide 26: AudioFrameSource
Data is audio samples captured over a specific interval of time
Audio data is associated with an “audio beam”
  A steerable “cone” of focus for audio
  May be automatically or manually aimed

## Slide 27: Other tools

## Slide 28: Coordinate mapping
Three coordinate systems
Coordinate mapper provides conversions between each system
Convert single or multiple points
Name | Applies to | Dimensions | Units | Range | Origin
ColorSpacePoint | Color | 2 | pixels | 1920x1080 | Top left corner
DepthSpacePoint | Depth, Infrared, Body index | 2 | pixels | 512x424 | Top left corner
CameraSpacePoint | Body | 3 | meters | – | Infrared/depth camera
Notes: CameraSpacePoint was named SkeletonPoint in the V1 API. But it applies more generally, not only to Body joint positions, but to any point that is within the depth camera’s field of view. Hence, the new name.

## Slide 29: MultiSourceFrameReader
Allows the app to get a matched set of frames from multiple sources on a single event
Caveat: Delivers frames at the lowest FPS of the selected sources
Notes: Replaces AllFramesReady event in V1

## Slide 30: Demo: Handle body frames and coordinate mapping

## Slide 31: Processing body data
Every app is different in what it does with body data. However, some processing is almost always required
  Smoothing
  Selectively ignoring low-confidence data
    Tracked vs. Inferred joints
  Heuristics
  Machine learning
  …
Notes: Guidance on using inferred joints

## Slide 32: Other features
Activities, Appearance, Expression
  EyeLeftClosed, EyeRightClosed, LookingAway, MouthMoved, MouthOpen, WearingGlasses, Happy expression, Neutral expression
Speech
HD Face
Unity
Fusion

## Slide 33: Other Talks @ //build
Kinect 101: Introduction to Kinect for Windows
  Wednesday, April 2nd 4-5pm, Room 3024
Building Windows, Windows Phone, and Xbox One Apps with HTML/JS/CSS & C++
  Wednesday, April 2nd 1-2pm. Room 3024

## Slide 34: Getting Started
Preorder v2 - Use your MS Store credit
Dev Center – http://aka.ms/k4wdev
More Info – http://kinectforwindows.com

## Slide 35: Q & A

## Slide 36
Your Feedback is Important
Fill out an evaluation of this session and help shape future events.
Scan the QR code to evaluate this session on your mobile device.
You’ll also be entered into a daily prize drawing!

## Slide 37
© 2014 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.