## Slide 2: Azure IoT Security
Clemens Vasters
Lead Architect, Azure IoT Services @clemensv
2-625

## Slide 3: Agenda
Connected Things and the IoT
Inventory – What We Already Know
Security and Privacy Principles
Azure IoT Services
Outlook and Roadmap

## Slide 4: Connected Things
Internet
ISP
(Mobile) Network Operators
Personal Environment and Networks
Device
Device
Device
Device
Field Gateway
Cloud Systems
Device
Cloud Gateway
Device
Local Interaction
MNO Gateway
Cloud Portals and APIs
Mobile & Web Interaction
Control System
Analytics
Data Management
Watches, Glasses, Work Tools, Hearing Aids, Robotic Assistance, …
Homes, Vehicles, Vessels, Factories, Farms, Oil Platforms, …
Vehicle Fleets, Sea Vessels, LV Smart Grids, Cattle, …
Local Gateway
Local Portals and APIs
Control System
Analytics
Data Management

## Slide 5: IoT Enabled Infrastructure
Electricity Distribution
Gas Distribution
Patient Tracking
Mobile Care
Safety Management
Climate Control
Lighting
Energy Management
Drinking Water
Waste Water
Pollution Control
Fire Protection
Medical Emergency
Public Order
Energy
Toll Collection
Traffic Flow
Air Traffic Control
Bus/Tram/Train
Traffic Alerts
Street Quality
Mobility
City
Health
Buildings
Flood Control
Solid Waste
Air Quality
Lifts and Escalators
Signage
Water
Wind/Solar/Geothermal
Fuel Distribution
Power Plants
Nuclear Waste
Oil/Gas Production
Coal Mining
OR Equipment
Vital Monitoring
Implants
Disability Aids
Lab Equipment
Radiology Equipment
Rule Enforcement
Airports
Taxi
Diabetes

## Slide 6: Many IoT solutions control critical operations at the core of industrial and civil infrastructure. Digital security will be increasingly interwoven with physical safety of life and equipment.

## Slide 7: Many IoT solutions will provide very deep and near-real time insight into industrial and business processes, as well as into homes and the immediate personal environment. Privacy matters.

## Slide 8: What Do We Already Know?
Best Practice: IT and OT engineers collaborate in making “cyberphysical” systems safe and secure.
OT engineers knows how to make physical things safe and secure
  Standards, Procedures, Training, Continuous Improvement
  Physical access management
  Hazard and Risk Analysis
  Monitoring and Maintenance
  Fail Safe and Safety Equipment
IT engineers know how to make digital things secure.
  Secure Development Lifecycle
  Secure Network Technologies
  Threat & Vulnerability Mitigation
  Monitoring and Alerting
  Software/Firmware Auto-Updates
  Privacy Models

## Slide 9: Microsoft Cloud Security Principles
Security Development Lifecycle & Operational Security Assurance
Network and Identity Isolation
Vulnerability / Update Management
Least Privilege / Just-in-Time (JIT) Access
Respond
Protect
Auditing and Certification
Live Site Penetration Testing
Fraud and Abuse Detection
Centralized Logging and Monitoring
Detect
Breach Containment
Coordinated Security Response
Customer Notification

## Slide 10: Secure Development Lifecycle
http://microsoft.com/sdl
Development process for creating (and running) secure software as practiced at Microsoft

## Slide 11: Defense in Depth
Policies, Procedures, Guidance
Cloud
Field Gateways
Devices
Physical
Global Network
Identity and Access Control
Application
Data
Physical
Physical
Local Network
Local Network
Edge
Application
Data
Data
Host
Host
Host
Data Privacy Protection and Controls
People and Device Identity Federation, Data Attestation
Trustworthy Platform Hardware, Signed Firmware, Secure Boot/Load
Secure Networks, Transport and Application Protocols, Segmentation
Tamper/Intrusion Detection Physical Access Security

## Slide 12: Where things get tricky…

## Slide 13: Capability constrained devices
IoT Sweet Spot
$1000 PCs
$400 Phones
IoT capabilities are primarily value-add to other primary capabilities
How much computer, storage, and networking circuitry can you add to the BOM for a $40-range retail product for that value-add?
Tiny devices make awfully vulnerable network servers
Cost
Computational Capabilities
Memory/Storage Capacity
Energy Consumption/Source
$1 Sensor
$10000 Server
Component Quality

## Slide 14: Not everything is “green-field”
Factories and other industrial and utility environments are “brown-field”
  Production lines and facilities represent very significant capital investments
  Iterative technology deployment and upgrades
  Re-fit of existing (sometimes decades old) equipment with tech add-ons
Buildings and homes are too
  Entertainment systems (TV, A/V receivers, Set-Top boxes, Bluray Players)
  Comfort and sanitation systems (Heaters, A/C, Water, Gas, Thermostats)
  Kitchen appliances
  Security systems
IoT solutions must often integrate into environments with devices designed and deployed a decade or more apart

## Slide 15: Legacy Network Design Attitude Reality
Network Security modeled after physical access security
Segregated networks. Well-defined gates.
Access control at the network/gateway level.
Network access sufficient to access assets.
Device
Device
Device
Device
Local Interaction
Local Gateway
Local Portals and APIs
Control System
Analytics
Data Management
AuthN/Z

## Slide 16: Legacy Remote Access Practices
PLC
VPN
LAN
LAN

## Slide 17: Threats?
Service Desk
Machine Control Logic
Operator
Configuration
S,R
T,I,D
T,I,D
T,I,D
T,I,D
T,I,D
T,I,D
S,T,R,I,D,E
S,T,R,I,D,E
T,R,I,D
Spoofing
Tampering
Repudiation
Information Disclosure
Denial of Service
Elevation of Privilege
PLC

## Slide 18: What do the boxes help with?
Service Desk
Machine Control Logic
Operator
Configuration
T,I
T,I
Spoofing
Tampering
Repudiation
Information Disclosure
Denial of Service
Elevation of Privilege
… and they even broaden the attack surface area by fusing the networks
Not a whole lot …

## Slide 19: What do the boxes really nicely help with?
Service Desk
Machine Control Logic
Operator
Configuration
T,I
T,I
1. Pwn This
2. Pwn That

## Slide 20: We’ve also seen this in vehicle telematics
Vehicle
Diagnostics
Entertainment
Control
CAN BUS / “Telematics Box”
VPN Gateway
ERP
CRM
Fleet, Vehicle, and Driver Solutions
…
…
MNO Private APN
Public APN
Vehicle
Vehicle
Vehicle
Vehicle
Own one, own them all
More issues:
+ Addressing and Discovery + Temporal Coupling

## Slide 21: Defense Strategies
Authentication Credentials Management
Authorization Policy Management
Denial of Service
Intrusion Detection
Auditing
Monitoring
Alerting
Will you defend a million tiny, underpowered, public network servers that must triage unsolicited traffic?
Or do you think they could use some help with defense?

## Slide 22: Service Assisted Communication (SAC)
(CG)NAT Firewall Router
Isolated Network
Service Gateway
Client
Port Mapping is automatic, outbound
Device does not actively listen for unsolicited traffic
No inbound ports open, attack surface is minimized
Public address, full and well defendable server platform
Q
Q
Device Identity Registry/Directory
Connections are device-initiated and outbound
Non-IP
Field Gateway
Access Control Policies

## Slide 23: Service Assisted Communication “Peer to Peer”
(CG)NAT Firewall Router
Mobile Cell
Service Gateway
Q
Q
(CG)NAT Router
Mobile Cell
Temporal Decoupling Logical Addressing
Device Authentication
Authorization (Access Policy Enforcement)
DoS Defense
Application Layer Integration (vs. Link/Network)
Mobile Backend

## Slide 24: SAC - Trust Brokerage for Nomadic Devices
Trust
Device Identity Registry/Directory Access Policies
“Resident Devices”
“Nomadic Devices”
Berlin
2
Tokens
Local Networking Scope
Cloud Scope
Token expresses current membership of the device in the solution context.
Asymmetrically signed by directory. Cacheable. Expires periodically.

## Slide 25: Vehicle Telematics
Datacenter(“Cloud”)
Vehicle
Diagnostics
Entertainment
Control
CAN BUS / “Telematics Box”
Telematics Gateway
ERP
CRM
Fleet, Vehicle, and Driver Solutions
…
…
Control
Value-Add Services, Analysis and Optimization
Servicing
Hard real-time
Near real-time
AMQP 1.0 Link Bi-Directional Secure
Reliable Transfer Application Level
No Peer Exposure

## Slide 26: Industrial Automation
Device
Device
Device
Device
OPC UA Gateway
Cloud Systems
Cloud Gateway
Cloud Portals and APIs
Control System
Analytics
Data Management
Local Gateway
Local Portals and APIs
Control System
Analytics
Data Management
AMQP
OPC/TCP & Fieldbuses
AMQP 1.0 Link Bi-Directional Secure
Reliable Transfer Application Level
No Inbound Ports

## Slide 27: Scale

## Slide 28: The Scale Challenge
Time Series and State Storage
Event Storage Real Time Analytics
Device Software Management
Device Identity Management
x Millions
x GByte/sec
Data Flow
Connectivity
x PByte
Historic and Predictive Analytics

## Slide 29: Device Identities. Device Management. Hyper Scale.
100
10,000
1,000,000
Makers. Prototypes. Hackathons.
“Enterprise Scale”
Consumer Products

## Slide 30: Azure IoT Hub

## Slide 31: Azure IoT Hub
HTTPS AMQPS
IoT Hub
Up to 10M Devices per Hub
Identity Registry
Device Management
Provisioning
IoT Hub Gateway HTTPS, AMQPS
Data and Command Flow
Per-device command queues
Event Hub
Self-Hosted Gateway MQTT, Custom
Field Gateway OPC UA, CoAP, AllJoyn, …
Cloud
Field
M
M
M
APIs
OSS Device Agents
Management
Communication
Provisioning

## Slide 32: Azure IoT Hub
HTTPS AMQPS
IoT Hub
Identity Registry
Device Management
Provisioning
IoT Hub Gateway HTTPS, AMQPS
Data and Command Flow
Per-device command queues
Event Hub
Self-Hosted Gateway MQTT, Custom
Field Gateway OPC UA, CoAP, AllJoyn, …
M
M
M
APIs
OSS Device Agents
Management
Communication
Provisioning
Hyper-Scale Identity Registry for millions of devices per IoT Hub
Can federate identity with and via Azure Active Directory

## Slide 33: Azure IoT Hub
HTTPS AMQPS
IoT Hub
Identity Registry
Device Management
Provisioning
IoT Hub Gateway HTTPS, AMQPS
Data and Command Flow
Per-device command queues
Event Hub
Self-Hosted Gateway MQTT, Custom
Field Gateway OPC UA, CoAP, AllJoyn, …
M
M
M
APIs
OSS Device Agents
Management
Communication
Provisioning
Native support for Service Assisted Communication model, potentially holding millions of concurrent bi-directional connections.
AMQP 1.0 (with WebSockets), HTTP/2
Secure by Principle.
IoT Hub does not permit insecure connections. TLS is always enforced.
TLS/X509 initially; TLS/PSK & TLS/RPK on roadmap for compute-constrained devices and bandwidth limited or expensive metered links.

## Slide 34: Azure IoT Hub
HTTPS AMQPS
IoT Hub
Identity Registry
Device Management
Provisioning
IoT Hub Gateway HTTPS, AMQPS
Data and Command Flow
Per-device command queues
Event Hub
Self-Hosted Gateway MQTT, Custom
Field Gateway OPC UA, CoAP, AllJoyn, …
M
M
M
APIs
OSS Device Agents
Management
Communication
Provisioning
Channel-level authentication and authorization against the gateway
Validation of signatures against identity registry and blacklists (for signature tokens)
All messages are tagged with originator on service side allowing detection of in-payload origin spoofing attempts

## Slide 35: Azure IoT Hub
HTTPS AMQPS
IoT Hub
Identity Registry
Device Management
Provisioning
IoT Hub Gateway HTTPS, AMQPS
Data and Command Flow
Per-device command queues
Event Hub
Self-Hosted Gateway MQTT, Custom
Field Gateway OPC UA, CoAP, AllJoyn, …
M
M
M
APIs
OSS Device Agents
Management
Communication
Provisioning
Device management foundation capabilities for device state inventory and update delivery
Device management foundation capabilities for device state inventory and update delivery

## Slide 36: Roadmap

## Slide 37: IoT Challenges
Policies, Procedures, Guidance
Cost pressure on device hardware
  Cheap sensors
  Weak/no crypto
  Source of randomness
Analog Gap
  Manipulations difficult to detect
Insecure Platforms
  Tiny Real-Time Operating Systems
  Legacy Protocols
Cloud
Field Gateways
Devices
Physical
Global Network
Identity and Access Control
Application
Data
Physical
Physical
Local Network
Local Network
Edge
Application
Data
Data
Host
Host
Host

## Slide 38: What can we do architecturally?
Service Assisted Communication
  Reduce the attack surface area for system and devices
  Only accept commands to the device from a “trusted source”
  Enforce secure channel
Machine Identity and Access Authorization
  Who is part of a system and gets to submit data?
  Authorize the sender
Data Streams and Processing Authorization
  Which data gets sent and who is authorized to process which data?
  Authorize the receiver
Data Plausibility and Flow Authorization
  What is the data quality and how plausible is it considering the system context? Is it plausible enough to permit it flowing further into the system and for it to influence decisions?
  Authorize the data stream
Data Attestation, Lineage, and Privacy Control
  Where did data originate, who participated in producing it, and how can we answer these questions only in an authorized context and break the associations altogether when required by policy or law?
  Authorize identification and association
STRIDE
STRIDE
STRIDE
STRIDE
STRIDE

## Slide 39: Call to Action!
IoT Security is a shared responsibility
  Security concepts to the edge
  Device code, provisioning, certificates, data management
Implement a Secure Development Lifecycle
  http://microsoft.com/sdl
  Keep track of the cyber supply chain
  Work out an incident response plan that includes updates
Leverage industry best practices for defense-in-depth
  Select device platforms by best balance between feature and security capabilities for your scenario and budget.
  Leverage best practice network design, but don’t just trust the network.
  Establish security boundaries at the application layer

## Slide 40: Call to Action!
Build on the Azure IoT Suite and IoT Hub
  Secure, Service Assisted, Bi-Directional Communication
  Hyper-Scale Device Identity Management
  Device Management Foundation
Review our platform principles and certifications
  Azure Trust Center http://azure.microsoft.com/en-us/support/trust-center/
ISO 27001/27002
SOC 1/SSAE 16/ISAE 3402 and SOC 2
Cloud Security Alliance CCM
FedRAMP
FISMA
FBI CJIS (Azure Government)
PCI DSS Level 1
United Kingdom G-Cloud
Australian Government IRAP
Singapore MTCS Standard
HIPAA
CDSA
EU Model Clauses
Food and Drug Administration 21 CFR Part 11
FERPA
FIPS 140-2
CCCPPF
MLPS

## Slide 41: Resources
Improve your skills by enrolling in our free cloud development courses at the Microsoft Virtual Academy.
Try Microsoft Azure for free and deploy your first cloud solution in under 5 minutes!
Easily build web and mobile apps for any platform with AzureAppService for free.