## Slide 2: Cluster in a Box in 2013: How Real Customers Are Making Their Businesses Highly-Available with Windows Server 2012
John Loveall
Principal Program Manager
Microsoft
MDC-B336

## Slide 3: Agenda
Cluster in a Box: Why “CiB”?
What new CiB solutions are available in 2013?
Customers and CiB
What’s new for CiB in Windows Server 2012 R2?

## Slide 4: Cluster in a Box Volume Platform for Availability

## Slide 5
Looking back to Windows Server 2012
“Continuous Availability” identified by customers as critical
Problem: High-Availability server hardware is costly and too difficult to buy, install, and manage.
Major investments made throughout Windows Server
Solution: “Cluster in a Box” (CiB) program
Microsoft works with our hardware partners to enable their release of new highly-available systems for a volume market

## Slide 6
“Windows Server 2012 – can you say
cloud?”
– Richard Fichera, Forrester Research
Windows Server 2012: “Takes your breath away… Features will be a boon for enterprises creating private clouds.”
– Jonathan Hassel, Computerworld
200+ customers participated in Windows Server TAP
“Comprehensive and DEEP.”
- Al Gillen, IDC
175,000+ Beta downloads
“Server 2012 is as big a leap over 2008 R2 as 2008 R2 was over 2003.”
– Trevor Pott, The Register

## Slide 7: Customer demand for Continuous Availability
Customer Focused Design (CFD) & Areas of Investigation
22 Areas of Investigation
200 Customer Focused Design Sessions
900+ Customer Prioritized Buckets
6000+ Voice of the Customer Statements
Continuous availability of the OS, applications, and data was ranked by customers WW (US, Germany and Japan) as a must have feature
2+ years of research
6,000+ customers

## Slide 8
Target markets for Cluster in a Box solutions
SMB
Branch
Private Cloud
High Availability
Simple OOBE
Storage Spaces configurations
HW RAID capability
SSD perf capability
Optional JBOD
storage expansion
Cluster in a Box
JBOD storage
Single node servers
Extended scale out
Advanced replication
Advanced power management
Advanced performance options
…
Storage Arrays
(iSCSI/FC, SMB/NFS)
Scale out Server Cluster
$$
IT Expertise
IT Generalist
PB 1 - 3
IT Specialist
PB 4+
Features
Extending the market for Continuous Availability
New systems expand choices of cost and features
Existing markets
Market expansion with CiB

## Slide 9: Cluster in a Box design considerations
Availability
At least one node and storage always available, despite failure or replacement of any component
Dual power domains
Simplicity
Pre-wired, internal interconnects between nodes, controllers, and storage
Flexibility
PCIe slots for flexible LAN options
External SAS ports for JBOD expansion
Office-level power, cooling, and acoustics to fit under a desk
Server Enclosure
Additional JBODs …
B ports
A ports
Server B
Server A
x8 PCIe
x4 SAS
External JBOD
x8 PCIe
x4 SAS
1/10G E or Infiniband
1/10G E or Infiniband
B ports
A ports
SAS Expander
SAS Expander
23
…
1
0
Network
Network
23
…
1
0
SAS Expander
Storage Controller
CPU
SAS Expander
Storage Controller
CPU
x8 PCIe
x8 PCIe
x4 SAS (through midplane)
1/10G Ethernet cluster
connect (through midplane)
Design Example (with Direct-Attached SAS)

## Slide 10: CiB Component Guidelines*
Virtualization Appliance
Entry to Medium configurations: Single CPU/node
Performance with Dedup
  Consider 2nd CPU for large, active datasets (>1GB/s throughput)
PCIe
  Entry: 1 available x8 slot
  Performance: 2-3 available x8 slots
CPU
Drives
Network
Entry: 8 cores (per server node)
For large capacity: 16+ cores (per server node)
PCIe
    Entry to medium capacity: 1 available x8 slot
Recommend 64GB per node
    Entry configuration: 32GB
Consider additional memory for large, active datasets (>1GB/s throughput)
Entry: 128GB
For large capacity: >128GB
SAS
Entry: HDDs acceptable
Recommend addition of SSDs
SAS
HDDs acceptable
Consider SSDs for I/O intensive workloads
Heartbeat connection
  Recommend 10GbE
  Entry: 1GbE
External
  10+GbE or IB, with RDMA
  2x per server node
Heartbeat connection
  Recommend 10GbE
  Entry: 1GbE
External
  Entry: 2x 1GbE
  Large capacity: 2x 10GbE (also for scale out scenarios)
Storage Server
* Note: These are guidelines only. System results are significantly dependent on the specific workloads and overall system configurations.
Memory

## Slide 11: What new CiB solutions are available in 2013? Partner updates, announcements, and launches

## Slide 12
Windows Server 2012: The starting line
Initial CiB products under development from HP, Fujitsu, Quanta, and WiWynn
Partnerships announced with leading storage platform providers
Clustered RAID controller under development from LSI
Partnerships announced with leading platform component providers

## Slide 13: Windows Server 2012 CiB products launch

## Slide 14: Product updates for 2013
LSI
Fujitsu
Quanta
Violin
?HP
Partner | Status | Product
Quanta | Released | 
 | Released | 
 | Released | 
Quanta Mesos CB220
Windows Storage Server
HP StoreEasy 5530
Windows Storage Server
Fujitsu Cluster-in-a-box based on BX400

## Slide 15: Product updates for 2013, continued
Partner | Status | Product
Quanta | Released | 
 | Evaluation | 
WiWynn SV330
Windows Storage Server
Fujitsu Cluster-in-a-box based on CX420

## Slide 16: Announcing at TechEd 2013…
Partner | Status | Product
Quanta | Announcing | 
 | Announcing | 
sTec™ s3000 storage appliance
Windows Storage Server
Violin VM6000
Windows Storage Server

## Slide 17: Announcing at TechEd 2013…
Partner | Status | Product
Quanta | Announcing | 
 | Announcing | 
DataON Cluster in a Box
DNS-9220
DNS-9470
Windows Storage Server
X-IO File Storage Controller 2200
Windows Storage Server

## Slide 18: Announcing at TechEd 2013, continued
Quanta | Windows Server Cluster in a Box Solution partner Hitachi “CiBS-12/24” prototype under development
 | Windows Server Cluster in a Box Solution partner

## Slide 19: Launching at TechEd 2013…
LSI
Fujitsu
Quanta
Violin
?HP
LSI Syncro CS
High-availability, clustered RAID controller for Windows Server 2012
Graphics by LSI Corporation

## Slide 20
Clustered RAID controllers
Meeting Windows Server requirements
Function | Goals | Requirement
RAID | Continue operation with single-component failures and robust handling of node failure, without data loss | RAID levels 1, 5, 6 or 10 (or equivalent) RAID “write hole” solution
Windows Failover Clustering | Continuous Availability depends on Windows Failover Clustering to survive node failure | SPC-3 Persistent Reservation support Shared LUNs accessible from all nodes
LUN access after failover | Transparent failover at the application layer requires data integrity and prevention of read/write timeouts | Preserve data for all acknowledged writes 5 seconds maximum blocking time for up to 100 LUNs All I/O requests must complete within 25 seconds
Minimum active mode | Customer expectation is active use of all nodes | Dual-Active (non-shared LUN access)
Recovery Processing | Transparent failover should not require IT admin attention to continue normal operation | Recovery processing resulting from node failure completes automatically
Server Enclosure
Additional JBODs …
B ports
A ports
Server B
Server A
x8 PCIe
x4 SAS
External JBOD
x8 PCIe
x4 SAS
1/10G E or Infiniband
1/10G E or Infiniband
B ports
A ports
SAS Expander
SAS Expander
23
…
1
0
Network
Network
23
…
1
0
SAS Expander
Storage Controller
CPU
SAS Expander
Storage Controller
CPU
x8 PCIe
x8 PCIe
x4 SAS (through midplane)
1/10G Ethernet cluster
connect (through midplane)
Design Example (with Direct-Attached SAS)
LSI Syncro CS application in Cluster in a Box

## Slide 21: Launching at TechEd 2013…
Dell PowerEdge VRTX
4-node Windows Server Cluster in a Box
Office level acoustics and power
Graphics by Dell

## Slide 22: Cluster in a Box in 2013 Building the vision of availability “wherever you buy a server”
All logos trademarks or registered trademarks of the respective partners
Quanta Mesos CB220
HP StoreEasy 5530
Fujitsu PRIMERGY BX400
WiWynn SV330
Fujitsu PRIMERGY CX420 S1
Violin VM6000
sTec s3000
Dell PowerEdge VRTX
X-IO FSC2200
DataON DNS-9470
DataON DNS-9220

## Slide 23: Customers and Cluster in a Box

## Slide 24: Case study: Edgenet
“Branch in a Box” scenario
Quanta CB220 Cluster in a Box with LSI Syncro CS
Video by LSI Corporation and Edgenet, Inc..

## Slide 25: Edgenet profile
Manages and distributes product information
  Covering over 4,000 companies, 8,000 brands and 6,000,000+ products
Customers: Top retailers, distributors, suppliers
  Offices in Atlanta, Nashville and Milwaukee
Maps by Bing

## Slide 26: Edgenet branch office application
Workload and environment
Domain Controllers – DNS, DHCP
Print Server
Visual Studio Team Foundation Server Proxy
Win 7 & Win 8 Workstations
SQL 2012 Server
IIS server
RedHat Linux Server
Existing implementation
2 – Dell R610 1U servers – Hyper-V
1 – HP EVA 4400 – Base 12 drives
2 – 8 Gb FibreChannel switches
Cluster in a Box implementation
1 – Quanta CB220
with LSI Syncro CS
Windows Server 2012

## Slide 27: Targeted customer scenarios
“Branch in a Box”
Virtualization Appliance
“Business in a Box”
Virtualization Appliance
Cloud/Datacenter
Storage Server
Part-time (IT not primary job function)
Generalist
May get assistance from VAR
Office environment equipment room
ISP network connection
Hyper-V appliance supporting all business apps and data, e.g., point of sale, inventory, documents/records
Doctor’s office
Individual retail store
Lawyer’s office
Design / Architecture consulting office
Centralized at HQ
Primarily remote support
Local assistance as required
Office environment equipment room
Domain-connected to main office
Hyper-V appliance running replicated branch workloads, with LOB applications, file server, and cached data
Retail chain stores
Bank branches
Specialists
Onsite and remote
Highly leveraged (expensive resource)
Enterprise equipment room
Switched network
High-performance NAS server supporting variable workloads, hosted LOB apps and data
Cloud solution builders
Hosters
Enterprise datacenters
IT Admin
Infrastructure
Workload
Examples

## Slide 28: Solution spotlight: Dell PowerEdge VRTX
“Business in a Box”
“Branch in a Box”
Virtualization Appliance
Remote and branch offices
Government
Small business & healthcare
Retail & hospitality
Education
Affordably extends the datacenter with centralized control
Address datacenter sprawl while empowering remote users and agencies
Power the office with better performance, manageability, reliability and security
Real-time and reliable management of every part of the business
Empower points of education with security and governance
Graphic by Dell

## Slide 29: Example customer applications Dell PowerEdge VRTX
“Business in a Box”
“Branch in a Box”
Graphics by Dell

## Slide 30: Example customer applications Dell PowerEdge VRTX, continued
“Business in a Box”
“Branch in a Box”
Graphics by Dell

## Slide 31: Solution spotlight: Flash-based Cluster in a Box solutions
Graphics by Violin Memories
Violin VM6000
Windows Storage Server
Partner focusing on customer scenarios demanding the highest levels of performance
Cloud/Datacenter
Storage Server

## Slide 32: Solution spotlight: Flash-based CiB solutions, continued
Graphics by sTec
sTec™ s3000 storage appliance
Windows Storage Server
Partner focusing on specific customer use cases demanding the highest levels of performance
Cloud/Datacenter
Storage Server

## Slide 33: What’s new for CiB in Windows Server 2012 R2?

## Slide 34: Windows Server 2012 R2 Cluster in a Box
Simple Guidance for Hardware Partners
Opportunity for Customers
Preserves hardware design investment
Extends value to new configurations
  Build on the same hardware platform
  Certify against the same requirements
  Release with Windows Server 2012 R2
    Supports new configurations
    New features enhance customer scenarios
  Watch for more solutions coming to market
  Evaluate new hardware configurations enabled using Windows Server 2012 R2

## Slide 35: Windows Server 2012 R2 Cluster in a Box
Build on Windows Server Cluster in a Box as the volume platform for availability
Leverage these Windows Server 2012 R2 features to deliver up to 4 node systems with enhanced storage and scale-out capabilities
Storage Spaces clustering enhancements (parity, SSDs)
Scale-out File Server rebalancing
SMB performance and per-share scale out
OOBE 4–node support
Deduplication optimized for VDI on CSV
Cloud/Datacenter
“Business in a Box”
“Branch in a Box”
Windows Storage Server 2012 R2
Virtualization Appliance
Target the primary Cluster in a Box customer scenarios

## Slide 36: Key new scenarios: Storage Spaces clustering enhancements
New clustered configurations using Parity Spaces and/or SSDs
Storage Spaces clustering enhancements (parity, SSDs)
Scale-out File Server rebalancing
SMB performance and per-share scale out
OOBE 4–node support
Deduplication optimized for VDI on CSV
Cloud/Datacenter
“Business in a Box”
“Branch in a Box”
Windows Storage Server 2012 R2
Virtualization Appliance
Spaces pool
Mirrored Space
Windows Server 2012
Spaces pool
Mirrored Space
Parity Space
Windows Server 2012 R2
SSDs
HDDs

## Slide 37: Example configurations Building on Storage Spaces clustering enhancements
Configuration #1: Capacity optimized
All HDDs
  12 drives, single pool, two 8 column, single parity Spaces, or
  24 drives, single pool, four 8 column, single parity Spaces
  (all interleave 256)
87% effective drive capacity
vs. 50% for 2-way mirrored Spaces
Spaces pool
Parity Space
All HDDs
Parity Space
Windows Failover Cluster

## Slide 38: Configuration #1: Capacity optimized Example implementations
Quanta MESOS CB220 (Value SKU)
  Per blade
  2 x Intel(R) Xeon(R) E5-2630 @ 2.3GHz
  128GB memory
  LSI SAS Adapter 9207-8i
  (2) 2.5" internal SATA for OS installation
  Drives
  (12) SEAGATE ST9300605SS, 10K RPM
  or
  (24) SEAGATE ST9300605SS, 10K RPM
  with JBOD
Load | Block Size | IOPS | MB/s
Sequential Read | 256K | 3484 | 871
Sequential Write | 256K | 212 | 53.0
Random Read | 8K | 3415 | 26.7
Random Write | 8K | 170 | 1.33
* Note: Results are examples only – performance will vary with configurations and workloads. Workload is SQLIO Disk Subsystem Benchmark Tool, available at http://www.microsoft.com/en-us/download/details.aspx?id=20163
Load | Block Size | IOPS | MB/s
Sequential Read | 256K | 3790 | 947
Sequential Write | 256K | 240 | 60.0
Random Read | 8K | 5608 | 43.8
Random Write | 8K | 274 | 2.14
12 HDDS
24 HDDs
Per node performance results*

## Slide 39: Example configurations Building on Storage Spaces clustering enhancements
Configuration #2: Balanced
Using SSDs for write-back cache
HDDs + SSDs
  10 HHDs + 2 SSDs, single pool, two 8 column, single parity Spaces
  or
  22 HHDs + 2 SSDs, single pool, four 8 column, single parity Spaces
    (all interleave 256)
Approximately 8x improvement in random write performance over HDD-only configuration
    Balanced for random write performance
Spaces pool
HDDs
SSDs
Parity Space
Parity Space
Windows Failover Cluster

## Slide 40: Configuration #2: Balanced Example implementations
Quanta MESOS CB220 (Value SKU)
  Per blade
  2 x Intel(R) Xeon(R) E5-2630 @ 2.3GHz
  128GB memory
  LSI SAS Adapter 9207-8i
  (2) 2.5" internal SATA for OS installation
  Drives
  (10) SEAGATE ST9300605SS, 10K RPM
  or
  (22) SEAGATE ST9300605SS, 10K RPM
  with JBOD
  (2) OCZ TALOS2, 200GB
Load | Block Size | IOPS | MB/s
Sequential Read | 256K | 3091 | 773
Sequential Write | 512K | 431 | 107
Random Read | 8K | 2272 | 17.7
Random Write | 8K | 1752 | 13.68
Per node performance results*
Load | Block Size | IOPS | MB/s
Sequential Read | 256K | 3666 | 916
Sequential Write | 256K | 926 | 231
Random Read | 8K | 4228 | 33.0
Random Write | 8K | 2065 | 16
10 HDDs
2 SSDs
22 HDDs
2 SSDs
* Note: Results are examples only – performance will vary with configurations and workloads. Workload is SQLIO Disk Subsystem Benchmark Tool, available at http://www.microsoft.com/en-us/download/details.aspx?id=20163

## Slide 41: Cluster in a Box calls to action
Understand your plans for high-availability servers
Investigate new CiB solutions
  Current configurations that can benefit from R2 features
  New configurations enabled by R2
Participate in Windows Server 2012 R2 early evaluation opportunities
  Evaluate Preview release to validate scenarios
Provide feedback on what works and what doesn’t work for your business
  We’re are developing additional customer case studies

## Slide 42: CiB partner information
Partner | Product | Contact / Reference
DataON | DataON DNS-9220/9470 CiB | http://www.dataonstorage.com/cluster-in-a-box.html
Dell | Dell PowerEdge VRTX | www.dell.com/poweredge/vrtx
Fujitsu | Fujitsu Cluster in a Box based on BX400 or CX420 | www.Fujitsu.com
Hitachi | Hitachi “CiBS-12/24” | www.hitachi.com
HP | HP StoreEasy 5530 | www.hp.com
LSI | LSI Syncro CS | www.TheSmarterWayToOn.com
Quanta | Quanta Mesos CB220 | www.QuantaQCT.com
sTec | sTec s3000 storage appliance | www.stec-inc.com
Violin Memory | Violin VM6000 | www.vmem.com
X-IO | X-IO File Storage Controller 2200 | xiostorage.com/products/FSC-2200
WiWynn | WiWynn SV330 | www.wiwynn.com/en/ps_01.html#anchor9
Microsoft | Developer information and contacts for CiB | http://technet.microsoft.com/en-us/windowsserver/jj542413.aspx
Edgenet | Customer case study | http://www.edgenet.com

## Slide 43: Cluster in a Box in 2013 Building the vision of availability “wherever you buy a server”
Quanta Mesos CB220
HP StoreEasy 5530
Fujitsu PRIMERGY BX400
WiWynn SV330
Fujitsu PRIMERGY CX420 S1
Violin VM6000
Dell PowerEdge VRTX
X-IO FSC2200
All logos trademarks or registered trademarks of the respective partners
sTec s3000
DataON DNS-9470
DataON DNS-9220
Building the vision of availability “wherever you buy a server”

## Slide 44: Related content
Breakout Sessions
  MDC-B218 Storage Spaces: What’s New In Windows Server 2012 R2
  MDC-B394 Shouldn’t All of Your Storage Be Highly Available?
  MDC-B305 Continuous Availability: Deploying and Managing Clusters Using Windows Server 2012 R2
  MDC-B335 Understanding the Hyper-V over SMB Scenario, Configurations, and End-to-End Performance
  MDC-B337 Failover Cluster Networking Essentials
  MDC-B349 Upgrading the Platform - How to Get There! Part 4: Your Fileservers and Storage Options
  MDC-B342 Reduce Storage Costs with Data Deduplication

## Slide 45: Track resources
Learn more about Windows Server 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/WS2012R2
Learn more about System Center 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/SC2012R2

## Slide 46: Resources
msdn
  Resources for Developers
http://microsoft.com/msdn
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
TechNet
  Sessions on Demand
http://channel9.msdn.com/Events/TechEd
  Resources for IT Professionals
http://microsoft.com/technet

## Slide 47: Evaluate this session
Scan this QR code to
evaluate this session.
Required Slide
*delete this box when your slide is finalized
Your MS Tag will be inserted here during the final scrub.

## Slide 48
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.