## Slide 2: Intel and Microsoft Software-Defined Networking Initiatives and Platforms
Glenn Ward
MDC-B346

## Slide 3: Session Objectives and Takeaways
Session Objective(s)
  Understand the key needs in cloud networks
  Understand the value of Network Virtualization in building scalable multi-tenant clouds
  Understand the Intel strategies and component technologies for Software Defined Networking
Key Takeaways
  Network Virtualization is deployable in today’s datacenter
  Network Virtualization revolutionizes multi-tenant clouds (private, hybrid, public)
  Software Defined Networking brings datacenter flexibility, control, & automation

## Slide 4: Evolution of the datacenter
Intel® Virtualization Technology (introduced in 2005)
Increased scalability
Increased virtualization capability
Dedicated
Servers
Windows Server* 2003
Intel® Xeon® processor (Single-core)
10 years ago
Server Virtualization
VM
VM
VM
Windows Server 2008
Intel Xeon processor (Quad-core)
5 years ago
Cloud
VM
VM
VM
VM
VM
VM
Windows Server 2012
Intel Xeon processor (8 plus-core)
Today

## Slide 5: Growth & IT challenges drive need for cloud computing
1 Cisco Global Cloud Index Nov 2011
2 IDC Extracting Value from Chaos June 2011
3 Intel ECG – One Smart Network device forecast
4 Cisco Visual Networking Index: Global Mobile Data Traffic Forecast Update, 2011–2016, Feb 2012
5 Datacenter Dynamics Global Datacenter Energy Demand 2012 forecast http://www.datacenterdynamics.com/research/energy-demand-2011-12; projected to 2015 by Intel; Assume $0.10/kWh
15B connected devices by 20153
>3B connected users by 20151
Up to 2X or $27B5
in additional power costs by 2015
>11X
increase in mobile data traffic by 20154
2X growth in information every two years2
Growth
IT Challenges
Avoid Lock-In
Seek interoperable solutions & services
Improve Agility Reduce service delivery times, improve TCO
Greater Efficiencies Reduce complexity & deploy new workloads
Gain Better Insights
Via intelligent analytics

## Slide 6: Cloud adoption growing & delivers benefits
Resource provisioning
Virtualized Platforms
Asset Utilization
Capacity
Traditional IT – 2009
Private cloud - 2011
90 days
45 minutes
12%
65%
10-20%
>60%
Silos
Shared globally
$9M in savings in 2 years
Cost Savings
1 ODCA global member survey, Oct 2011, N=63
2 Gartner, Dec 2010, N=55 The Road Map From Virtualization to Cloud Computing (G00210845)
3 Source: Intel IT- http://premierit.intel.com/docs
Intel IT example3
    Public Cloud
    Private Cloud
    Hybrid Cloud
35% by 20152
Today: 7%
2014: 23%
Today: 14%
2014: 42%
IT Survey Results
>40% of IT operations1
>40% of IT operations1
    Public Cloud
    Private Cloud

## Slide 7: Barriers to cloud adoption
Compliance
Quality of Service
Lock In
Risk Aversion
Structure
New roles
Skills development
Cultural/
Organizational
Scaling the Infrastructure
Security
Scale & Automation
Standards
Technology Maturity
Unpredictable demand
Space/power constrained
Massive data growth
Inflexible, hard to scale
Lack flexibility
Complex management
Servers
Networking
Storage
Resource Orchestration: Complex/management silos
Cloud Security: Lack of control, manual auditing, identity theft

## Slide 8: Evolving datacenter capabilities
SSD and NVM for low latency/high bandwidth
Server
Performance & efficiency optimized
Storage
Scalable converged storage servers + storage apps
Enhanced distributed storage & file systems, erasure code
Add’l core data protection
NVM acceleration
Data mgmt optimizations
Increasing application performance, reliability, scale, serviceability
Dynamic integrity assurance and recovery
Security
Automated controls, data protection, multi-tenant
Increased intelligence on platform & VM resource usage /optimizations
Orchestration
Automated density/ efficiency
10GbE Unified Networking
Virtualization
Network
Programmable network equipment, open interfaces
10/40/100GbE platform with CPU based network apps
2012
2013
2014
Programmable control plane & 10/40GbE ToR switch
Management APIs
Hardware-based data and multi-tenant workload integrity
DC efficiency and density tuning via deep power and resource usage instrumentation

## Slide 9: Windows Server 2012 R2 Cloud optimize your IT
Build on an open and scalable web platform that supports applications across premises.
Support a mobile and flexible work style.
Scale and secure workloads, cost-effectively build a private cloud, and securely connect to cloud services.
Efficiently manage infrastructure while maximizing uptime and minimizing failures and downtime.
Every app, any cloud
Modern workstyle, enabled
Beyond virtualization
The power of many servers, the simplicity of one

## Slide 10: Transforming the network for the cloud
Deliver networking as part of pooled, automated infrastructure
Expand datacenter capacity seamlessly as per business needs
Reduce operational complexity
Ensure multitenant isolation, scale and performance

## Slide 11: What is Software-defined Networking (SDN)?
Abstracting the physical network with virtual networks
Spanning policies across physical and virtual networks
Controlling datacenter traffic flow
Enables software to dynamically manage the network

## Slide 12: Microsoft’s approach to SDN
End-to-end solution
Promote industry innovation in software & hardware
Open, extensible and standards-based
Automation
Flexibility
Control

## Slide 13: Delivering on SDN with Windows Server & System Center
Dynamic, policy-driven network (re)configuration
Consistent, profile-based deployment of SDN traffic policies through distributed virtual switch
Provision load balancers, site-to-site VPNs and gateways
Integrated control plane to co-relate workload placement and virtual network policy
Dynamic traffic control policies with Network QoS
Traffic monitoring and flow control with switch extensions
Virtual network abstraction with multitenant isolation
BYOIP for tenant onboarding & workload mobility
Secure cross-premises connectivity
Flexibility
Control
Automation

## Slide 14: Application storage support – SMB 3.0
  Highly available, shared data store for SQL Server databases and Hyper-V workloads.
  Increased flexibility, easier provisioning and management.
  Ability to take advantage of existing network infrastructure.
  No application downtime for planned maintenance or unplanned failures with failover clustering.
  Near line rate performance for both small and large IOs.
  Can work with existing storage investments.
  Built-in encryption support.
File server cluster
Cluster shared volumes
Single file system namespace
SMB
Single logical server \\foo\share
RAID array
RAID array
RAID array
SAN
Hyper-V cluster
ENTERPRISE-CLASS FEATURES ON LESS EXPENSIVEHARDWARE
Windows virtualized storage
Tiered physical storage
Storage pool
Storage pool
Storage space
Storage space
Storage space
SSD
HDD
Microsoft SQL Server

## Slide 15: Using the speed of 10Gb Ethernet for storage
Shared
Storage
Hyper-V Cluster
File Server Cluster
Server Message Block (SMB) 3.0
Store Hyper-V files in shares over the Server Message Block (SMB) 3.0 protocol
Works with both standalone & clustered servers
Automatic configuration to detect and use multiple paths
Highlights
Increases flexibility
Eases provisioning, management & migration
Leverages converged network
Reduces CapEx and OpEx
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark* and MobileMark*, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products.
Hyper-V
Hyper-V
Hyper-V
SQL
Server
IIS
VDI
Desktop
SQL
Server
IIS
VDI
Desktop
SQL
Server
IIS
VDI
Desktop

## Slide 16: Sharing the load get 10Gb per second performance
  Only one TCP/IP connection
  Only one CPU core engaged
  Receive Side Scaling (RSS) helps distribute load across CPU cores
With Multichannel
Without Multichannel
CPU utilization per core
Core 1
Core 2
Core 3
Core 4
CPU utilization per core
Core 1
Core 2
Core 3
Core 4
Can’t use full 10Gbps
Full 10Gbps available

## Slide 17: Combining LBFO teaming with multichannel for SMB 3.0
LBFO
LBFO
NIC Teaming with LBFO With Multichannel
NIC Teaming with LBFO Without Multichannel
Automatic NIC failover
But…
Can’t use full bandwidth
Only one NIC engaged
Only one CPU core engaged
Automatic NIC failover
With…
Combined NIC bandwidth available
Multiple NICs engaged
Multiple CPU cores engaged
LBFO
LBFO

## Slide 18: Server Message Block (SMB) 3.0 multichannel performance
Chart: SMB Client Interface Scaling - Throughput
| 512 | 1024 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
1 x 10GbE | 156.8149 | 226.1836 | 687.6917 | 875.673 | 1124.8726 | 1138.7496 | 1128.3732 | 1163.7644 | 1164.9838 | 1170.0508 | 1154.3338
2 x 10GbE | 162.0595 | 322.3353 | 1224.7526 | 2116.9096 | 2334.7591 | 2337.8289 | 2307.9321 | 2305.1336 | 2324.7594 | 2313.7383 | 2332.6083
3 x 10GbE | 161.8836 | 321.1907 | 1238.7885 | 2410.8725 | 3131.6209 | 3329.5767 | 3326.9938 | 3190.6087 | 3147.5608 | 3139.8305 | 3123.3739
4 x 10GbE | 161.5843 | 315.5044 | 1232.7342 | 2397.5162 | 3211.4626 | 3978.5875 | 4234.7012 | 4307.2203 | 4303.5958 | 4265.05 | 4231.0107
Source: Microsoft Sept 2012 white paper provides full details See http://go.microsoft.com/fwlink/p/?LinkId=227841
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark* and MobileMark*, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products.

## Slide 19: Comparing networking connections physical vs. virtualized servers
PG -A
PG -B
PG - Storage
PG - vMotion
PG - Mgmt
Access Switch
Server Adapters
Servers/Storage
Switch Uplinks
Aggression Switch
Physical Servers
Virtualized Servers
Microsoft* Windows Server 2012 with Hyper-V
VM
VM
Management OS
VMBus
Virtual Switch
VMBus

## Slide 20: Windows Server 2012 Virtual Switch Features
Tenant Isolation
Traffic Shaping
Security
Performance
Diagnostics
Port ACL
PVLAN
Trunk mode
Bandwidth Minimum
Bandwidth Cap
DHCP Guard
Router Guard
IPsec Task Offload
Dynamic VMQ
Port Mirroring
Event Tracing (ETW)
Unified Tracing (UT)
Network Controllers
Stateless Offloads
Virtual Machine Queues
SR-IOV Hypervisor Bypass

## Slide 21: Microsoft* Windows* Server 2012 with Hyper-V* provides multiple options for 10GbE networking
Intel® Ethernet with VT-c Support
PCI Express
Virtual Ethernet Bridge and Classifier (L2 Switch)
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Virtual Function
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
VMQ1 Queue
1PCI-SIG Single Root I/O Virtualization and Sharing (SR-IOV)
Dynamic Virtual Machine Queues (DVMQ)
Example: VM1 is traffic is assigned to VMQ1
SR-IOV1 for VM Direct Assignment
Example: VM2 is directly assigned to a virtual function
Windows Server
VM 2
VM 1
Hyper-V
Parent Partition
Child Partitions
Virtual Service Provider (VSP)
VSC
VMBus
Virtual Machine Bus (VMBus)
Windows Kernel
Miniport Driver
Windows Kernel
VSC
Windows Kernel
Miniport VF Driver
Intel® VT-d
Virtual Function
VMQ2
Queue
Default
Queue

## Slide 22: Higher throughput & lower CPU utilization Intel® Ethernet Converged Network Adapter X520 using SR-IOV in Microsoft* Windows* Server 2012 with Hyper-V
Using SR-IOV can
improve Performance
SUT Configuration |  | Client Configuration |  |  |  | 
Platform | Intel® Server Board S2600GZ | Client Platform | Supermicro* 6016TT-TF (10GbE clients) |  |  | 
OS | Windows Server 2012 Hyper-V | OS | Windows Server 2008 R2 x64 |  |  | 
Processor | Intel® Xeon® processor E5-2690 (8C/16T, 20M Cache, 2.90 GHz, 8.00 GT/s Intel® QPI) | Processor | Intel® Xeon® Processor X5680 (12M Cache, 3.33 GHz, 6.40 GT/s Intel® QPI) |  |  | 
QPI Speed | 8.0 GT/s | Memory | 12GB DDR3 @1333 MHz |  |  | 
Memory | 128 GB @ 1333 MHz | BIOS | 2.0b |  |  | 
BIOS Version | SE5C600.86B.01.02.0006 | NIC | Intel® Ethernet CNA X520-T2 (Iron Pond) |  |  | 
NIC | Intel 82599 10 Gigabit Ethernet Controller | NIC Driver | 2.11.114.0 |  |  | 
NIC Driver | ixn63x64-3.1.42.0 | Switch Configuration |  |  |  | 
NIC EEPROM | 0x18bf0001 | Switch Type | Force10 Networks* ExaScale* E1200i |  |  | 
System Slot # | PCI Slot 2 Bus 9 | Config | Each NIC port in it's own VLAN |  |  | 
Chipset | Intel® C602 Chipset |  |  |  |  | 
BIOS Changes | Power management disabled. |  |  |  |  | 
OS / Kernel Changes | Added Hyper-V role, for the VMQ tests, SR-IOV was not enabled in the Virtual Switch |  |  |  |  | 
Notes | used 8 VMs per port, for the WS2012 tests, the VMs were WS2012 build 8400 |  |  |  |  | 
Up to
47%
Up to
26%
Reduction in CPU Utilization
(65535 Bytes)
Increase in Throughput (Mb/s)
(64 Bytes)
LAD SW Performance Lab
July 2012
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark* and MobileMark* are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products.
Intel® Ethernet Converged Network Adapter X520
Intel® Ethernet Converged Network Adapter X540

## Slide 23: Challenges of traditional networking
Increasing operational complexity
Server and network provisioning
Controlling datacenter traffic flow

## Slide 24: What is the next step?
Server virtualization
  Multiple virtual servers on a physical server
  Each VM has illusion it is running as a physical server
Network virtualization
  Multiple virtual networks on a physical network
  Each virtual network has illusion it is running as a physical network
Physical
server
Blue VM
Red VM
Blue network
Red network
Virtualization
Physical
network
VM
VM

## Slide 25: Using VLANs to isolate VM traffic
VLAN tags
Top of Rack Switch (ToR)
Aggregation Switches
Requires Network Admins to configure VLANs and Subnets
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Server Admin
Network Admin

## Slide 26: Hyper-V network virtualization benefits
To Workload Owners
Seamless migration to the cloud
Move n-tier topology to the cloud
Preserve policies, VM settings, IP addresses
To Enterprises
Private Cloud datacenter consolidation and efficiencies
Extension of datacenter into hybrid cloud
Incremental integration of acquired company network infrastructure
To Hosters
Bring Your own IP
Bring Your network topology
To Private/Public Cloud Datacenter Admins
Flexible VM placement without reconfiguration
Decoupling of server and network admin roles increases agility
Scalable multi-tenancy

## Slide 27: Standards-based encapsulation - NVGRE
Provider Addresses
Better network scalability by sharing PA among VMs
Explicit Virtual Subnet ID for better multi-tenancy support
10.0.0.5
10.0.0.5
10.0.0.7
10.0.0.7
192.168.4.11
192.168.4.22
192.168.4.11
192.168.4.22
10.0.0.5 
10.0.0.7
GRE Key 5001
MAC
10.0.0.5 
10.0.0.7
GRE Key 6001
MAC
192.168.4.11
192.168.4.22
10.0.0.5
10.0.0.7
10.0.0.5
10.0.0.7
10.0.0.5 
10.0.0.7
10.0.0.5
10.0.0.7
VM2
VM2
Customer Addresses
Virtual Switch
Virtual Switch
VM1
VM1

## Slide 28: Using NVGRE for network virtualization
Provider Network
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Encapsulated Traffic
Blue
VM1: MAC1, CA1, PA1
VM2: MAC2, CA2, PA3
VM3: MAC3, CA3, PA5
VM4: MAC1, CA4, PA7
VM5: MAC2, CA5, PA8
Red
VM1: MACX, CA1, PA2
VM2: MACY, CA2, PA4
VM3: MACZ, CA3, PA6
datacenter Policy
Green
VM1: MACa, CA1, PA1
VM2: MACb, CA2, PA2
VM3: MACc, CA3, PA5
VM4: MACZ, CA3, PA9

## Slide 29: Why is SDN important in the Cloud?

## Slide 30: Software Defined Networking
Three key virtues
  Decoupled Control and data planes are decoupled
Centralized
  Network intelligence and state are centralized
Abstracted
  Network infrastructure is abstracted from the applications

## Slide 31: Property management
Rental House
Apartment
Hotel
# of Tenants | One | Several | Many
Change | Infrequent | Occasional | Daily
$$ | Long term | Utilization, low turnover | Utilization, low OPEX
Management | Individual | Building Manager | Staff, Systems, & Automation

## Slide 32: Bringing it back to the datacenter
# of Tenants | One | Several | Many
Change | Infrequent | Occasional | Daily
$$ | Long term | Utilization, low turnover | Utilization, low OPEX
Management | Individual | Building Manager | Staff, Systems, & Automation
Dedicated
Servers
Server Virtualization
VM
VM
VM
Cloud
VM
VM
VM
VM
VM
VM

## Slide 33: Benefits of Software Defined Networking
Programmability, automation and control
  Increased scale and flexibility
  Easily adaptable to new business needs
Significant reduction in OpEx and CapEx
  Provides centralized view of the network (at large scale)
  Automates mapping of network resources to changing workflows
  Supports uniform control of multi-vendor network environments

## Slide 34: Evolution: Dis-aggregated network
Standard Switching Hardware
Standard Switching Hardware
Standard Switching Hardware
Standard Switching Hardware
Standard Switching Hardware
Operating
System
App
App
App
Operating
System
App
App
App
Operating
System
App
App
App
Operating
System
App
App
App
Operating
System
App
App
App
App
App
App
Network Controller
Dis-aggregated Control Plane
Dis-aggregated Control Plane
Dis-aggregated Control Plane
Dis-aggregated Control Plane
Dis-aggregated Control Plane

## Slide 35: Intel® Open Network Platform Switch Reference Design
SP App
OEM App
ISV App
SDN Controller
Software
HW
Intel Product
3rd Party
Wind River Product
Wind River* Open Network Software (ONS)
Hardware
Intel Communications
Chipset 89xx Series
Intel Ethernet FM6700 Switch
Intel Architecture
*Other names and brands may be claimed as the property of others.

## Slide 36: Switch silicon designed for SDN
Simultaneously supports legacy and SDN networks
Designs can be optimized for flexibility or scale
Offers flexible tagging and overlay networks
Delivers uncompromising performance
Intel® Ethernet Switch FM6000 Series

## Slide 37: Intel® FlexPipe™ Technology
Mux &
Transform
CAM
Action
RAM
Sample Programmable Protocols
Tunneling TRILL, MPLS, NAT
Network Overlays VXLAN, NVGRE
Virtualization EVB, VEPA, VEPA+, VN-Tag
Proprietary Customer defined headers
Programmable and deterministic up to 960Mpps
Modify
TCAM &
BST
L2
Lookup
L3
Actions
Global
Ports
Egress
Actions
Statistics
Nexthop
Table
CM &
Sched
Parser
Mapper
Channels
Header
Atomic Tables
Configurable Logic
Multiple Stages
Mux &
Transform
CAM
Action
RAM

## Slide 38: Using gateways to bridge virtual and physical network
Provider Network
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Encapsulated Traffic
VLAN tags
Intel® Open Network Platform Switch Reference Design
HW NVGRE gateway

## Slide 39: Standards based switch management
Automate deployment and management of both the tenant network and the hoster network
Standards based CIM model / schema to communicate with switch
CIM enabled switch

## Slide 40: Delivering Software-Defined Networking (SDN)
Windows Server 2012
  Hyper-V Network Virtualization
  Hyper-V Extensible Switch
System Center 2012 SP1
Intel® Ethernet Building Blocks
  Optimizations for Hyper-V Switch
  Network Virtualization gateways
  Intel® Open Network Platforms
Automation
Flexibility
Control

## Slide 41: Summary
Network Virtualization is deployable today
Network Virtualization revolutionizes multi-tenant clouds (private, hybrid, public)
Software Defined Networking brings datacenter flexibility, control, and automation

## Slide 42: Related content
Intel and Microsoft Server and Cloud Platform Resources
Intel white paper “Game-Changing Capability for Your datacenter—and a Solid Foundation for Your Cloud” http://www.intel.ie/content/dam/www/public/us/en/documents/white-papers/cloud-computing-xeon-e5-server-2012-paper.pdf
Intel solution brief “Microsoft Windows Server* 2012 and the Intel® Xeon® processor E5 family” http://www.intel.com/content/www/xa/en/cloud-computing/cloud-computing-xeon-e5-microsoft-server-solution-brief.html
Intel Cloud Computing Technology and Vision http://www.intel.com/content/www/us/en/cloud-computing/intel-s-cloud-computing-vision.html
Intel Cloud Computing Solutions http://www.intel.com/content/www/us/en/cloud-computing/intel-cloud-based-solutions.html
Intel® Xeon® Processor E5 Family http://www.intel.com/content/www/xa/en/processors/xeon/xeon-processor-5000-sequence.html
Microsoft* Server and Cloud Platform (Windows Server, System Center, Azure) http://www.microsoft.com/en-us/server-cloud/cloud-computing/
Microsoft Windows Server* 2012 http://www.microsoft.com/en-us/server-cloud/windows-server/
Find me at the Intel booth or on Twitter @thehevy

## Slide 43: Track resources
Breakout Sessions
MDC-B350 How to Design and Configure Networking in Microsoft System Center - Virtual Machine Manager and HyperV Part 1
MDC-B351 How to Design and Configure Networking in Microsoft System Center - Virtual Machine Manager and HyperV Part 2
MDC-B380 Deep dive on Hyper-V Network Virtualization in Windows Server 2012 R2
MDC-B216 What’s new in Windows Server 2012 R2 Networking

## Slide 44: Track resources
Learn more about Windows Server 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/WS2012R2
Learn more about System Center 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/SC2012R2

## Slide 45: Resources
msdn
  Resources for Developers
http://microsoft.com/msdn
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
TechNet
  Sessions on Demand
http://channel9.msdn.com/Events/TechEd
  Resources for IT Professionals
http://microsoft.com/technet

## Slide 46: Evaluate this session
Scan this QR code to
evaluate this session.
Required Slide
*delete this box when your slide is finalized
Your MS Tag will be inserted here during the final scrub.

## Slide 47: Summary of Intel Enablement and Optimization of Windows Server* 2012
Microsoft Pillar | Intel Technology | Windows Server* 2012 Technology | IT Benefit
Beyond Virtualization |  |  | 
Dynamic Resource Control | Virtual Machine Device Queues (VMDq) | Dynamic Virtual Machine Queue (DVMQ) | I/O virtualization with optimized balance of performance and IT control
 | PCI-SIG Single Root I/O Virtualization (SR-IOV) | SR-IOV | Alternative I/O virtualization option for lower latency and CPU utilization
Power of Many Servers, Simplicity of One |  |  | 
Continuous Availability | Machine Check Architecture (MCA) Recovery | Windows* Hardware Error Architecture (WHEA) Also supported in Hyper-V*, Microsoft SQL Server* 2012 | Recovery from uncorrectable errors for robust reliability. Delivered by Intel® Xeon® processor E7 family with MCA Recovery
 | Intel® Advanced Encryption Standard New Instructions (Intel® AES-NI) Intel® Secure Key Technology Intel® OS Guard Intel® XD Bit | Microsoft Crypto Next Generation* (CNG*) library | Fast, low-overhead encryption High-quality keys Enhanced protection from escalation of privilege attacks Secure key storage Reduce platform attack surface
Unified Networking | Fibre Channel over Ethernet (FCoE) datacenter Bridging (DCB) iSCSI with intelligent offloads | FCoE and iSCSI software initiators | Unified 10 GbE networking: High-bandwidth, low-latency Low cost Ethernet fabric
Breakthrough Storage Economics | Intel® Xeon® processor E5 family 10 Gb Intel® Converged Network Adapters NetEffect™ Ethernet Server Cluster Adapters (for RDMA) | Server Message Block (SMB) 3.0 SMB 3.0 Direct for remote direct memory access (RDMA) | SAN-like storage using low-cost file servers and disk arrays
Energy Efficiency | Intel® Intelligent Power Technology Intel® Node Manager 2.0 | Kernel optimizations Logical processor idling | 15 percent greater efficiency versus Windows Server 2008 R2 Improved power budgeting

## Slide 48: Empower Windows Server* 2012 with Intel® Xeon® Processors
Windows Server* 2012 designed for cloud-optimized IT
      A cloud-optimized IT environment with support for multitenancy, dynamic resource control, unified 10 Gb networking, and breakthrough storage economics
Intel® Xeon® processor E5 family
      Enhanced security through fast, low-overhead encryption with Intel® Advanced Encryption Standard New Instructions (Intel® AES-NI) and associated Intel security technologies
      Superior energy efficiency via Intel® Intelligent Power Technology and Intel® Node Manager 2.0
10 Gigabit Intel® Ethernet Converged Network Adapter family
      Better I/O performance via Intel® Virtualization Technology for Connectivity (Intel® VT-c) (Virtual Machine Device Queues [VMDq] and Single Root I/O Virtualization [SR-IOV])
Intel® Open Network Platform family
      Intel® Ethernet Switch silicon, reference architectures and software for SDN & network virtualization to enable the network architecture transformation

## Slide 50
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.