## Slide 2: How to Design and Configure Networking in Microsoft System Center Part 1 of 2
Greg Cusanza
Senior Program Manager, Microsoft
MDC-B350

## Slide 3: Agenda
MDC-B350: Part 1
Room: You are in it
Time: Now
What we introduced in SP1 recap
How to setup your datacenter networking from scratch
What’s new in R2
MDC-B351: Part 2
Room: Same
Time: 5:00pm
Hybrid Networking
  Configuring network fabric for Network Virtualization
  Network Virtualization Gateways
  Tenant self service

## Slide 4: VMM 2012 SP1 review
Capability
Quality of service (QOS)
Security
Optimizations
Monitors
Extensiblity
Teaming
Connectivity
Multi-tenancy
Isolation
Mobility
Bring your own IP
Result: VM Networks
Result: Logical Switch

## Slide 5: Partner Ecosystem

## Slide 6
Step One…

## Slide 7
Lots of question
Where do I start, what do I do next?
How do I offer networking to my virtualization workloads?
How do I make my network resilient to failure?
How do I provide tenant self service?
How can I provide isolation?
How do I maintain consistency in large datacenters?
Takeaways
The ability to answer these questions and configure VMM networking in your data center
Preparedness for what’s in R2

## Slide 8: Steps to a successful deployment
Design
Draw your network requirements.
Ask questions up front and get answers.
Hardware
Use hardware that supports your design.
Iterate back on your design.
Configure hardware.
VMM configuration
Create logical objects
Configure hosts
Add tenants
Deploy workloads

## Slide 9: Network Design

## Slide 10
Windows Azure Pack
Gateway
Tenant 2 VMs
Tenant 2
Tenant 1 VMs
Tenant 1
SQL
SPF, etc.
VMM
Management
Corporate
Public Internet
Network Overview
1st question: how do I provide isolation?
Datacenter isolation – separation of infrastructure traffic as security boundar and for QOS
Tenant isolation – keeping tenants from each other and protect the infrastructure
LM, Cluster, Storage
Hyper-V hosts

## Slide 11: Isolation
Physical separation
Physical switches and adapters for each type of traffic
Layer 2:
VLAN
Tag is applied to packets which is used to control the forwarding
Network Virtualization
Isolation through encapsulation. Independence from physical address space.
Layer 2:
Private VLAN (PVLAN)
Primary and Secondary tags are used to isolate clients while still giving access to shared services.

## Slide 12: One more type of isolation
Physical separation
Physical switches and adapters for each type of traffic
Layer 2:
VLAN
Tag is applied to packets which is used to control the forwarding
Network Virtualization
Isolation through encapsulation. Independence from physical address space.
Layer 2:
Private VLAN (PVLAN)
Primary and Secondary tags are used to isolate clients while still giving access to shared services.
External
Isolation is implemented by switch extension.
Technology is opaque to VMM.
All isolation types are abstracted away under a VM network

## Slide 13: VLAN Isolation
Defines a layer 2 broadcast domain, achieved by tagging packets to tell switch where it can go.
Why use?
Very mature and reliable technology
Universally adopted
Well understood
Why not?
Limited VLAN capacity on each switch and port (4095 max)
Limited machine capacity on each VLAN
Limits migration of machines
High management overhead

## Slide 14: Private VLAN (PVLAN) Isolation
Secondary
VLANs
Primary
VLAN
VLAN pairs used to provide isolation with small numbers of VLANs.
VMM 2012 SP1 and R2 only supports creation of isolated PVLAN VMs
Isolated
Promiscuous
Community
Net.Virt.

## Slide 15: Network Virtualization
10.0.1.0/24
10.0.2.0/24
Production Network
Exchange server, AD
192.168.1.0/24
Development Network
192.168.1.0/24
Network Virtualization
Gateway
Corporate
192.168.2.0/24
Physical Hosts
Customer Address
Spaces
Provider Address
Space

## Slide 16: No Isolation
Why
Provides direct access to the logical network
VMM picks the right VLAN based on placement
Upgrade to SP1
Pre-SP1 VMs have direct connectivity to the logical network by default.
Public Shared
Shared internet network.
Direct access to infrastructure
Think of the System Center in a VM scenario.

## Slide 17: Where should you use what?
Infrastructure networks
Load balancer back end and internet facing
Tenant networks
VLAN or No isolation
PVLAN
Network virtualization or
External

## Slide 18: Address spaces
Size based on broadcasts and address utilization
Can be DHCP and Static
IPv4 and IPv6
Logical network | Address space defined by | Example
Corp | Corp IT | 172.30.0.0/16
Internet | ICANN | 65.55.57.0/24
Management | Datacenter Admin | 10.0.0.0/24
Net. Virt. Provider | Datacenter Admin | 10.0.1.0/24
Cluster/Storage/etc… | Datacenter Admin | 10.0.2.0/24
Tenant N | Tenant | 192.168.1.0/24
Who
Defines
What?

## Slide 19: Hardware considerations

## Slide 20: Single root IO virtualization (SR-IOV)
Why?
Virtual switch bypass for high performance workloads
Why not?
You need bandwidth controls
Physical adapters don’t support it
Limited number of VMs that can use it per host
You lose the capabilities of the vSwitch
Must be enabled when virtual switch is created
Must be enabled as needed on port profile
Limited support for intelligent placement

## Slide 21: Remote Direct Memory Access (RDMA) Adapters
Why?
High performance access from hosts to SMB3 based file servers
Why not?
No teaming
No virtual switch
Can also be used for live migration, management, clustering

## Slide 22: Teamed Adapters Three basic patterns for configuration
Converged
10GbE each
VMN
VM1
10GbE each
Storage
Live Migration
Cluster
Manage
Non-converged
1GbE
1GbE
1GbE
10GbE
HBA/
10GbE
Storage
Live Migration
Cluster
Manage
VM1
VMN
Converged with RDMA
VMN
VM1
Storage/LM/Cluster
Management
RDMA 10GbE each
10GbE each

## Slide 23: Connecting hosts to the data center
Data center Edge
Aggregator
Switches
Access
Switches
Hyper-V Host
Virtual Switch
Team
RDMA
VM
External (Corp,
Internet, etc.)
VM

## Slide 24: VMM configuration

## Slide 25: Physical and logical in VMM In VMM
Logical Network
Models the physical network
Separates like subnets and VLANs into named objects that can be scoped to a site
Container for fabric static IP address pools
VM networks are created on logical network
Logical Switch
Central container for virtual switch settings
Consistent port profiles across data center
Consistent extensions
Compliance enforcement

## Slide 26: Creating logical networks for infrastructure demo

## Slide 27: Fabric Configuration – New in R2
All network devices* and services are now “network services”
  New interfaces
    Network manager: Separation of Virtual Switch and Network management
    Physical switch
Microsoft IPAM as a network manager
  In-box plugin for Microsoft IPAM
  Exchange logical networks, sites and subnets
*except load balancers
Network Service
Virtual Switch Extension
Network Manager
Net. Virt. Policy
Gateway
Physical Switch

## Slide 28: VMM - Microsoft IPAM integration
Fabric Layer
Network Admin
SCVMM
IPAM
VN Layer
Configure Address Space, Subnets, Pools, VLAN
Associate Host Groups to LN
Associate MAC Pools to LN
Subnets, Pools for NS / LN
LN, NS, Isolation settings…
Pool utilization, meta-data…
IP address, meta-data…
Address utilization tracking (stats & trends)
Changes – Pools, VLANs, Address and meta-data
Conflict detection, notification and updates
Compliance status
Inventory of CA space, subnets, Pools
Address utilization tracking of CA (stats & trends)
Tenants create VM Networks
Pool utilization, meta-data…
IP address, meta-data…
Subnets, Pools for VN
VMM Admin
Tenant Admin

## Slide 29: Physical Switch Management– New in R2
Plugin model for:
In-box plugin for the Standards-based (CIM) Network Switch Profile
CIM profile implemented and shipping with Arista EOS 4.12 which is a common binary across all Arista switching platforms.
Host to TOR port discovery
Port compliance
Remediation

## Slide 30: Arista switch managed by VMM

## Slide 31: Logical Switch
Why?
Automatic team creation
Configuration for DC on a single object
Compliance
Access to hyper-v port settings
3rd party extension management
Updates get applied to all hosts
Why not?
More up-front configuration
Limits live migration

## Slide 32: How the logical switch works
Logical Switch in VMM
Port Profiles
(Uplink)
Port Profiles
(Virtual)
Hyper-V host #1
Virtual Switch
Switch settings
Switch settings
Hyper-V host #2
Virtual Switch
!
!
Corp
Mgmt
Clust.
Mgmt
Mgmt
Non-compliant
 Remediate

## Slide 33: Host configuration… with teaming
Several ways to get there:
Manual configuration in host properties
Already deployed hosts
Updating an existing configuration
Bare metal deployment
Consistent deployment
Use host profile
Can re-deploy
Manual configuration in Hyper-V
For hosts brought into VMM with an existing workload
Will appear as a “Standard switch”
Logical Switch
Standard Switch

## Slide 34: VM configuration
VM Networks
  All virtual adapters now only connect to VM networks
Port classifications
  Container for port profile settings
    For Hyper-V switch port settings and extension port profiles
  Reusable
  Exposed to tenants through cloud

## Slide 35: Using a logical switch demo

## Slide 36: How the logical switch works
Logical Switch in VMM
Port Profiles
(Uplink)
Port Profiles
(Virtual)
Hyper-V host #1
Virtual Switch
Switch settings
Switch settings
Hyper-V host #2
Virtual Switch
Corp
Mgmt
Clust.
Mgmt
Mgmt
Extension manager
Extensions
Extensions
Extensions

## Slide 37: External Isolation
Virtual Switch Extension
Manager
Logical Network
“Not connected”
(VSEM)
External VM Network 1
VMM
Admin
Network Sites
(VSEM)
External VM Network 1
VM Network
(External)
Network Sites
(VSEM)
Network Sites
(VSEM)
Logical Network
“Not connected”
External VM Network 1
Network Sites
(VSEM)
External VM Network 1
VM Network
(VLAN)
Network Sites
(VSEM)
Network Sites
(VLAN)
Logical Network
“Connected”
External VM Network 1
Network Sites
(VSEM)
VM Network
(HNV)
Network Sites
(VSEM)
Network Sites
Hyper-V Network Virtualization
Network
Admin

## Slide 38: SCVMM and NEC ProgrammableFlow SDN
OpenFlow/SDN Solution for
Windows Server and System
Center Virtual Machine Manager
Simple network and VM provisioning
Secure multi-tenant networks
Dynamic traffic control with Network QoS
Central control, including physical and virtual networks
⌃
ProgrammableFlow
Controller (PFC)
VM1
VM2
VM2
Windows Server 2012
Hyper-V Host 1
Windows Server 2012
Hyper-V Host 2
Microsoft
System Center
Virtual Machine Manager
Virtual Tenant
Network
VLAN

## Slide 39: NEC ProgrammableFlow SDN demo

## Slide 40: Forwarding extensions in R2
Hyper-V network virtualization and forwarding extensions can coexist
Enable network virtualization by the forwarding extension itself

## Slide 41: External VM networks
Virtual Switch Extension
Manager
Logical Network
“Not connected”
(VSEM)
External VM Network 1
VMM
Admin
Network Sites
(VSEM)
External VM Network 1
VM Network
(External)
Network Sites
(VSEM)
Network Sites
(VSEM)
Logical Network
“Not connected”
External VM Network 1
Network Sites
(VSEM)
External VM Network 1
VM Network
(VLAN)
Network Sites
(VSEM)
Network Sites
(VLAN)
Logical Network
“Connected”
External VM Network 1
Network Sites
(VSEM)
VM Network
(HNV)
Network Sites
(VSEM)
Network Sites
Hyper-V Network Virtualization
Network
Admin

## Slide 42: External VM networks in R2
Virtual Switch Extension
Manager
External VM Network 1
VMM
Admin
Network Sites
(VSEM)
External VM Network 1
VM Network
(External)
Network Sites
(VSEM)
Network Sites
(VSEM)
Logical Network
“Not connected”
External VM Network 1
Network Sites
(VSEM)
External VM Network 1
VM Network
(VLAN)
Network Sites
(VSEM)
Network Sites
(VLAN)
Logical Network
“Connected”
External VM Network 1
Network Sites
(VSEM)
VM Network (HNV)
Network Sites
(VSEM)
Network Sites
(VSEM or VLAN)
HNV
External VM Network 1
VM Network (External NV)
External
Network
Admin

## Slide 43: Preview of Cisco Nexus 1000v with R2

## Slide 44: Takeaways from this session
Plan first, deploy second
New in R2: Network managers, IPAM, Physical switch management
Better forwarding extension integraiton

## Slide 45: Scenes from the next episode…
Enabling network virtualization with VMM
Gateway deployment
Windows Server tech behind the gateway
Tenant experience

## Slide 46: Related content
MDC-B210 | Everything You Need to Know about the Software Defined Networking Solution from Microsoft
MDC-B311 | Application Availability Strategies for the Private Cloud
MDC—B321 | Lessons Learned from Implementing Windows Server 2012 and System Center 2012 SP1 for Hosters (Service Providers)
MDC-B327 | Monitoring and Managing the Network and Storage Infrastructure with Microsoft System Center 2012 - Operations Manager
MDC-B354 | What's New in Microsoft System Center 2012 SP1
MDC-IL301 | Transform the Datacenter Immersion, Part 1 of 4: Infrastructure Foundation
MDC-B205 | Windows Server Session to be Announced
MDC-B215 | Windows Server and System Center Session to be Announced
MDC-B216 | Windows Server Networking Session to be Announced
MDC-B331 | System Center Session to be Announced
MDC-B312 | Windows Server Session to be Announced
MDC-B375 | Microsoft Private Cloud Fast Track v3: Private Cloud Reference Architecture Based on Windows Server 2012 and Microsoft System Center 2012 SP1

## Slide 47: Evaluate this session
Scan this QR code to
evaluate this session.
Required Slide
*delete this box when your slide is finalized
Your MS Tag will be inserted here during the final scrub.

## Slide 48
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.