## Slide 2: How to Design and Configure Networking in Microsoft System Center Part 2 of 2
Greg Cusanza
Senior Program Manager, Microsoft SCVMM
Charley Wen
Program Manager, Microsoft Windows
MDC-B350

## Slide 3: Session Objectives And Takeaways
Session Objective(s):
  How we’ve expanded on what was built in Windows Server 2012 and System Center 2012 SP1 to complete our hybrid networking solution.
Windows Server 2012 R2, System Center 2012 R2, and Windows Azure come together to enable hybrid networking for Windows powered clouds.

## Slide 4: What is a hybrid network
Tenant 3
Tenant 2
Wingtip Hosted
Compute
Storage
Network
Hoster infrastructure
Gateway
Wingtip private cloud
Internet
Windows
Azure Pack
VMM
Service provider
Remote users

## Slide 5: Hybrid networking in 2012 and 2012 SP1
Windows Server 2012 – Network Virtualization, Routing and remote access (RRAS), Microsoft IPAM
SC 2012 SP1 – VM networks with single VPN
3rd party gateways –
Introduced Windows Azure Services for Windows Server portal – not hybrid!

## Slide 6: Benefits
For hoster or private cloud:
Multi-tenant gateway reduces cost
Enhanced Reliability with Clustering
Works Seamlessly with Hyper-V network virtualization
Self-service provisioning for tenants
Private Cloud (Enterprise)
Hoster Cloud
Public Cloud (Windows Azure)
Site-to-Site
Gateway
Multi-tenanted
Site-to-Site
Gateway
Multi-tenanted
Site-to-Site
Gateway
“Cost effective for hosters… up front and per-tenant”
For Enterprise as tenant:
Extend the enterprise network from multiple on-premises sites to the hoster
Establish contract for average throughput for each connections
Easily provision and configure site-to-site connection on the hoster side

## Slide 7: Working together for hybrid networking
Windows Server
2012 R2
Multi-tenant gateway
Site-to-site VPN
Network address translation (NAT)
IP address management and automation
System Center
2012 R2
Management and deployment of Windows Server gateway
Built-in Microsoft IPAM integration
Built-in top-of-rack switch management
Reporting of metrics for chargeback
Service provider foundation (SPF)
Windows Azure
services for
Windows Server
Tenant portal for self service networks
Create, manage, connect multiple end points

## Slide 8: Scenario Walkthrough
Network fabric configuration
Gateway deployment and overview
Tenant Experience
Hybrid
Network

## Slide 9
Windows Azure Pack
Gateway
Tenant 2 VMs
Tenant 2
Tenant 1 VMs
Tenant 1
LM, Cluster, Storage
Hyper-V hosts
SQL
SPF, etc.
VMM
Management
Corporate
Public Internet
Network Overview
with extensible
Virtual switch

## Slide 10
Public Internet
Network
Virtualization
Gateway
Tenant 2 VMs
Tenant 2
Tenant 1 VMs
Tenant 1
LM, Cluster, Storage
Hyper-V hosts
SQL
SPF, etc.
VMM
Management
Corporate
Network Overview with Network Virtualization
Provider
with extensible
Virtual switch
Windows Azure Pack

## Slide 11: Network fabric configuration
  Enabling network virtualization
    WS 2012 R2 no longer requires NV filter enablement
  Configuring provider address space
    Must have static IP pool
    Must enable network virtualization on logical network for provider addresses
  If mixing 2012 and 2012 R2 hosts, must have KB2779768 on 2012 hosts

## Slide 12: Enabling network virtualization in the fabric

## Slide 13: Enabling hybrid connectivity
  Gateway is required
  3rd party gateways
  Windows Server Gateway

## Slide 14: Windows Server Gateway Charley Wen

## Slide 15: Hybrid cloud connectivity – WS2012
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 1
Fabrikam
Site 2
S2S tunnel
S2S tunnel
S2S tunnel
S2S tunnel
S2S tunnel
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
One site-to-site GW per tenant
Limited routing capability
Manual provisioning
Internet connectivity back to remote site
Internet
Hoster

## Slide 16: Hybrid cloud connectivity – WS2012 R2
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 1
Fabrikam
Site 2
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Internet
Hoster
S2S tunnel
S2S tunnel
S2S tunnel
S2S tunnel
S2S tunnel
Multitenant site-to-site network virtualization GW
Clustering for high availability
BGP for dynamic routing
Multitenant NAT for internet access
BGP

## Slide 17
Demo
GWHost1
Cloud
GW 1
Web Server
Northwind
Contoso
Client
GWHost2
Cloud
GW 2
Hosted Cloud

## Slide 18: Private Cloud with WS2012 R2
Private Cloud
HNV
Private Cloud
AD / DNS
IIS Server
VM Network 1
VM Network 2
VM Network 3
Remote site
3rd party VPN router
S2S VPN
Forwarding
GW

## Slide 19: Multitenant Networking Stack
VM NIC
TCP/IP
Network Services
IP Interface
VM
Hyper-V switch

## Slide 20: Multitenant Networking Stack
VM NIC
TCP/IP
Default Compartment
Compartment for
Tenant VM Network
Compartment for Tenant VM Network
IP Interface
IP Interface
IP Interface
IP Interface
Existing Network Services
Multitenant Network Services
VM
Hyper-V switch

## Slide 21: Multitenant Networking Stack
Provide tenant traffic isolation per compartment
Allow overlapping IP addresses
Enabled through Windows Server 2012 R2 Hyper-V host

## Slide 22: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Interface
Step 1: Northwind subscribes to cloud infrastructure service

## Slide 23: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind
Compartment
Northwind
VM Network
Step 2: Hoster admin creates a site-to-site endpoint for Northwind
Interface
Interface

## Slide 24: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Step 3: Northwind initiates a connection and is authenticated by Machine Certificate, PSK, or EAP
Interface
Interface
S2S Tunnel

## Slide 25: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Step 4: Authentication credentials are used to map Northwind to its compartment
Interface
Interface
S2S Tunnel

## Slide 26: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Interface
Interface
S2S Tunnel
Contoso Compartment
Contoso
VM Network

## Slide 27: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Interface
Interface
S2S Tunnel
Contoso Compartment
Contoso
VM Network
Interface
Interface
Interface
S2S Tunnel
S2S Tunnel

## Slide 28: Multitenant Site-to-Site
Default Compartment
VM
Contoso Site1
Contoso Site2
Northwind
Northwind Compartment
Northwind
VM Network
Interface
Interface
S2S Tunnel
Contoso Compartment
Contoso
VM Network
Interface
Interface
Interface
S2S Tunnel
S2S Tunnel
Packet
Support rate-limiting per tunnel in either direction

## Slide 29: Multitenant NAT
Default Compartment
VM
Northwind Compartment
Northwind
VM Network
Interface
Contoso Compartment
Contoso
VM Network
Interface
Interface
Internet
Packet
Contoso NAT

## Slide 30: Multitenant NAT
Default Compartment
VM
Northwind Compartment
Northwind
VM Network
Interface
Contoso Compartment
Contoso
VM Network
Interface
Interface
Internet
Contoso NAT
Northwind NAT
Each tenant has its own NAT with a unique public IP address

## Slide 31: Multitenant NAT
Default Compartment
VM
Northwind Compartment
Northwind
VM Network
Interface
Contoso Compartment
Contoso
VM Network
Interface
Interface
Internet
Contoso NAT
Northwind NAT
Inbound connection is allowed via static mapping
Packet

## Slide 32: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16

## Slide 33: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
BGP

## Slide 34: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
Route selection for traffic

## Slide 35: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16

## Slide 36: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
BGP

## Slide 37: BGP Dynamic Route Learning & Best Path Selection
S2S VPN
S2S VPN
Hosted site
VM Network
Site 1
Site 2
Contoso
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
No manual intervention

## Slide 38: Multitenant BGP
All tenants routes can be exchanged on a single gateway
Support routing tables with overlapped addresses
Integrated with site-to-site VPN

## Slide 39: Guest Clustering for High Availability

## Slide 40: Guest Clustering for High Availability
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Active
Standby
1:1 redundant VMs with guest clustering
Redundant VM is in hot standby
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 1
Fabrikam
Site 2
Internet
Hoster

## Slide 41: Guest Clustering for High Availability
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Active
1:1 redundant VMs with guest clustering
Redundant VM is in hot standby
Standby
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 2
Fabrikam
Site 1
Internet
Hoster

## Slide 42: Guest Clustering for High Availability
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Active
1:1 redundant VMs with guest clustering
Redundant VM is in hot standby
Failure of Active is detected immediately
Standby
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 2
Fabrikam
Site 1
Internet
Hoster

## Slide 43: Guest Clustering for High Availability
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Active
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
1:1 redundant VMs with guest clustering
Redundant VM is in hot standby
Failure of Active is detected immediately
Remote S2S disconnects and reconnects on new Active
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 2
Fabrikam
Site 1
Internet
Hoster

## Slide 44: Guest Clustering for High Availability
Contoso
VM Network
Northwind
VM Network
Fabrikam
VM Network
Active
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
S2S Tunnel
1:1 redundant VMs with guest clustering
Redundant VM is in hot standby
Failure of Active is detected immediately
Remote S2S disconnects and reconnects on new Active
Failover fast enough to keep end-to-end TCP connections alive in most cases
Contoso
Site 1
Contoso
Site 2
Northwind
Fabrikam
Site 2
Fabrikam
Site 1
Internet
Hoster

## Slide 45: Back to VMM

## Slide 46: Provisioning process through VMM
  All steps performed from within VMM
    Deploy host
    Deploy gateway VMs from service
    Add gateway to VMM
    Finalize gateway configuration
  Post-preview functionality configured from SCVMM
    Highly available gateway
    Forwarding gateway

## Slide 47: Demo – Enabling hybrid connectivity
VMM Server
Virtualization Admin
“GW-H01” - Hyper-V Host Dedicated to Network Virutalization Gateway
External/Internet
To compute
Hyper-v hosts
Infrastructure
Tenant backend
Deploy GW-VM01
Add as gateway
Set connectivity
Create tenant vm networks
“GW-VM01” –
Network address translation
Site-to-Site VPN
Gateway:
“GW-VM01”

## Slide 48: Gateway Deployment

## Slide 49: Enabling tenant self-service
Using Windows Azure services for Windows Server
  Tenants create their own networks
  Consistent experience with Windows Azure
  Configuration of topology and border gateway protocol (BGP)
  Reporting and chargeback
Service Provider Foundation (SPF) provides REST API to enable Hosters and Private cloud providers to build own portal
Support for guest clusters and guest specified IP addresses with network virtualization

## Slide 50: Demo – Tenant self-service
Tenant 3
Tenant 2
Tenant 1
Compute
Storage
Network
Hoster infrastructure
Windows Server
Gateway
Tenant 1 private cloud
Internet
Windows Azure Services for Windows Server
VMM
1
2
3
4
Service provider
Remote users

## Slide 51: Tenant self service

## Slide 52: Closing remarks
Microsoft provides an end-to-end multi-tenant hybrid networking solution utilizing site-to-site VPNs, border gateway protocol (BGP) and network address translation (NAT).
It’s simple, reliable and scalable

## Slide 53: Related content
MDC-B210 | Everything You Need to Know about the Software Defined Networking Solution from Microsoft
MDC-B311 | Application Availability Strategies for the Private Cloud
MDC—B321 | Lessons Learned from Implementing Windows Server 2012 and System Center 2012 SP1 for Hosters (Service Providers)
MDC-B327 | Monitoring and Managing the Network and Storage Infrastructure with Microsoft System Center 2012 - Operations Manager
MDC-B354 | What's New in Microsoft System Center 2012 SP1
MDC-IL301 | Transform the Datacenter Immersion, Part 1 of 4: Infrastructure Foundation
MDC-B205 | Windows Server Session to be Announced
MDC-B215 | Windows Server and System Center Session to be Announced
MDC-B216 | Windows Server Networking Session to be Announced
MDC-B331 | System Center Session to be Announced
MDC-B312 | Windows Server Session to be Announced
MDC-B375 | Microsoft Private Cloud Fast Track v3: Private Cloud Reference Architecture Based on Windows Server 2012 and Microsoft System Center 2012 SP1

## Slide 54: Track resources
Learn more about Windows Server 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/WS2012R2
Learn more about System Center 2012 R2 Preview, download the datasheet and evaluation bits on http://aka.ms/SC2012R2

## Slide 55: Resources
msdn
  Resources for Developers
http://microsoft.com/msdn
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
TechNet
  Sessions on Demand
http://channel9.msdn.com/Events/TechEd
  Resources for IT Professionals
http://microsoft.com/technet

## Slide 56: Complete an evaluation on CommNet and enter to win!

## Slide 57: Evaluate this session
Scan this QR code to evaluate this session and be automatically entered in a drawing to win a prize
Required Slide
*delete this box when your slide is finalized
Your MS Tag will be inserted here during the final scrub.

## Slide 58
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.