## Slide 2: Next Generation Remote Access with DirectAccess
Richard Hicks – MVP
Iron Networks
@richardhicks
WCA-B339

## Slide 3: The Remote Access Challenge…

## Slide 4: Agenda
What is DirectAccess?
What are the Benefits of DirectAccess?
What’s New in Windows Server 2012 DirectAccess
DirectAccess Components
Limitations of DirectAccess
How DirectAccess Works
Demonstration
Security Considerations

## Slide 5: What Is DirectAccess?

## Slide 6: What Is DirectAccess?
Next Generation Remote Access
Always On
Seamless and Transparent
Bi-Directional Connectivity
NOT a VPN!

## Slide 7: DirectAccess vs. Legacy VPN
VPN
  Intrusive
  User Initiated
  Remote User Connects to the Corporate Network…
DirectAccess
  Seamless and Transparent
  No User Action Required
  Extend Corporate Network to the User!

## Slide 8: DirectAccess Benefits
  Streamlined User Experience
  Familiar Access
  Increased Productivity
End User
  Always Managed
  Improved Compliance
  Reduced Administration Costs
Administrator

## Slide 9: Evolution of DirectAccess
Windows Server 2008 R2
Forefront Unified Access Gateway (UAG) 2010
Windows Server 2012

## Slide 10: What’s New in Server 2012 DirectAccess?

## Slide 11: What’s New in Windows Server 2012
DirectAccess and RRAS Coexistence
Simplified Deployment
No PKI
Perimeter/DMZ Deployment
Integrated Network Load Balancing
Multi-Domain Support
NAP Integration
OTP/Virtual Smartcard
Automated Force Tunneling
IP-HTTPS Improvements
Manage Out
Multi-Site
Server Core
PowerShell
Monitoring and Reporting

## Slide 12: New Feature Highlights
Easier to Deploy
  Simplified Deployment
  Flexible Network Placement
Improved Management
  Monitoring, Reporting, and Diagnostics
  PowerShell
Performs Better
  Single IPsec Tunnel*
  IP-HTTPS Improvements
More Scalable
  Load Balancing
  Geographic Redundancy

## Slide 13: DirectAccess Components
Windows Server 2012
Windows 8 Enterprise
IPv6 and IPsec
Active Directory and Group Policy

## Slide 14: DirectAccess Components (Cont’d)
Certificates
  PKI is optional (Strongly Recommended!)
  PKI required for Windows 7 clients
Network Location Server (NLS)
  HTTPS web server
DNS64/NAT64
  IPv6 to IPv4 translation
Name Resolution Policy Table (NRPT)
  Policy based name resolution routing
Windows Firewall w/Advanced Security

## Slide 15: DirectAccess Requires IPv6 End to End

## Slide 16: IPv6 Transition Technologies
6to4
  Public Client IP Address
  IP Protocol 41
Teredo
  Private Client IP Address
  UDP Port 3544
IP-HTTPS
  6to4/Teredo Not Available
  SSL/TLS
ISATAP
  Intranet Manage Out
  ISATAP Router
  DNS

## Slide 17: A Word About ISATAP…
ISATAP NOT Recommended
  Global In Scope
  Lower Layer Protocols Depend on Upper Layer Protocols
  Lack of Monitoring and Management
Deploy IPv6
Restrict ISATAP to Specific Hosts
  Group Policy
  Powershell [SetNetIsatapConfiguration –Router NameOrIPAddress]
  Netsh [netsh interface isatap set router NameOrIPAddress]
  HOSTS file

## Slide 18: DirectAccess Limitations

## Slide 19: DirectAccess Limitations
Supported Clients
  Windows 8 Enterprise
  Windows 7 Enterprise
  Windows 7 Ultimate
  Domain-Joined
Non-Supported Clients
  Windows 8 Professional
  Windows Vista
  Windows XP
  Non Domain-Joined

## Slide 20: DirectAccess Limitations
  Protocols with Embedded IPv4 Addresses
  Applications with Hard Coded IPv4 Addresses
  IP Protocol Communication
Client Compatibility Issues

## Slide 21: How DirectAccess Works

## Slide 22: How DirectAccess Works
Client on the Intranet…
  Client Assumes it is Not Connected to the Intranet
  Establishes HTTPS Connection to NLS
  Domain WFAS Profile Activated
  NRPT Disabled
  No DirectAccess IPsec Tunnels

## Slide 23: How DirectAccess Works
Client on the Internet…
  Client Assumes it is Not Connected to the Intranet
  Fails to Establish HTTPS Connection to NLS
  Public or Private WFAS Profile Activated
  NRPT Enabled
  DirectAccess IPsec Tunnels Enabled

## Slide 24: Implementing DirectAccess
Install RemoteAccess Feature
  GUI
  PowerShell
    Install-WindowsFeature remoteaccess –IncludeManagementTools –Restart
Configure RemoteAccess
  Simplified Deployment
  Complex Deployment

## Slide 25: Demonstration
Richard Hicks – MVP
Iron Networks
@richardhicks

## Slide 26: Security Considerations
Authentication
  Password Policy
  SmartCards
  Dynamic Passwords (OTP)
Endpoint
  Whole Disk Encryption
  Boot PIN
  Anti-Virus
Infrastructure
  NAP Integration
  Remote Content Filtering
  Disable Computer Account for Lost/Stolen Machines

## Slide 27: Closing Thoughts…

## Slide 28: Thank You!
Richard Hicks – MVP
Iron Networks
richardh@ironnetworks.com
richardhicks.com/connect

## Slide 29: Windows Track Resources
Windows Enterprise: windows.com/enterprise
Windows Springboard: windows.com/ITpro
Microsoft Desktop Optimization Package (MDOP): microsoft.com/mdop
Desktop Virtualization (DV): microsoft.com/dv
Windows To Go: microsoft.com/windows/wtg
Outlook.com: tryoutlook.com

## Slide 30: Resources
msdn
  Resources for Developers
http://microsoft.com/msdn
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
TechNet
  Sessions on Demand
http://channel9.msdn.com/Events/TechEd
  Resources for IT Professionals
http://microsoft.com/technet

## Slide 31: Evaluate this session
Scan this QR code to
evaluate this session.
Required Slide
*delete this box when your slide is finalized
Your MS Tag will be inserted here during the final scrub.

## Slide 32
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.