## Slide 2: Deploying & Managing Lync Voice
Zahid Saeed (Lync MCM & CCIE Voice)
Communications TSP
OFC-B337

## Slide 3: Session Objectives And Takeaways
Session Objective(s):
  Provide quick recap of Lync Call Routing
  Explain Lync Server 2013 location-based routing capabilities.
  Recommend solutions using location-based routing to enable regulatory compliance or optimize call paths.
  Explain Lync Call Handling Services available out of the Box with Lync Server 2013

## Slide 4: Agenda
Choosing your Project Sponsors
Lync Architecture Overview
Lync Voice Call Routing Recap
Location Based Routing (LBR)
Lync Call Handling Services

## Slide 5: Sponsors

## Slide 6: Get support for your project
Executive sponsorship must be appropriate and accountable for the scale of deployment planned. The level and intensity of sponsorship will also change as projects progress from pilot to full deployment.
  Is the executive sponsorship appropriate and properly accountable for the scale of the next phase of the deployment?
  Is the anticipated return on investment clear and measurable?
  Is the sponsoring executive accountable to achieve the ROI and the overall value of the Lync deployment?

## Slide 7: Lync Voice Architecture Overview

## Slide 8: Deployment Types
Enabling gradual migration and coexistence between Lync private and public clouds
Microsoft Office 365, Lync Online
Partner-hosted or multi-tenant
Single domain and directory
Users split—server/online
Lync Server 2013
Private cloud/dedicated
Hybrid
On-premises
Cloud

## Slide 9: Overview of Lync Offerings
Lync Server 2013 on-premises – Full UC including Enterprise Voice May be used with Exchange Online or Exchange Server on-premises
Lync Online – IM, Presence, & Meetings without Enterprise Voice May be used with Exchange Online or Exchange Server
Lync Hybrid – Lync Server & Lync Online in a shared setup Combining both worlds, on-premises users with Full UC including Enterprise Voice , IM & Presence, and Conferencing for Online users. Sharing the same namespace.

## Slide 10: Lync Server High-Level Topology
Public
Providers
Reverse
proxy
External
Edge
server
Federated
Network
Hybrid
Perimeter network
Internal
UC end points
EE pool
IP-PSTN
gateway
Persistent
Chat (optional)
AD
MIIS
Identity
Voicemail/
Archive
Monitoring
File store
Web Access
CDR/QoE/
Report DB
Exchange
SCOM
DFS
Office Web Apps
SQL
PBX
New!
New!

Mediation Server
(optional)
PSTN
Front-end
Back-end
Edge
More secure federation and interoperability
External user ingress
Pool
Fewer, consolidated servers
Virtualized and higher scale
Services
Consolidated archiving
SCOM, AD, DFS

## Slide 11: Voice Routing in Lync
A quick recap of the most important elements

## Slide 12
Select usages
12
Announcement or Call Park Application
Dialing Behaviors
Routing & Authorization
Normalization Rule
Normalization Rule
Normalization Rule
Dial Plan
PSTN Usage
PSTN Usage
PSTN Usage
Voice Policy
Routes
Route
Route
Route
Route
External Endpoint Receives Call
UC Endpoint Receives Call
User=phone
Yes
Global?
No
SIP URI
Match
Reverse Number Lookup
No match
Trunk Configuration / Number Translation
Gateway / IP-PBX / SIP Trunk
Inbound Routing
Yes
Emergency Call?
No
Call Park Orbit Range
1
2
3
4
5
6
7
8
10
11
12
13
Must Match A Rule
RFC 3966 Starts with +
msRTCSIP-Line msRTCSIP-PrivateLine
Convert # to Local Format
Apply Called Party Prefs
PSTN Fallback for CAC and Network Outages
14
External Normalization Rules
Internal Normalization Rules
Dial Plan
EAP?
Client-side normalization
Unassigned number?
Call Park?
Conference dial-out?
From trunk with usages?
Location-based routing?
Gateway
Mediation Server
Emergency call?
Referred-by?
Usages on inbound trunk
Usage from location policy
Usages of meeting organizer
Usages from network site
Usages of referrer
Usages of caller
9
Voice Routing
Notes: Start Time xx:xx / Length: 1 minute
Walk the students through each of the elements in the diagram, explaining their roles in the configuration process and any dependencies.
Discuss the difference between Dialing Behaviors and Routing & Authorization.
Dialing behaviors happen when the client dials a number. With the exception of emergency numbers, its sole purpose is to get the number into a routable (= E.164) format.
Routing & Authorization takes place after the number is globally unique. This is the process used to select the right route to the final destination, and then check to determine whether the user is authorized to make the call.
Advance through the animations by clicking and use the arrows to explain every step in the process.

## Slide 13: Routing and Authorization
The big picture of the most important elements
Voice policies
PSTN usages
Routes
Called number Cost of call
Purpose (usage, caller’s intent) Calling location Priority
User authorization Class of service Voice feature set

## Slide 14: Voice Policies
Can be assigned per user, per site or global
Provides admins with flexibility to control user voice entitlements Call Forwarding, Delegation, Call Transfer, Call Park, Simultaneous Ringing, Team Call, PSTN Rerouting, BW Policy override Malicious call tracing
Control dialing capabilities (class of service) by assigning public switched telephone network (PSTN) usages
Not only for users. Also useful to address common area device requirements Assign a Voice Policy to a common area phone to prevent misuse and high cost

## Slide 15: PSTN Usages
A PSTN usage record specifies a class of call (such as internal, local, or long distance) that can be made by various users or groups of users in an organization
By themselves, PSTN usage records do not do anything. For them to work, they must be associated with the following Voice policies, which are assigned to users Routes, which are assigned to phone numbers

## Slide 16: Routes
A voice route associates destination phone numbers with one or more PSTN gateways or session initiation protocol (SIP) trunks, and one or more PSTN usage records
A route is selected based on a matching pattern
PSTN usages control if a user is allowed to use the route
Routes are associated with one or more trunks

## Slide 17: Controlling Gateway Preference
Multiple trunks in same route Gateway will be selected randomly. Useful when there is no gateway preference and multiple gateways are available for same path to PSTN.
Multiple routes in the same usage Gateway selected based on matching pattern. If multiple routes match, do not rely on route ordering for enforcing preference. Used when different gateways are used for different called numbers but all belong to the same class of service.
Routes in different usages Gateway selected based on the order of the usages in the user’s voice policy. Useful for enforcing primary/secondary relationships between gateways.

## Slide 18: Location Based Routing

## Slide 19: Regulatory Requirements
57+ countries regulate voice over internet protocol (VoIP)
  Countries include: UAE, India, Egypt, Pakistan, Oman, Qatar, parts of China, many African and Asian countries
Regulation Examples
  No allowed to toll bypass
  No allowed to bypass local telephony providers
Regulations may provide exceptions for closed user groups (such as enterprises, educational institutions, and so on) and allow VoIP and video within the user group, even if international
Location-Based Routing (LBR) was designed specifically to enable compliance in India

## Slide 20: Introducing Location-Based Routing
LBR is designed to enable compliance with regulatory requirements that restrict toll bypass
Routes the call based on the location of the caller
Enforce routing of PSTN calls to prevent toll bypass
Scoped to specific sites, gateways, and users
Delivered in the July 2013 update to Lync Server 2013 LBR for PSTN calls was introduced in the February 2013 update The July 2013 update adds support for dial-out conferencing

## Slide 21: Least Cost Routing vs. Location-Based Routing
Least cost routing (LCR)
  Route call to the gateway closest to the called party
  Minimize toll charges (toll bypass)
  Prioritize the use of the WAN
Location-Based Routing
  Route call to the gateway closest to the calling party
  Minimize use of WAN
  Enable compliance with regulations that do not allow toll bypass
Toll Bypass
Use the own (WAN) infrastructure as much as possible
Egress to the PSTN closest to the destination
Avoid international (costly) PSTN charges

## Slide 22: Routing Considerations for LBR
Outbound Routing
Routing decisions are made based on where the user is located and what PSTN number they are trying to dial
Inbound Routing
Routing Decisions are made based on where the call enters the Lync system and where the called party is located
Location A
Location B
WAN
PSTN
Bob
Alice
Location A
Location B
WAN
PSTN
Alice
Bob

## Slide 23: Routing Considerations for LBR
Outbound Routing
Routing decisions are made based on where the user is located and what PSTN number they are trying to dial
Inbound Routing
Routing Decisions are made based on where the call enters the Lync system and where the called party is located
Location A
Location B
WAN
PSTN
Alice
Bob
UM
Location A
Location B
WAN
PSTN
Alice
Bob

## Slide 24: Location-Based Routing Capabilities
Enforces that outgoing calls must egress from an allowed PSTN gateway in the caller’s voice policy, based on the callers location
Can prevent the incoming call to the Lync client if the endpoint is not in the PSTN gateway’s location
Lync Conferencing honors LBR policies for PSTN dial-out

## Slide 25: LBR Regulatory Compliance Limitations
Call park and response groups
  Call flows with these scenarios could violate the regulatory principles
  Either a) do not deploy or b) deploy only to users within a single site
Dial-in conferencing
  Dialing in may create a conference that has PSTN and VoIP users from different sites
  For strict compliance, do not deploy dial-in access numbers and require dial-out
UM routing
  Denied inbound calls are sent to UM
  For strict compliance, place the UM server for a group of users in same site as the gateway that terminates their direct inward dialing (DID)

## Slide 26: Location Based Routing
Support & Configuration

## Slide 27: Location-Based Routing Basics
    Site
  One or more Lync subnet(s) assigned to a location
  Uses existing network sites as defined for LIS, Media Bypass, and E911
    Voice Routing Policy
  Voice policy that only contains usages
  Specifically assigned to a site for LBR
  Contains all allowed usages for that specific site or trunk
    Unknown Location
  Location (subnet) that is not known as a Lync Site
    Trunk
  Connects gateways and mediation servers
  Can be enabled for LBR and must be assigned to site

## Slide 28: Pool Support for Location-Based Routing
Pool version | Mediation server version | Supported
Lync Server 2013 February 2013 Cumulative Update | Lync Server 2013 February 2013 Cumulative Update | Yes
Lync Server 2013 February 2013 Cumulative Update | Lync Server 2013 | No
Lync Server 2013 February 2013 Cumulative Update | Lync Server 2010 | No
Lync Server 2013 February 2013 Cumulative Update | Office Communications Server 2007 R2 | No
Lync Server 2013 | Any | No
Lync Server 2010 | Any | No
Office Communications Server 2007 R2 | Any | No

## Slide 29: Client Support for Location-Based Routing
Client type | Supported | Details
Lync 2013 | Yes | Including Lync 2013 February 2013 Cumulative Update
Lync 2010 | Yes | 
Office Communicator 2007 R2 | No | 
Lync Phone Edition | Yes | 
Lync Attendant | Yes | 
Lync for Windows 8 | No | 
Lync Mobile 2013 | No | VoIP must be disabled for Lync Mobile 2013 clients if used by users with Location-Based Routing enabled.
Lync Mobile 2010 | Yes | 

## Slide 30: Configuring Location-Based Routing
  New-CsVoiceRoutingPolicy
    -Identity <voice routing policy ID> -Name <voice routing policy name>
    -PstnUsages <usages>
  Set-CsNetworkSite
  -Identity <site ID>
  -EnableLocationBasedRouting <$true|$false>
  -VoiceRoutingPolicy <voice routing policy ID>
  Create the Voice Routing Policy
  Enable Location Based Routing for Network Sites
  Enable Location Based Routing and assign a Voice Routing Policy to the Network Site
  New-CsTrunkConfiguration -Identity < trunk configuration ID>
  Set-CsTrunkConfiguration
    -Identity <trunk configuration ID>
    -EnableLocationRestriction $true
    -NetworkSiteID <site ID>
  Create a Trunk Configuration (Only for PSTN gateways, not Internal PBX routes)
  Enable Location Based Routing through Trunks
  Enable Location Based RoutingOn the Trunk

## Slide 31: Configuring LBR (Continued)
  Set-CsVoicePolicy
  -Identity <voice policy ID>
  -PreventPSTNTollBypass <$true|$false>
  Modify the Voice Policy
  Enable LBR through Voice Policy
  Set-CsRoutingConfiguration
  -EnableLocationBasedRouting $true
  Create a Trunk Configuration (Only for PSTN gateways, not Internal PBX routes)
  Enable Location Based Routing Globally

## Slide 32: Design Considerations
    When using LBR, the site routing policy must include a route for all possible calls
  It is possible that a call would be allowed by the user’s policy, but if it were not allowed by the site’s policy, it would be blocked
    Trunks are associated with one network site
  For LBR, your campus must be represented as one site if using centralized SIP Trunks

## Slide 33: Lync Voice Applications Update

## Slide 34: Lync Call-Handling Services
Administrator Configured
User Configured *
Lync Call Handling Services
Unassigned Numbers Service
Prompt playback and transfer capability for unassigned numbers
Response Group
Call queuing, treatment, and routing for departments
Call Park
Asynchronously transfer of a call between users, endpoints, or both
Team Call
Users define who their calls are forked to
Group Call Pickup
Users in a group can retrieve calls presented to another user

## Slide 35: Response Group Service
Basic ACD functionality
  Scenarios including Receptionist, Helpdesk, Departmental call routing
  Installed with Enterprise Voice, licensed with Lync Plus CAL.
  Server side media application that runs on all Front Ends along with web-based administration
Not intended as a contact center replacement
  Limited Management Capabilities – no real time views, monitoring/barge-in/whisper, agent reporting
  Limited Integration – no database dips, programmability, skills matching, weighted routing

## Slide 36: Managing RGS- Groups
Agents
List of individuals or DL
Participation policy-
Informal- Lync user sign in
Formal- Specific queue activation
Routing method
Longest idle, parallel, round robin, serial, attendant
Alert time
Time to wait before iterating through routing tree

## Slide 37: Managing RGS- Queues
Groups
One or more Agent groups servicing queue
Queue timeout
  How long can a caller sit in the queue?
  Where to send those callers after timeout(another queue, URI, disconnect, phone number, VM)
Queue overflow
Maximum queue size
Action- Which call to dispatch and where

## Slide 38: Managing RGS- Workflows
Hunt Group
Basic recorded greeting
Business hours or holiday based recordings and routing/queuing
Interactive Response Group
Hunt group basic time of day options
2-tier IVR with custom messages and routes/queues
DTMF or voice based response

## Slide 39: Response Group Administration by Roles
Response Group Administrator
Configuration for all RGS settings and all groups (including creation)
Improves RG admin scalability by delegating workflow to managers
Response Group Manager
Manages specific Workflow settings for designated groups
Cannot manage resources not owned by that manager

## Slide 40: Agent Anonymity
Ringing
RGS
Caller Alice
Caller dials helpdesk
Established
RGS
Ringing
Caller Alice
Agent Bob
Caller navigates IVR and is put into queue. Agent is alerted.
If Bob is not anonymous
Established
Caller Alice
Agent Bob
Bob and Alice connect directly.
If Bob is Anonymous
Established
RGS
Established
Caller Alice
Agent Bob
Bob answers. Call continues to pass through RGS.
Agent

## Slide 41: Unassigned Number Service
Call treatment for dialing numbers owned by the enterprise but unassigned to users
  Avoid busy tones if callers misdial
  Transfer to predetermined destination
    Phone number
    SIP URI
    Voicemail
    Announcement Service

## Slide 42: Unassigned Number Management
Create announcement message and transfer target
Text to speech or audio file announcement
Target URI if forwarding is desired
Then define applicable number range
Only define ranges that are
owned by Lync!
PS > New-CsAnnouncement -Identity ApplicationServer:2013-lync-fe.conto
so.com -Name "Number does not exist" -TextToSpeechPrompt "The number you dialed is not in service.
You will now be sent to the operator for assistance" -Language "en-US" -TargetUri "sip:garthf@contos
o.com"

## Slide 43: Call Park
Call Park and Retrieve
Orbit (number) returned when call is parked
Parked user is listening to Music on Hold (MoH)
Call can be retrieved from PBX phone dialing orbit
Parker notification when call is retrieved
Ring back
Calls not retrieved are transferred to parker
Transfer to fallback destination
Abandoned calls are forwarded to configurable target (receptionist, response group, etc.)

## Slide 44: Call Park- Configuration
Call Park Service installed when configured for Enterprise Voice
Enable in user policy (off by default)
Configure orbit ranges
Number ranges per pool
Range is globally unique, not DIDs
Digits must be of uniform length

## Slide 45: Call Park- Additional settings in PowerShell
Music on hold
  Enabled or Disabled (service wide). Default enabled.
  To change music- Set-CsCallParkServiceMusicOnHoldFile
Ring back attempts
  1 – 10, default 2.
  Ring back timeout
  10-600s, default 00:01:30
Fallback destination
Routing destination after ring back expires
Default NULL

## Slide 46: Call Park- Flow
Mediation Server
Lync Front End
(CPS)
Alice
Bob
Incoming call
Incoming call
Incoming call
Media
1- Initial call setup
Media

## Slide 47: Call Park- Flow
Mediation Server
Lync Front End
(CPS)
Alice
Bob
Transfer to CPS
Park call
Media
1- Initial call setup
2- Bob parks call
OK- orbit #199
Media

## Slide 48: Call Park- Flow
Mediation Server
Lync Front End
(CPS)
Alice
Bob
Transfer to Charlie
Dial #199
Media
1- Initial call setup
2- Bob parks call
3- Charlie dials #199
“Charlie picked up #199”
Charlie
Media

## Slide 49: Group Call Pickup
  Feature
  Incoming calls to a user are intercepted by group member by dialing a predefined orbit number
  Private Line, Delegation, Teamcall, Simulring, RGS & Personal Contact calls cannot be picked up
  Administration
  Call Park Orbits can be flagged for Group Call Pickup - Users are enabled by being assigned an orbit number
  GCP group members are managed by administrator (SEFAUtil). NOT end user configurable.
  Calls to GCP user ring the callee AND fork to CPS.

## Slide 50: Question?

## Slide 51: Track resources
http://technet.microsoft.com/en-us/library/jj205403.aspx
http://technet.microsoft.com/en-us/library/jj205321.aspx
http://technet.microsoft.com/en-us/library/jj994038.aspx

## Slide 53: Resources
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
msdn
  Resources for Developers
http://microsoft.com/msdn
TechNet
  Resources for IT Professionals
http://microsoft.com/technet
  Sessions on Demand
http://channel9.msdn.com/Events/TechEd

## Slide 54: Complete an evaluation and enter to win!

## Slide 55: Evaluate this session
Scan this QR code to evaluate this session.

## Slide 56
© 2014 Microsoft Corporation. All rights reserved. Microsoft, Windows, and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.