## Slide 1: Architecting Cloud Infrastructure Using Window Server 2012
Yigal Edery
Principal Program Manager
Microsoft Corporation
Joshua Adams
Senior Program Manager
Microsoft Corporation
WSV329

## Slide 2: Agenda
Windows Server 2012 - The cloud infrastructure
Considerations in building clouds
  Workloads
  Networking
  Storage
  Resiliency
Representative cloud configurations
  Demos

## Slide 3: Windows Server 2012 is Cloud Optimized
Multi-Tenant Clouds
High Scale & Low Cost Datacenters
Manageable & Extensible

## Slide 4: Windows Server 2012 : Summary of Cloud Enabling Features
Dynamic & Multi-Tenant
High Scale & Low cost – Network
High Scale & Low cost - Compute
Network Virtualization
Datacenter Bridging (DCB) on 10GbE Networks
QoS
Live & Storage Migrations
Policy-Based Isolation
Performance Metrics
Cross-Premise Connectivity
RDMA
RSC / RSS
Hardware offloads
Large VMs
NIC Teaming
Hyper-V Extensible Switch
PowerShell
Manageable and Extensible
Synthetic Fibre Channel
Storage Thin Provisioning
Storage Spaces
Copy offload (ODX)
Hyper-V over SMB
High Scale & Low-Cost - Storage
Larger hosts
Higher VM density
SR-IOV
Large clusters

## Slide 5: Scope of this talk… DDC Reference Architecture
http://aka.ms/bzm1rl

## Slide 6: OK. I’m In! How do I build my Cloud Infrastructure?

## Slide 7
SR-IOV
LBFO
RSS
iSCSI
Clusters
QoS
SAS
Spaces
10GbE
DCB
Network Virtualization
VMQ
Building your cloud requires decisions and tradeoffs.
We’re here to help!
???

## Slide 8: Requirements Influence Choices
Scalability
Reliability
Security
Performance
High Availability
Cost
Workloads
Networking
Storage
Resiliency

## Slide 9: Primary Considerations
Workloads
Networking
Storage
Resiliency

## Slide 10: Primary Considerations
Workloads
Networking
Storage
Resiliency

## Slide 11: Understanding Workloads
Cloud-aware stateless apps or legacy / stateful apps?
  IaaS clouds fully supports legacy apps
  Do you manage virtual servers or apps?
Workload performance requirements
  2 sockets servers usually offer best ROI, large workloads may need larger servers
  Apps networking patterns and the need for SR-IOV
  Mixing different servers to serve different workloads
Are workloads trusted?
  Level of isolation between workloads, QoS policies

## Slide 12: Primary Considerations
Workloads
Networking
Storage
Resiliency

## Slide 13: Primary Network Considerations
Isolation of traffic flows at physical & virtual level
Type of infrastructure
NIC Offloads

## Slide 14: Typical Hyper-V Server Traffic Flows
Virtual Machines traffic
Cluster traffic
Storage traffic / CSV
Live Migrations
Management

## Slide 15: Traffic Isolation / Separation Approaches
How many NICs should be in the server?
  Separate NICs for different traffic flows - WS2008 R2 best practice
  Separate “Datacenter” traffic from “Tenant” Traffic (VMs vs. Infrastructure)
  WS2012: Run everything through the virtual switch, one physical network
Use Port ACLs, QoS, DCB & VM QoS to enforce isolation and performance guarantees

## Slide 16: InfiniBand vs. 10GbE vs. 1GbE
10 Gb Ethernet
  Great performance on familiar fabric
  RDMA optional (for SMB 3.0 file access)
  Offers Quality of Service (DCB) & Flexible bandwidth allocation
  New offloads
  …But physical switch ports more expensive
InfiniBand (32 Gb and 56 Gb)
  Very high performance, low latency
  RDMA included (for SMB 3.0 file access)
  …But Network management different than Ethernet
1 Gb Ethernet
  Adequate performance for many workloads
InfiniBand
1 GbE
10 GbE

## Slide 17: Hardware Offloads for Scalability & Performance
Hyper-V Extensible Switch
VM 1
Live Migration
Storage
Manage
Hyper-V Server
VM n
Windows Server 2012 supports many NIC features including:
HW QoS via Datacenter Bridging (DCB)
Remote Direct Memory Access (RDMA)
Receive Segment Coalescing (RSC)
Receive Side Scaling (RSS)
Virtual Machine Queue (VMQ)
Guest IPsec Task Offload (IPsecTO)
Single Root I/O Virtualization (SR-IOV)
DCB
RDMA
RSS
RSC
SRIOV
VMQ
NOTE: Offloads require capable HW, Windows Server 2012 drivers and potentially BIOS support (e.g. SR-IOV)
DCB
RSS
IPsecTO

## Slide 18: Selecting the right NIC Offloads *
Flexibility and Scalability
Raw Performance
RDMA
SR-IOV
Hyper-V Extensible Switch
Hyper-V Network Virtualization
NIC Teaming
RSS
VMQ
IPsecTO
Some Performance offloads bypass Windows functionality
* Per NIC constraints

## Slide 19: Primary Considerations
Workloads
Networking
Storage
Resiliency

## Slide 20: Storage Selection Considerations
Cost / Performance
Block vs. File
Manageability
Vendor preference
Existing Investments
Approach to scaling

## Slide 21: Storage Scaling Approaches
When?
Very low cost
Disk-bound VMs
Compute & Storage Scale Together
Compute & Storage Scale Independently
Hyper-V Servers
SAS
Hyper-V Servers
Compute/Storage
Compute/Storage
SAS / iSCSI / FC
Hyper-V Servers
Compute
Storage
File Servers
10 GbE / RDMA
Optional Controller
Hyper-V Servers
SAN
Controller
When?
Grow capacity on two axis
Compute-bound VMs
Storage offloading

## Slide 22: Primary Considerations
Workloads
Networking
Storage
Resiliency

## Slide 23: What happens when hardware fails?

## Slide 24: Resiliency Approaches
VMs designed to handle failures (e.g. Guest Clustering) or downtime acceptable.
Lower End Industry Standard Server, single infrastructure
App-Level Resiliency
Application-controlled failover
/ Guest clustering
Switch
Switch
Parent
VMs
VMs
VMs
Parent
VMs
VMs
VMs
Cluster
VMs not designed to handle failures, H/A at server level, Failover clustering as another layer of protection, high-end servers, redundant power and network gear
Hyper-V Failover Clustering
Infrastructure Resiliency
Parent
VMs
VMs
VMs
Parent
VMs
VMs
VMs
Switch
Switch

## Slide 25: Representative Configurations
Optimized for Windows Server 2012
Validated at Microsoft’s Enterprise Engineering Center (EEC)
Step by Step guidance & PowerShell Script Samples Available
  http://technet.microsoft.com/en-us/library/hh831441
  http://blogs.technet.com/b/privatecloud/archive/2012/05/02/let-s-build-a-cloud-with-powershell.aspx
EEC Hardware Used
  Dell R710 servers with SR-IOV support
  Mellanox MHZ29-XTR NICs (RDMA, DCB support)
  Emulex OCE11102-NX (SR-IOV support)

## Slide 26: Non-Converged Configuration (“Traditional” Enterprise)
Easiest transition Path
Physically isolated networks
Regular SANs
Similar to Windows Server 2008 R2 guidance
Backward compatible design, taking advantage of 10GbE, SR-IOV, LBFO, RSS, RSC, VMQ, ODX
SAN
FC / iSCSI
Hyper-V Extensible Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Hyper-V Server
Storage
HBA /
10GbE
1 GbE
1 GbE
1 GbE
1GbE /
10 GbE + SR-IOV

## Slide 27: Non-Converged Configuration (“Traditional” Enterprise)
Easiest transition Path
Physically isolated networks
Regular SANs
Similar to Windows Server 2008 R2 guidance
Backward compatible design, taking advantage of 10GbE, SR-IOV, LBFO, RSS, RSC, DCB, VMQ, ODX
SAN
FCoE / iSCSI
Hyper-V Ext. Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Hyper-V Server
Storage
10GbE
1 GbE
1 GbE
1 GbE
1GbE /
10 GbE + SR-IOV
RSS
ODX
NIC Teaming
Scale & Resiliency for storage access
DCB

## Slide 28: Non-Converged Configuration (“Traditional” Enterprise)
Hyper-V Ext. Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Hyper-V Server
Storage
1 GbE
1 GbE
1 GbE
NIC Teaming
Easiest transition Path
Physically isolated networks
Regular SANs
Similar to Windows Server 2008 R2 guidance
Backward compatible design, taking advantage of 10GbE, SR-IOV, LBFO, RSS, RSC, VMQ, ODX
SAN
FC / iSCSI
HBA /
10GbE
1GbE /
10 GbE + SR-IOV
Scale & Resiliency for VMs
VMQ
1 GbE
1 GbE
1 GbE

## Slide 29: Non-Converged Configuration (“Traditional” Enterprise)
Easiest transition Path
Physically isolated networks
Regular SANs
Similar to Windows Server 2008 R2 guidance
Backward compatible design, taking advantage of 10GbE, SR-IOV, LBFO, RSS, RSC, VMQ, ODX
SAN
FC / iSCSI
Hyper-V Ext. Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Hyper-V Server
Storage
HBA /
10GbE
1 GbE
1 GbE
1 GbE
1GbE /
10 GbE + SR-IOV
Switch Extensions
Network Virt.
QoS
Flexible & Extensible

## Slide 30: Non-Converged Configuration (“Traditional” Enterprise)
Easiest transition Path
Physically isolated networks
Regular SANs
Similar to Windows Server 2008 R2 guidance
Backward compatible design, taking advantage of 10GbE, SR-IOV, LBFO, RSS, RSC, VMQ, ODX
SAN
FC / iSCSI
Hyper-V Ext. Switch
VM 1
VM 2
Live Migration
Cluster
Manage
Hyper-V Server
Storage
HBA /
10GbE
1 GbE
1 GbE
1 GbE
1GbE /
10 GbE + SR-IOV
SRIOV
Switch Extensions
Network Virt.
QoS
Very High Scale VMs w/ SRIOV
But, there are tradeoffs!

## Slide 31: Non-Converged Configuration
demo
Joshua Adams
Program Manager
Enterprise Engineering Center

## Slide 32: Converged Datacenter Network + File Server Storage
SAN / JBODs
File Server
Cluster
Storage
Manage
HBA
(Optional)
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
iSCSI
FC/SAS
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
(RDMA)
10GbE
(RDMA)
1/10GbE

## Slide 33: Converged Datacenter Network + File Server Storage
JBODs
File Server
Cluster
Storage
Manage
SAS
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
SAS
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
(RDMA)
10GbE
(RDMA)
1/10GbE
Pool
CSV
SMB File Share
Space
Scale out FS
Storage Spaces lowers cost of storage

## Slide 34: Converged Datacenter Network + File Server Storage
JBODs
File Server
Cluster
Storage
Manage
Clustered
RAID
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
SAS
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
(RDMA)
10GbE
(RDMA)
1/10GbE
CSV
SMB File Share
Scale out FS
Using hardware RAID controllers
(WSV310: Cluster In a Box, And more…)

## Slide 35: Converged Datacenter Network + File Server Storage
SAN
File Server
Cluster
Storage
Manage
HBA
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
FC
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
(RDMA)
10GbE
(RDMA)
1/10GbE
CSV
SMB File Share
Scale out FS
Also possible : Front-end the SAN with an SMB Share
LUN

## Slide 36: Converged Datacenter Network + File Server Storage
File Server
Cluster
Storage
Manage
SAS
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
(RDMA)
1/10GbE
OS QoS
DCB
Switch QoS
Using Qos & DCB
JBODs
SAS
10GbE
(RDMA)
QoS
New-NetQosPolicy
Switch QoS
Set-VMNetworkAdapter
DCB
Add-WindowsFeature Data-Center-Bridging
Import-Module DcbQos
Enable-NetAdapterQos
Enable-NetQosFlowControl
New-NetQoSTrafficClass

## Slide 37: Converged Datacenter Network + File Server Storage
File Server
Cluster
Storage
Manage
SAS
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
Note: LBFO & RDMA can’t coexist on same NICs.
10GbE
1/10GbE
NIC Teaming
OS QoS
DCB
NIC Teaming
OS QoS
DCB
Use of NIC Teaming & Qos/DCB
10GbE
10GbE
SAN / JBODs
SAS

## Slide 38: Converged Datacenter Network + File Server Storage
File Server
Cluster
Storage
Manage
SAS
Hyper-V Extensible Switch
VM 1
Live Migration
Cluster / Storage
Manage
Hyper-V Server
VM n
Datacenter Network
Tenants Network
“Green Field”
10GbE Network(s)
File Server for VM storage
  Actual storage may be an existing FC/iSCSI SANs or JBODs+Spaces
Highlighted features: 10GbE w/DCB, QoS, LBFO, Hyper-V over SMB, Spaces
10GbE
1/10GbE
RDMA with two Datacenter NICs
10GbE
RDMA
10GbE
RDMA
SAN / JBODs
SAS
10GbE
RDMA
10GbE
RDMA
SMB Multichannel
2 Cluster Networks
2 Networks for LM
Multiple Mgmt IPs
Min BW using DCB

## Slide 39: Converged Configuration with File Server
demo
Joshua Adams
Program Manager
Enterprise Engineering Center

## Slide 40: Converged Network and Storage
JBODs
Hyper-V Extensible Switch
VM 1
Hyper-V Server
VM n
Converged Network
Converged Compute + Storage:
10GbE Network(s), fully converged, routing all traffic through the switch
Shared JBODs, scale compute and storage together
Highlighted features: Storage Spaces on the Hyper-V nodes, Hyper-V Switch ports for VM and Host traffic, QoS policies.
SAS
SAS
Cluster / Storage
Live Migration
Manage
10GbE

## Slide 41: Converged Network and Storage
JBODs
Hyper-V Extensible Switch
VM 1
Hyper-V Server
VM n
Converged Network
SAS
SAS
Manage
ACLs, QoS
VM NICs, with ACLs + QoS on the Switch
Converged Compute + Storage:
10GbE Network(s), fully converged, routing all traffic through the switch
Shared JBODs, scale compute and storage together
Highlighted features: Storage Spaces on the Hyper-V nodes, Hyper-V Switch ports for VM and Host traffic, QoS policies.
VM NICs
Cluster / Storage
Live Migration
10GbE

## Slide 42: Converged Network and Storage
JBODs
Hyper-V Extensible Switch
VM 1
Hyper-V Server
VM n
Converged Network
Converged Compute + Storage:
10GbE Network(s), fully converged, routing all traffic through the switch
Shared JBODs, scale compute and storage together
Highlighted features: Storage Spaces on the Hyper-V nodes, Hyper-V Switch ports for VM and Host traffic, QoS policies.
SAS
SAS
Cluster / Storage
Live Migration
Manage
Cluster/Storage
Tenants
Live Migration
Management
Setup VLANs to separate traffic flows
10GbE
VLANs

## Slide 43: Converged Network and Storage
JBODs
Hyper-V Extensible Switch
VM 1
Hyper-V Server
VM n
Converged Network
SAS
SAS
Manage
Pool
CSV
Space
Spaces and CSV directly on the Hyper-V Servers
Converged Compute + Storage:
10GbE Network(s), fully converged, routing all traffic through the switch
Shared JBODs, scale compute and storage together
Highlighted features: Storage Spaces on the Hyper-V nodes, Hyper-V Switch ports for VM and Host traffic, QoS policies.
Cluster / Storage
Live Migration
10GbE

## Slide 44: Converged Network and Storage
JBODs
Hyper-V Extensible Switch
VM 1
Hyper-V Server
VM n
Converged Network
SAS
SAS
Manage
1/10GbE
Pool
CSV
Space
Add RDMA NICs for fast CSV Redirection
Converged Compute + Storage:
10GbE Network(s), fully converged, routing all traffic through the switch
Shared JBODs, scale compute and storage together
Highlighted features: Storage Spaces on the Hyper-V nodes, Hyper-V Switch ports for VM and Host traffic, QoS policies.
10GbE
RDMA
CSV Traffic
Cluster / Storage
Live Migration

## Slide 45: Converged Configuration without a File Server
demo
Joshua Adams
Program Manager
Enterprise Engineering Center

## Slide 46: DAS, Non-Clustered Configuration
Hyper-V Extensible Switch
VM 1
Live Migration
Manage
Hyper-V Server
VM n
Converged Network
Very Low Cost (Huge Scale Clouds)
10GbE Network(s), fully converged
No clusters, no H/A, local DAS
For cloud-ready applications
Highlighted feature: Live migration w/o clusters
DAS

## Slide 47: Windows Server 2012 is Cloud Optimized !
Flexible – Different cloud architectures to fit your needs
Efficient - Supports existing architectures, and promotes new more efficient ones.
Detailed guidance and configuration scripts on TechNet
System Center 2012 SP1 to manage it all !

## Slide 48: Related Content
Breakout Sessions
VIR303 - An Overview of Hyper-V Networking in Windows Server 2012
VIR306 - Hyper-V over SMB2: Remote File Storage Support in Windows Server 2012 Hyper-V
WSV310 - Windows Server 2012: Cluster-in-a-Box, RDMA, and More
WSV315 - Windows Server 2012 File System Enhancements: Redefining File Storage
WSV320 - Understanding and Deploying Hosted Private Cloud: Concepts and Implementation
MGT314 - What's New in System Center 2012 SP1 - Virtual Machine Manager
VIR201 - What’s New with Windows Server 2012 and Microsoft System Center 2012 SP1
  Additional Content
  Cloud Configuration Guides : http://technet.microsoft.com/en-us/library/hh831441
White Paper - Building IaaS Clouds using Windows Server 2012 : http://aka.ms/dtpq3a
Find Me Later At the Windows Server Networking & Hyper-V areas
Follow me @yigaledery

## Slide 49: SIA, WSV, and VIR Track Resources
Talk to our Experts at the TLC
#TE(sessioncode)
DOWNLOAD Windows Server 2012 Release Candidate
microsoft.com/windowsserver
Hands-On Labs
DOWNLOAD Windows Azure
Windowsazure.com/
teched

## Slide 50: Resources
  Connect. Share. Discuss.
http://northamerica.msteched.com
Learning
  Microsoft Certification & Training Resources
www.microsoft.com/learning
TechNet
  Resources for IT Professionals
http://microsoft.com/technet
  Resources for Developers
http://microsoft.com/msdn

## Slide 51
Required Slide
Complete an evaluation on CommNet and enter to win!

## Slide 52: MS Tag
Scan the Tag
to evaluate this
session now on
myTechEd Mobile

## Slide 53
© 2012 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.