## Slide 1: Microsoft Lync 2010: High Availability and Resiliency
Mahendra Sekaran
Principal Group Program Manager
Microsoft
EXL320

## Slide 2: Voice Customer Momentum
ChungHwa Telecom

## Slide 3: Session Objectives and Takeaways
Session Objectives:
  Resiliency Architecture
  Branch Office Resiliency
  Data Center Resiliency
Takeaways:
  Microsoft LyncTM Server 2010 Architecture provides High Availability for Voice
  Survivable Branch Appliances built by UC partners deliver Voice High Availability for branch users
  Voice Data Center Resiliency delivers Voice High Availability across geo-dispersed datacenters
  Metropolitan Data Center Resiliency delivers High Availability for all UC modalities across datacenters separated by high bandwidth & low latency
  Backup and restore procedures allow for expedient service restoration

## Slide 4: Agenda
High Availability & Resiliency Architecture
Branch Office Resiliency
Data Center Voice Resiliency
Metropolitan Data Center Resiliency

## Slide 5: Agenda
High Availability & Resiliency Architecture
Branch Office Resiliency
Data Center Voice Resiliency
Metropolitan Data Center Resiliency

## Slide 6: Design changes to support Voice high availability
Registrar Component
  Registration and Routing
  Each registrar has its SQLExpress DB
User Services Component
  Presence & Conferencing
Registrar and User Services are collocated in same physical Front End in the DC
All user end points register with same registrar
Users are load balanced by Registrars using a Distributed Hash Algorithm
Registrar can be installed in remote locations
Lync Clients
User Services Component
(Presence & Conferencing)
User’s Desktop
Registrar Component
Registration & Routing

## Slide 7: Resiliency Architecture
Each user has a “Primary Registrar Pool”.
  Discovers through DNS SRV. Directed to “Primary & Backup Registrar Pool”
  For Data Center User = Data Center
  For Branch User = Survivable Branch Appliance (SBA)
Branch Users always register with the SBA Registrar unless it is unavailable
Each Registrar Pool can have a “Backup Registrar Pool”
  Backup Registrar Pool = Data Center CS Pool
Backup Registrar heart-beats Primary Registrar.
  If heart-beat not received, Backup starts accepting client registrations
  Configurable Failover Interval (default = 120 sec for branch offices)

## Slide 8: Resiliency Architecture
Backup
Registrar
Pool
Bob’s Primary Registrar & User Services: EE Pool 1
Data Center - EE Pool 1
Presence
Conferencing
Registrar
(Registration
& Routing)
AD & DNS
Alice’s Primary Registrar & User Services: EE Pool 2
Data Center - EE Pool 2
Presence
Conferencing
Registrar
(Registration
& Routing)
AD & DNS
Registrar
Survivable Branch Appliance
Branch Office
Joe’s Primary Registrar: SBA
User Services: EE Pool 1

## Slide 9: Other Resiliency enhancements
DNS Based Load Balancing for Internal Pools
  All traffic can be DNS Load Balanced except Client –> Server HTTP
  Still require Hardware Load Balancer (HLB) for this traffic – Windows Network Load Balancing (NLB) not supported for production
Draining: Ability to drain a “server” before taking the server down
Session Dialog Resiliency for Conferencing
  Even if the Front End goes down, User can still participate in a conference
Client caches successful connections to Lync Server 2010
  FQDN and IP of SIP Registrar, Media Relay & Media Relay Authentication Server
  Reconnections are very fast

## Slide 10: Agenda
High Availability & Resiliency Architecture
Branch Office Resiliency
Data Center Voice Resiliency
Metropolitan Data Center Resiliency

## Slide 11: Branch Resiliency Options
Users
Large Branch (>1000 users)
Medium Branch - (25-1000 users)
25
500
1000
Small Branch (<25 users)
No Local Infrastructure
or gateway only
Survivable Branch Server or Standard Edition Server and Separate Media Gateway
Survivable Branch Appliance(s)
SBA
Data Center
AD & DNS
Circuit
Packet
PSTN
WAN

## Slide 12: Survivable Branch Appliance (SBA) Purpose-built appliance optimized to provide resilient multi-modal communication for maximizing branch office user productivity
Data Center
Lync Server Pool
Edge
Server
SBA
Branch Office
PSTN
WAN

## Slide 13: Survivable Branch Appliance (SBA)
Components | Functionality | Go-To Market
Windows Server® 2008 R2 Mediation Server Registrar PSTN Gateway | SIP Registrar Normal/Failover mode SIP Proxy & Routing engine PSTN connectivity Voicemail routing PSTN re-routing Centrally provisioned Up to 1000 user support | OEM (Embedded channel) Some partners: Audiocodes Dialogic Ferrari HP NET
Voice high availability for branch offices
Appliance form factor with Hardened Windows Server 2008 R2
Sold and supported by UC partners
Centrally Managed from the Datacenter

## Slide 14: SBA - Partner Solutions
Audiocodes | Mediant 1000 –1U, 4E1/T1, redundant power supply, MSBG-Firewall, Routing engine Mediant 2000 – 1U, redundant power supply
 | DMG 4000, 1U, 4 E1/T1, Redundant power supply
Ferrari | 1U, 4 E1/T1, Redundant Power supply
HP | SBA Module running on Procurve 54xx switch Chassis. Redundant Power supply, 8 E1/T1, Layer 2 functionality
 | UX Series. 1U, 8 E1/T1, Redundant power supply. MSBG-Firewall, Routing engine
Audiocodes: Existing M1k and M2k gateways can be converted to SBA
Dialogic: Existing DMG4000 Hybrid can be converted to SBA
NET: New HW to support SBA. Migration plan for customers wanting to move to UX platform.
Ferrari: Existing R2 Hybrid gateway can be converted into SBA
HP: Customers using ProCurve switches can convert it into a SBA by buying the module
Dialogic
NET

## Slide 15: SBA - Deployment Simple, Easy, Repeatable
Technician connects to WEB based GUI, IP Configuration.
SBA Drop Shipped to Branch with Software installed
Join to Domain &
complete SW configuration.
Start CS services. Finish GW Config and test PSTN Connectivity with temp user account.
Active Directory Computer
Add SBA to the Topology.
Move Users
to the SBA.
Enable CS Replication.
SBA downloads topology & configuration.
Request & Assign Certs.
Lync Admin (Data Center)

## Slide 16: SBA - Central Management Centralizing Move, Add, Changes
Branch Office(s)
SBA receives & processes replication
Change Normalization Rules
Change Routing Rules
Change User Policies
Lync Central Management Server
Store Configuration
Replicate to SBA
Lync Admin (Data Center)
Replicated
to the SBA

## Slide 17: SBA - Support and Service
SBA supported and serviced by the SBA partner
Windows Server Updates
  SBA partner can act as the gatekeeper OR
  Customers can deploy updates
Microsoft Lync Server 2010 updates
  SBA partner will test and release product notice on whether a particular update can be applied on the SBA
Original equipment manufacturer (OEM) notified about impending CS Update
OEM Downloads and tests the update
Compatibility issues
Partner addresses the issue if any
Partner notifies the customer on update compatibility
X-5 Biz Days
Date X
MSFT Update
X+30 Days

## Slide 18: SBA - User Experience
Features Available with WAN Down
PSTN Inbound and Outbound calls
Intra-Site calls, Inter site calls (PSTN Rerouting)
Hold, Retrieve, Transfer
Authentication, Authorization
Voicemail Deposit (Redirect to ExUM in Data Center)
Voicemail Retrieve (through PSTN)
Call Forwarding, SimulRing, Boss-Admin, Team-call
Call Detail Records (CDR)
All 2 Party Intra Site communications
Audio Conferencing through PSTN
Contact Search
Features Unavailable
Inter-site Data (IM, App Sharing, etc.)
Conferencing (IM, Video and Web)
Presence & DND based routing
Modify Presence or Change Call Forwarding Settings
Contact List
Response Group and Call Park
WAN Up
All Features Available
WAN Down
Basic Voice Features Available
Resilient Lync clients: Lync, Lync Attendant Console, Lync Phone Edition

## Slide 19: SBA – Lync Server 2010 Discovery
Data Center
Lync Server Enterprise Edition Pool
Lync Server Director
Branch Office
SBA
Bob
Active Directory Domain Services
Domain Name Server
2. TLS to Director Pool. SIP Register
1. DNS SRV Query
3. https;//PoolFQDN/CertSvc
5. SIP Register
4. Certificate Replication
6. SIP-TLS* Register
200 OK
(Cert Auth)
Client caches SBA FQDN**
And IP Address
Response: (Multiple) Director Pool FQDN
Response: 401 Redirect to Cert Provisioning
Response: 301 Redirect
Primary: SBA FQDN, Backup: EE Pool FQDN
IIS - IWA Auth
Get Certificate

## Slide 20: Branch Client Registration Scenarios
SBA Down
Users register w/Backup registrar in the datacenter
WAN Down
Branch user: No change
External: Register to pool
Normal Mode
User Registers with SBA
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN
SBA
Data Center
Edge
Server
PSTN
WAN
SBA
Data Center
Edge
Server
PSTN
WAN
Lync Server Pool
Lync Server Pool

## Slide 21: Branch Office: Server Connectivity when WAN down
WAN
Branch Office
SBA
TLS to cached FQDN and IP
SIP Register
(Cert Auth)
200 OK
Data Center
Lync Server Enterprise Edition Pool
Lync Server Director
Active Directory Domain Services
Domain Name Server
Bob

## Slide 22: Branch Client Media and Signaling Paths WAN Available
Media
Signaling
Intra-Branch
Signaling/media don’t traverse WAN
SBA routes the call between the users
SBA
Data Center
Lync Server
Pool
Edge
Server
PSTN
WAN
Branch PSTN Calls
SBA sends call to the PSTN
No WAN involved
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN

## Slide 23: Branch Client Media and Signaling Paths WAN Available
Inter-Branch / HQ Calls
Signaling/media traverse WAN
SBA routes the call to the other pool
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN
Media
Signaling
Branch User through Edge
Call Routing through SBA
WAN used for Signaling, not Media
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN

## Slide 24: Branch Client Media and Signaling Paths Key Failure Scenarios: WAN Down
Media
Signaling
Intra-Branch Calls
Two-party voice/video/IM/App Sharing
Audio Conferencing through PSTN
No Presence or Video Conferencing
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN
Inter-Branch/HQ Calls
SBA Initiates PSTN Rerouting
Media is over PSTN (Voice Only)
SBA
Data Center
Lync Server Pool
Edge
Server
PSTN
WAN

## Slide 25: Branch Client Media and Signaling Paths Key Failure Scenarios: Edge User & SBA Down
Media
Signaling
SBA Down
Clients register w/Backup Registrar in DC
Functionality driven by pool over WAN No functionality loss
SBA
Data Center
Lync Server pool
Edge
Server
PSTN
WAN
External Branch User
Remote user has full functionality (excepting inbound PSTN) through data center pool
SBA
Data Center
Lync Server pool
Edge
Server
PSTN
WAN

## Slide 26: Agenda
High Availability & Resiliency Architecture
Branch Office Resiliency
Data Center Voice Resiliency
Metropolitan Data Center Resiliency

## Slide 27: Data Center Voice Resiliency Failover to Backup Data Center
Lync Server pools operate as separate systems.
Client DNS SRV request discovers one or multiple Lync Server Pools. That Lync Server Pool directs client to primary and backup SIP registrar.
Client connects to Backup if connecting to Primary Registrar Pool fails.
  Limited feature set available on failover.
  Enable/Disable automatic failover, configurable failover interval.
  Automatic Failback, configurable failback interval.
If Primary Data Center cannot be restored:
  Restore Central Management Server in backup datacenter.
  Restore other services including Presence, Conferencing by “moving” users to other Pool.

## Slide 28: Data Center Voice Resiliency Failover to Backup Data Center (Discovery)
Berlin Data Center
Lync Server
Pool One
Edge
Server
Lync Server Director
AD DS & DNS
Client DNS SRV request. Example: DNS SRV for _sipinternaltls._tcp.contoso.com
DNS SRV Response includes:
  Lync Director Pool.contoso.com:5061, Priority=0, Weight=10,
  LSPool2.contoso.com:5061, Priority=1 , Weight=10
Client connects via TLS to Lync Server Director Pool. Sends SIP Register. Authenticates.
Lync Server Director Pool redirects client. SIP 301 includes Primary & Backup Registrar pool
If Primary Registrar Pool is available, client connects and registers with it
If unavailable, client connects and registers with Backup Registrar Pool (Lync Pool 2)
(1)
(2)
(3)
(4)
(5)
Singapore Data Center
Lync Server Pool Two
Edge
Server
Backup
Registrar
WAN
(6)

## Slide 29: Data Center Voice Resiliency Failover to Backup Data Center
Features Available to Users In Case of Data Center Disaster
PSTN Inbound calls (carrier provided)
PSTN Outbound calls
Intra-Site calls and Inter site calls
Hold, Retrieve, Transfer
Authentication, Authorization
2 Party Intra Site Instant Messaging (IM) and Audio/Video (A/V)
Call Detail Records (CDR)
Call Forwarding, Simultaneous Ringing, Delegation, Team-call
Join conferences scheduled by users homed on other pool
Features Unavailable
Conferencing Auto Attendant (AA) (through PSTN)
Schedule IM, A/V & Web Conferences
Presence and Do Not Disturb (DND) based routing
Updating Call Forwarding settings
Response Group Service & Call Park
Voicemail Deposit (Redirect to Exchange UM in the DC)
Voicemail Retrieve (through PSTN)
Failover
WAN
Backup
Registrar
Berlin Data Center
Lync Server Pool
Edge
Server
Singapore Data Center
Lync Server Pool
Edge
Server
WAN

## Slide 30: Agenda
High Availability & Resiliency Architecture
Branch Office Resiliency
Data Center Voice Resiliency
Metropolitan Data Center Resiliency

## Slide 31: Metro Data Center Resiliency Lync 2010 Pool Extended Across Two Data Centers
FE 1-2
FE 3-4
NY Data Center
NJ Data Center
Active
SQL
Passive SQL
Features Available Depending on Exchange UM Deployment
Voicemail Deposit
Voicemail Retrieve
Features Available to Users If One Data Center goes Down
PSTN Inbound calls
PSTN Outbound calls
Intra-Site calls and Inter site calls
Hold, Retrieve, Transfer
Authentication, Authorization
2 Party Intra Site IM and A/V
Call Detail Records (CDR)
Call Forwarding, SimulRing Boss-Admin, Team-call
Voice Apps (CAA, Response Group, Call Park)
Conferencing (IM, A/V and Web)
Presence and DND based routing
Updating Call Forwarding settings
Low latency WAN
Lync server pools operate as one logical system
  Split Front End pool across two datacenters (all FEs active)
  SQL Geo cluster for backend (Stretched Virtual Local Area Network (VLAN))
  Data replication is done by storage arrays (Ex: EMC SRDF, HP CLX EVA)
  Requires low latency WAN (20 milliseconds)
In one site is down, clients are serviced by FEs in other site
Nearly all features available
  PSTN termination may affect inbound calls
Edge
Server
Edge
Server
http://technet.microsoft.com/en-us/library/gg670905.aspx

## Slide 32: Backup and Restore
The Backup and Restore document covers the following:
  Strategy and best practices to help in planning and prepping for backup and restore – that fit individual customer needs.
  Backing up all relevant Server Roles, Lync Databases and data stores (core data and settings, Arch/Mon databases, File stores)
  Restoring Lync servers based on server and failure types.
    Restoring Lync Servers (standard and enterprise), Central Management Store, Backend, RGS settings,
    Procedures when backend fails, when entire pool fails
Coming Soon!

## Slide 33: Lync 2010 – Expect the Best
“Microsoft Lync Server 2010 passed an aggressive SIP Load Torture Test without dropping any calls or reporting errors in the 4,000,000 call attrition test. This sustained operation without error is the best we have seen to date for any Unified Communications / IP PBX product we have tested.”
Miercom (January 2011)

## Slide 34: Session Objectives and Takeaways
Session Objectives:
  Resiliency Architecture
  Branch Office Resiliency
  Data Center Resiliency
Takeaways:
  Lync Server 2010 Architecture provides High Availability for Voice services
  Survivable Branch Appliances built by UC partners deliver Voice High Availability for branch users
  Voice Data Center Resiliency delivers Voice High Availability across geo-dispersed datacenters
  Backup and restore procedures allow for expedient service restoration

## Slide 35: Lync Breakout Sessions
Monday | 4:30PM | EXL201 | Microsoft Lync 2010: Winning in Voice and Video | Kirk Gregersen
 | 3:00PM | EXL316 | Microsoft Lync 2010: In the Cloud | Ziv Fass
Tuesday | 8:30AM | EXL303 | Four Ways to Leverage the Microsoft Lync 2010 Client API's in Your Applications | Albert & Marcello
 | 3:15PM | EXL319 | Microsoft Lync 2010: Setup, Deployment, Upgrade, and Coexistence Scenarios | Peter Schmatz
Wednesday | 8:30 AM | EXL402 | Microsoft Lync's Unified Communications Managed API - Writing Advanced SIP Applications | Albert & Stephane
 | 10:15 AM | EXL318 | Monitoring Microsoft Lync 2010 Deployments | Jeff & Arish
 | 1:00 PM | EXL320 | Microsoft Lync 2010: High Availability and Resiliency | Mahendra Sekaran
 | 5:00 PM | EXL323 | Setting Up and Deploying Microsoft Lync Server 2010 Edge Servers | Rui Maximo
Thursday | 8:30 AM | EXL325 | Troubleshooting Microsoft Lync Server 2010 | Cameron & Tim
 | 8:30 AM | EXL314 | Microsoft Lync 2010 and the Enterprise Network | Arish Alreja
 | 10:15 AM | EXL321 | Microsoft Lync Server 2010: Administering Lync Server Deployment | Anand & Cezar
 | 1:00 PM | EXL315 | Microsoft Lync 2010: Core Voice Planning and Deployment | Roy Kuntz
 | 2:45 PM | EXL301 | Microsoft Lync 2010: Audio, Video, and Web Conferencing Architecture and Experience | Cameron Parker
 | 4:30 PM | EXL317 | Microsoft Lync 2010 Interoperability, Integration with Competition or Legacy | Francois Doremieux

## Slide 36: Resources
www.microsoft.com/teched
  Sessions On-Demand & Community
  Microsoft Certification & Training Resources
  Resources for IT Professionals
  Resources for Developers
www.microsoft.com/learning
http://microsoft.com/technet
http://microsoft.com/msdn
Learning
http://northamerica.msteched.com
  Connect. Share. Discuss.

## Slide 37
Complete an evaluation on CommNet and enter to win!

## Slide 39
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.