## Slide 1: RemoteFX Hardware Selection and Deployment Considerations for VDI and Sessions
Eric Han
Senior Program Manager
Microsoft
WSV201

## Slide 2: Agenda
Why RemoteFX and Demo
Architecture of Server and Client with Diagrams
Capacity Planning and Graphs
Deployment Considerations and Hardware
RemoteFX Partners

## Slide 3: Why RemoteFX VDI
IT: Control and Compliance
Applications: Knowledge Workers with Multimedia
Employees: Access to Applications
“We’ve been really impressed with the RemoteFX feature in Windows Server 2008 R2 SP1. The reduction in power consumption and the rich graphical user experience are both significant advantages. We now use VDI for more than 75 percent of our work force worldwide. With Windows Server 2008 R2 SP1, our employees get a rich graphical user experience, better phone quality, and USB remote access within the VDI session.“
Alan Bourassa Chief Information Officer, EmpireCLS Worldwide Chauffeured Services
http://www.computerworld.com/s/article/9215316/BP_employee_loses_laptop_containing_data_on_13_000_oil_spill_claimants
Multimedia and 3D:
Google Earth
Flash
PowerPoint
Silverlight
Skype
Visual Studio 10
Windows Media Player
Windows Presentation Format
Windows Desktop (DWM)
We save 70 to 80 hours each month by delivering classes remotely using RemoteFX in Windows Server 2008 R2 Service Pack 1. At our consultant billing rate of $250 an hour, that’s more than $200,000 a year.
Rand Morimoto
President, Convergent Computing

## Slide 4: RemoteFX Enabled Client
demo
Hector Angulo
Product Manager, Wyse Zero
Wyse Technology

## Slide 5: Agenda
Why RemoteFX and Demo
Architecture of Server and Client with Diagrams
Capacity Planning and Graphs
Deployment Considerations and Hardware
RemoteFX Partners

## Slide 6: Architecture for Server Remoting
Hyper-V`
WDDM Driver
Platform Integration with Hyper-V components
Hardware GPU
RDVGM
Render
Capture
Encode
Host
VM Management components
Virtual Machine
WDDM
U-Mode vGPU
K-Mode vGPU
RDP 7.1

## Slide 7: Summary of Server and VM Operations
Application calls standard libraries within the VM
The virtual GPU is a 3D graphics driver in the VM, integrated with Hyper-V. Driver presents the industry’s first WDDM driver in a VM
The management components manage shared resources and control the lifetime of the RDVGM processes
  Consumed amount of VRAM is a function of VM’s monitors and resolutions
  System Memory and VRAM consumption documented in whitepaper
The RDVGM operates on behalf of the VM within the host:
  Render – draw, flip, rotate, etc. Supporting behavior of DirectX applications in a VM
  Capture – capture frames, difference for changes, and throttle based on admin control and client backpressure. Capture rate controllable by Group Policy
  Encode – encode in GPU /CPU. Encode level controllable by Group Policy
Encoded data then transferred to each VM. A RemoteFX module in the VM (not drawn) sends to the client

## Slide 8: Client Architecture – Decoding RemoteFX
Decode RemoteFX
RemoteFX
Decode Abstraction Layer
CPU
HW Decoder
CPU/ GPU
Aero UX Thin Client
Bitmap
Core Services
Networking/
Security
Virtual Channels
Devices
Bulk Decompress
Key/Mouse
RDP 7.1

## Slide 9: IT Monitoring and Control
demo and video

## Slide 10: Agenda
Why RemoteFX and Demo
Architecture of Server and Client with Diagrams
Capacity Planning and Graphs
Deployment Considerations and Hardware
RemoteFX Partners

## Slide 11: Capacity Planning Overview
What we did in testing
  Added multimedia criteria and content
  Constrained some variables
  Ran benchmark and measured
Caveats
  Data is based on benchmark
  Recommend piloting
“Knowledge Worker with Multimedia Scenario”
  Word
  Outlook
  PowerPoint
  WMV
  Flash
  …

## Slide 12: Capacity Planning and Performance
Scalability measures performance as we add users
RemoteFX reserves resources to help ensure performance
  System Memory – below includes Hyper-V formula for a 2GB VM
  Video Memory – below value is constant
System Memory Reservation (Server) Values are for 2GB Virtual Machine |  |  |  | 
Resolution Maximum | Monitor | Monitors | Monitors | 4 Monitors
1024x768 | 72 MB | 85 MB | 99 MB | 112 MB
1280x1024 | 108 MB | 145 MB | 183 MB | 220 MB
1600x1200 | 166 MB | 247 MB |  | 
1920x1200 | 183 MB | 278 MB |  | 
Video Memory Reservation (Server GPUs) Values consistent for any Virtual Machine |  |  |  | 
Resolution Maximum | Monitor | Monitors | Monitors | 4 Monitors
1024x768 | 75 MB | 105 MB | 135 MB | 165 MB
1280x1024 | 125 MB | 175 MB | 225 MB | 275 MB
1600x1200 | 184 MB | 257 MB | NA | NA
1900x1200 | 220 MB | 308 MB | NA | NA
*above is reservation on host, separate from dynamic versus static memory.

## Slide 13: Capacity Planning Measurement
Add users and measure criteria
  User Experience
  Resources
Example: CPU Utilization
Example: Network Utilization
Frame Rate and Jitter (Introduced with RemoteFX)
Input Response Time (Common to RDVH)

## Slide 14: Capacity Planning for Comparability
Results applicable anywhere
Variables in test
  Virtual Machine Settings
  RemoteFX Settings
Row | Virtual Machine Configuration |  |  |  | RemoteFX Server Settings | 
 | Vproc # / System Memory | Static or Dynamic Memory | Arch | Monitor Resolution | Capture Frame Rate | Image Quality
A | 1-4 / 1024 | Static | 32-bit | 1280x1024 | Default | Default
B | 1-4 / 2048 | Static | 64-bit | 1280x1024 | Default | Default
C | 2 / 2048, 3072, 4096 | Dynamic | 64-bit | 1280x1024 | Default | Default
D | 2 / 2048 | Dynamic | 64-bit | 1024 x 768 1280 x 1024 1600 x 1200 1920 x 1200 | Default | Default
E | 2 /2048 | Dynamic | 64-bit | 1280x1024 | High | Medium
 |  |  |  |  | Medium (Default) | Medium (Default)
 |  |  |  |  | Low | Medium
F | 2 /2048 | Dynamic | 64-bit | 1280x1024 | High | Low
 |  |  |  |  | Medium (Default) | Medium (Default)
 |  |  |  |  | Low | High

## Slide 15
Virtual Processors
OS Architecture
Dynamic and Static Memory
Capture Frame Rate Setting
Image Quality Setting
More in upcoming June whitepaper
Capacity Planning Recommendation Next slides provide key takeaways

## Slide 16
Recommendation based on results
  Dual Processor
  64-bit OS Virtual Machines
CPU Utilization
Users (4 – 32)
Users (4 – 32)
Frame Rate
64-bit
32-bit
Capacity Planning Recommendation Virtual Processor and OS

## Slide 17
Dynamic and Static Memory near equal Frame Rates and Resource Utilization
CPU Utilization
Users (4 – 32)
Users (4 – 32)
Frame Rate
Capacity planning recommendation Dynamic and static memory

## Slide 18
Recommendation based on results [here]
  Frame rate 39 FPS versus 32 FPS at four VMs
  CPU Utilization comparable
CPU Utiliz.
Users (4 – 32)
Users (4 – 32)
Frame Rate
39 FPS
High Capture
32 FPS
Low Capture
37 FPS
Med. Capture
Capacity Planning Recommendation Capture frame rate

## Slide 19
Capacity Planning Recommendation Maximize experience, balanced, minimize resource use
 | RemoteFX Server Settings |  | Purpose of this configuration
Label | Capture Frame Rate | Image Quality | 
Experience | High | High | Maximize user experience.
Default | Medium (Default) | Medium (Default) | Baseline configuration to facilitate comparisons.
Resource | Low | Low | Minimize server resource consumption.

## Slide 20
Frame rate mirrors Capacity test
Image Quality Setting varies, changing network load
Capacity Planning Recommendation Maximize experience, balanced, minimize resource use
39 FPS
Experience
32 FPS
Resource
37 FPS
Default
Users (4 – 32)
Frame Rate
Network (Mbps)
Users (4 – 32)
88 Mbps
32 users
46 Mbps
32 users
64 Mbps
32 users
Low Image
High Image

## Slide 21: Agenda
Why RemoteFX and Demo
Architecture of Server and Client with Diagrams
Capacity Planning and Graphs
Deployment Considerations and Hardware
RemoteFX Partners

## Slide 22: Deployment Considerations
Frame Rate
Server Requirements in Hardware Requirements
GPUs with RemoteFX Logo Additional Qualification in Server Catalog
Hardware Considerations
SLAT CPU
GPU AQ
BMC Video

## Slide 23
HP Proliant RemoteFX Hardware
HP ProLiant DL/ML370 G6 Server
HP ProLiant WS460c G6 Workstation Blade with WS460c Graphics Expansion Blade

## Slide 24
Dell PowerEdge Servers and Appliances RemoteFX Hardware
Dell PowerEdge R710 and M610x
Dell PowerEdge C410x
Nvidia M2070Q and AMD v7800

## Slide 25
IBM iDataPlex dx360 M3 RemoteFX Hardware
IBM iDataPlex
Nvidia M2070Q

## Slide 26: RemoteFX Partners
Please visit these partners at the
Microsoft RemoteFX Partner Pavilion here at TechEd:

## Slide 27: Related Content
Required Slide
Speakers, please list the Breakout Sessions, Interactive Discussions, Labs, Demo Stations and Certification Exam that relate to your session. Also indicate when they can find you staffing in the TLC.
Breakout Sessions (RemoteFX GPU Virtualization – Deep Dive: VIR313)
Capacity Planning Whitepaper (Watch the team blog: http://blogs.msdn.com/b/rds)
Case Studies (search for ‘RemoteFX’ www.microsoft.com/casestudies)
Server Architecture and Offerings
  Dell: http://content.dell.com/us/en/enterprise/d/shared-content~solutions~en/Documents~solution-brief-microsoft-remote.pdf.aspx
  IBM: http://www.ibm.com/common/ssi/cgi-bin/ssialias?infotype=PM&subtype=SP&appname=STGE_XS_XG_USEN&htmlfid=XSS03076USEN &attachment=XSS03076USEN.PDF (just published)
  HP: http://h20000.www2.hp.com/bc/docs/support/SupportManual/c02478570/c02478570.pdf and www.hp.com/go/cv
GPU Offerings and Drivers
  AMD: http://www.amd.com/us/products/workstation/graphics/software/Pages/remote-fx.aspx
  Nvidia: http://blogs.nvidia.com/2011/02/it’s-here—nvidia-quadro-driving-virtual-desktops-with-microsoft-remotefx

## Slide 28: Summary
Thank You, Eric Han
Find Me Later At… RemoteFX Partner Pavilion
Why RemoteFX and Demo | 
Architecture of Server and Client with Diagrams | 
Capacity Planning and Graphs | 
Deployment and Hardware Pictures | 
RemoteFX Partners | 
Case Studies and Demo with Wyse Zero Client
Architecture for Server Remoting and Client
Overview of Operations (provided as a Handout)
Testing Approach
Recommendation based on Testing
Upcoming Whitepaper in June
Ecosystem Investments to Make Your Selection Easier
Servers Offerings and Reference Guides from Partners
Industry Leading Partners for Server, Client, WAN Acceleration, Thin Clients, Decoders

## Slide 29: Track Resources
Don’t forget to visit the Cloud Power area within the TLC (Blue Section) to see product demos and speak with experts about the Server & Cloud Platform solutions that help drive your business forward.
You can also find the latest information about our products at the following links:
Windows Azure - http://www.microsoft.com/windowsazure/
Microsoft System Center - http://www.microsoft.com/systemcenter/
Microsoft Forefront - http://www.microsoft.com/forefront/
Windows Server - http://www.microsoft.com/windowsserver/
Cloud Power - http://www.microsoft.com/cloud/
Private Cloud - http://www.microsoft.com/privatecloud/

## Slide 30: Resources
www.microsoft.com/teched
  Sessions On-Demand & Community
  Microsoft Certification & Training Resources
  Resources for IT Professionals
  Resources for Developers
www.microsoft.com/learning
http://microsoft.com/technet
http://microsoft.com/msdn
Learning
http://northamerica.msteched.com
  Connect. Share. Discuss.

## Slide 31
Complete an evaluation on CommNet and enter to win!

## Slide 33
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.