## Slide 1
SAC-433T
Network acceleration and other NIC technologies for the data center
Don Stanwyck, Senior Program Manager
Michael Nanakul, Senior Test Lead

## Slide 2: What’s this session about?
WHO WILL BENEFIT FROM THIS TALK
Hardware vendors planning support for Windows Server 8
OEMs planning to source networking equipment for systems running Windows Server 8
Anyone needing to learn about the latest advances in networking support for Windows Server 8

## Slide 3: What’s this session about?
TOPICS
What new networking enhancements are in the Windows 8 networking stack?
How does Windows Server 8 use the latest hardware acceleration and task offloads to enhance the customer experience?
What should NICs support to best meet customer needs with Windows Server 8?

## Slide 4: What’s this session about?
WHAT YOU’LL LEAVE WITH
A broad overview of the new networking capabilities supported in Windows Server 8 – and how they work for customers
Enough acronyms to make you sound like a networking expert at your next cocktail party discussion

## Slide 5
Performance
What customers want in the cloud
Reliability
Cost

## Slide 6: Hardware offloads make cloud performance possible

## Slide 7: The network stack optimizes specific scenarios.

## Slide 8: Improved network performance and reliability greater workload densities lower operational costs

## Slide 9: Roadmap for this session
Fabric convergence in the cloud
  Datacenter bridging (DCB)
  Remote direct memory access (RDMA)
  Datacenter TCP (DCTCP)
Operations Reliability
  Consistent Device Naming (CDN)
  NIC Teaming (LBFO)
Flexible, secure clouds
  Generic Routing Encapsulation (GRE)
  IPsec Task Offload v2 (IPsecTOv2) for VMs
High Performance Networking Offloads
  Receive Side Scaling (RSS) extensions
  Receive Segment Coalescing (RSC)
  Dynamic Virtual Memory Queues (VMQ)
  Single-Root I/O Virtualization (SR-IOV)

## Slide 10
Fabric convergence in the cloud
reducing costs of storage and infrastructure

## Slide 11: Bottlenecks in the converged fabric cloud
In the host stack
In the host NIC
In the network

## Slide 12: Convergence in the cloud
QoS, Bandwidth management
Congestion avoidance leading to full pipes with small buffers
DCB
DCTCP
Fast data transfer for storage and high-performance applications
Network Direct / kernel-mode RDMA / SMB2-Direct

## Slide 13: Traffic congestion
Stop and go
or smooth flow?

## Slide 14
Windows 8 addresses congestion in the network by reacting to degree of congestion, not presence of congestion
Goal: Low latency, high burst tolerance, and high throughput, with shallow buffered switches
Requires ECN (RFC 3168) capable switches
Datacenter TCP (DCTCP)

## Slide 15: DCTCP Needs Less Buffer Memory than TCP
1 Gbps flow controlled by TCP
  Requires 400 to 600 KB of memory
  TCP sawtooth visible
1 Gbps flow controlled by DCTCP
  Requires 30KB of memory
  Smooth

## Slide 16: Assigned lanes to avoid local adapter and switch congestion

## Slide 17
Addresses congestion in the network adapter and the network by reserving bandwidth for particular traffic types
Windows 8 provides support and control for DCB, tags packets by traffic type
Provides lossless transport for mission critical workloads
Requires:
  Enhanced Transmission Selection (IEEE 802.1Qaz)
  Priority Flow Control (IEEE 802.1Qbb)
  (Optional) Datacenter Bridging Exchange protocol
  (Not required) Congestion Notification (IEEE 802.1Qau)
Datacenter Bridging (DCB)

## Slide 18: “Beam me up, Scotty”
kRDMA

## Slide 19
Addresses congestion in the network stack by offloading the stack to the network adapter
Storage traffic seeks higher throughput with lower CPU utilization
SMB2-Direct uses new RDMA capability if the NICs present support RDMA
HPC’s Network Direct feature is now in Windows Server 8 for low latency, high speed application-to-application data transfer
Remote DMA (Network Direct, SMB2-Direct)
Session 446 – Designing Systems for Continuous Availability & Scalability
LEARN
MORE

## Slide 20: Remote DMA (Network Direct, SMB2-Direct)
Initial testing with SMB2-Direct saw
  CPU utilization drop by almost 2/3rds
  File access latency drop to approximate local storage
Demonstrated at the Server Keynote
  2 Gbytes/sec throughput
  <1% CPU utilization
  . . . . And we’re not done!

## Slide 21
Reliability is job 1

## Slide 22: Reliability
Predictable, consistent names for NICs
CDN
Bandwidth aggregation and NIC failure protection
NIC Teaming

## Slide 23: Meaningful names for Ethernet ports

## Slide 24: Consistent Device Naming (CDN)
BIOS supplied naming consistently identifies NICs with names, numbers - Names can be printed on the chassis!
Most major OEMs have signed up to ship their machines with CDN-compliant BIOS
Microsoft’s implementation of PCI-SIG Engineering Change Notice (ECN)
  http://www.pcisig.com/specifications/pciexpress/specifications/ECR_Slot_Naming-10.pdf.
NIC Vendors – if your driver uses a virtual bus driver you need to talk to us!

## Slide 25: NIC Teaming (LBFO)
Customers are tired of administering different teaming solutions that often don’t work well with their Windows Server features.

## Slide 26: NIC Teaming (LBFO)
Many NIC vendors are tired of spending resources engineering and supporting a teaming solution that doesn’t show an income stream.

## Slide 27: NIC Teaming (LBFO)
The most popular feature in the data center just got better!
  Microsoft supported, inbox, vendor agnostic teaming
Managed through PowerShell or an on-box UI
  Support multiple servers from a single interface

## Slide 28: NIC Teaming configurations
NIC Teaming
TCP/IP
Stack
TCP/IP Stack
NIC Teaming
Hyper-V
Switch
VM
VM
VM
Up to 32 NICs
Unlimited virtual interfaces
Multiple teaming modes
Local/Remote management through PowerShell or UI

## Slide 29: NIC Teaming
demo

## Slide 30
Clouds must be flexible and secure

## Slide 31: Flexible, secure cloud
Isolation of private networks
Better security with reduced VM CPU use
GRE
IPsecTOv2 for VMs

## Slide 32: Separating hosted clients through virtualization
Physical
network
Physical
server
Blue VM
Red VM
Blue network
Red network
Virtualization

## Slide 33: Generic Routing Encapsulation (GRE)
Multi-tenant environments need to hide the tenant’s own multi-premise networking from the datacenter’s networking.
GRE (RFCs 2784 & 2890) provides the mechanism to tunnel tenant networks over the datacenter network
Without NIC participation GRE breaks today’s task offloads
NIC vendors should support GRE offload if they want to be used in cloud hosting scenarios
Session 442 - Building Secure, Scalable Multi-Tenant Clouds Using Network Virtualization
LEARN
MORE

## Slide 34: IPsec Task Offload v2 (IPsecTOv2) for VMs
Compliance (SOX, HIPPA, etc.)
IPsec is a required security protocol in many networks
IPsec is a CPU intensive workload
IPsecTOv2 was only available to native and host workloads in Windows Server 2008 R2
  Now extended to VMs
  Managed by the Hyper-V switch

## Slide 35
High-performance networking hosts create lower OP-EX clouds

## Slide 36: High-performance hosts
Direct data placement in VMs
SR-IOV
Reduced packet header processing
RSC
Interrupt spreading across
k-groups
RSS
Dynamic reassignment of queues
VMQ

## Slide 37: Single root I/O Virtualization (SR-IOV)
For virtual networking the Holy Grail is near-native-I/O
  reduces CPU, reduces latency, and increases network throughput
  Improved hardware usage = allows more VMs per host
VM network I/O bypasses the host, moved directly between the VM and NIC
Requires:
  Chipset:
    Interrupt and DMA remapping: VT-d2 or IOMMU
      Access Control Services (ACS) on PCIe root ports
      Alternative Routing-ID Interpretation (ARI)
  CPU: Hardware virtualization, EPT or NPT
Session 437 - A Deep Dive into Hyper-V Networking
LEARN
MORE

## Slide 38: Receive Segment Coalescing (RSC)
Coalesces packets in the NIC so the stack processes fewer headers
  Multiple packets belonging to connection that arrive within a single interrupt are coalesced to a larger packet (max of 64 K) by the NIC
10 – 30% improvement in I/O overhead

## Slide 39: Receive Side Scaling (RSS)
RSS has been helping servers scale for many years. Windows 8 takes RSS to the next generation of servers
Spreads interrupts across all available CPUs – even for those very large scale hosts
  RSS now works across k-groups
RSS now load balances UDP traffic across the CPUs

## Slide 40: Dynamic Virtual Machine Queues (VMQ)
VMQ is to virtualization what RSS is to native workloads
Dynamic VMQ reassigns available queues based on changing networking demands of the VMs

## Slide 41
Review

## Slide 42
Performance and reliability reduce costs

## Slide 43
New and improved hardware offloads and networking stack make Windows Server 8 the best OS for your datacenter or cloud

## Slide 44: Your next steps
Customers demand better network performance.
IHVs: Join us in making it happen. Make sure your NICs are delivering the features customers want.
OEMs: Set your sourcing requirements to ensure customers get the performance and scale to meet their needs

## Slide 45: For more information
RELATED SESSIONS
CONTACT: buildmultimedia@microsoft.com
Session SAC-429T
Session SAC-430T
Session SAC-437T
Session SAC-439T
Session SAC-442T
Contacts
General networking questions on these topics: ndis6fb@microsoft.com
Session SAC-559T
Session SAC-565T
Session HW-566T
Session SAC-593T
Session HW-667P

## Slide 46
Feedback and questions http://forums.dev.windows.com
Session feedback http://bldw.in/SessionFeedback
thank you

## Slide 47
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.